## Slide 1
F5 Certified Technology Specialist
BIG-IP LTM
Scenario-Based Certification Prep Course
Covering the F5-CTS BIG-IP LTM Beta Exam Series
F5CTSLTM1-B through F5CTSLTM6-B
With full mapping to the legacy 301A — BIG-IP LTM Specialist:
Architect, Setup and Deploy
Notes: WHAT THIS SLIDE TEACHES
Course title slide. Sets context: this course prepares students for the new F5-CTS BIG-IP LTM Beta certification series (six exams) while maintaining backward compatibility with the legacy 301A exam.

## Slide 2
2 © 2026 F5
What this course covers
A comprehensive, scenario-based training course for the F5-CTS BIG-IP LTM certification
Who is this for
F5 engineers preparing for F5-CTS BIG-IP LTM certification (Beta or legacy 301A). Network engineers expanding into application delivery. Anyone managing BIG-IP LTM in production who wants deeper expertise and an industry-recognized credential.
What you will learn
Deploy LTM applications end-to-end. Configure profiles, persistence, SSL, iRules, and monitors. Build HA clusters with DSC, traffic groups, and failsafe. Troubleshoot using logs, tcpdump, and AVR. Secure and optimize the BIG-IP platform. Pass all six Beta exams.
How we teach it
Scenario-based slides with real-world context. GUI walkthroughs and TMSH command coverage. Hands-on labs (11 modules, 5–6 hours total). Exam checkpoint questions after every lab. Full speaker notes for self-study. Gap-fill slides for objectives not covered in labs.
Course structure: 11 hands-on lab modules (slides + labs) + gap-fill slide block (8 objectives not covered in labs) + final review and exam prep. Each lab has an opener mapping Beta objectives, technical slides with GUI + TMSH, a lab exercise, and exam checkpoint questions with answers in speaker notes.
Notes: WHAT THIS SLIDE TEACHES
Course overview. Three columns: audience, learning outcomes, teaching methodology. Blue callout explains the structure.

## Slide 3
3 © 2026 F5
301A vs F5-CTS Beta exam series
The legacy 301A is being replaced by six focused exams — this course covers both
 | 301A (Legacy) | F5-CTS Beta Series (New)
Structure | ONE exam: 301A — BIG-IP LTM Specialist: Architect, Setup and Deploy | SIX exams: F5CTSLTM1-B through F5CTSLTM6-B. Take in any order.
Questions | 80 questions (70 scored + 10 pilot). 90 minutes. | Per-exam question count TBD (Beta). Each exam ~60 minutes.
Passing score | 245 out of 100–350 scaled score. | Beta scoring TBD. Standard F5 scaled scoring expected.
Objectives | 2 sections, ~20 objectives. Broad coverage in one sitting. | 6 exams, 47 objectives total. Deeper per-topic coverage.
Prerequisite | F5 Certified BIG-IP Administrator (F5-CA) | F5-CA, BIG-IP Certification (same prerequisite)
Credential | None standalone. Prereq for 301B. | F5 Certified Technology Specialist, BIG-IP LTM (F5-CTS, LTM)
New topics | — | FAST templates, expanded packet capture/troubleshooting, performance analysis (A/E), config optimization (A/E)
What changed from 301A to Beta?
The 301A covered architecture and deployment in one broad exam. The Beta splits this into six focused exams, adds dedicated packet capture/troubleshooting exams (Exams 5 and 6), expands HA and monitoring coverage (Exam 4), and introduces A/E (Analyze/Evaluate) level questions for config optimization and performance analysis. Students who passed the 301A will find ~70% familiar content and ~30% new depth.
Notes: WHAT THIS SLIDE TEACHES
Direct comparison of 301A and Beta exam series. Students coming from 301A prep need to understand the structural change and new content areas.
KEY POINTS:
- 301A was one 90-minute exam. Beta is six shorter exams taken in any order.
- Beta adds dedicated pcap exams (5-B and 6-B) that didn't exist as standalone in 301A.
- Beta adds A/E level questions for performance analysis and config optimization.
- Prerequisite is the same: F5-CA (BIG-IP Administrator).
- This course covers ALL shared objectives plus the new Beta-only objectives.

## Slide 4
4 © 2026 F5
Prerequisites and assumed knowledge
What you should already know before taking this course
Required: F5-CA (BIG-IP Administrator)
The F5-CA certification validates that you can:
• Navigate the BIG-IP GUI and TMSH CLI
• Create VLANs, self IPs, and routes
• Create basic virtual servers and pools
• Apply simple profiles (HTTP, TCP)
• Configure basic monitors
• Understand SNAT at a basic level
• Perform initial BIG-IP setup (licensing, provisioning, NTP, DNS)
• Save and load configurations
If you don't have your F5-CA, you must pass it before attempting the F5-CTS exams.
Assumed networking knowledge
This course assumes you understand:
• TCP/IP fundamentals (3-way handshake, ports, IP addressing, subnetting)
• DNS resolution process
• HTTP request/response model
• TLS/SSL handshake basics (certificates, cipher suites)
• VLANs, trunks, and Layer 2/3 switching
• Static and dynamic routing concepts
• Basic Linux CLI (ssh, grep, tail, cat)
• Syslog concepts and severity levels
We won't teach these topics — we'll use them to explain BIG-IP concepts.
Quick self-assessment — can you answer these?
1. What is the difference between a virtual server and a virtual address on the BIG-IP?
2. If a pool member fails its health monitor, what happens to traffic destined for that member?
3. What does SNAT do, and why might you need it?
4. Name three profiles you might assign to a virtual server and explain why.
If you can answer all four confidently, you're ready for this course. If not, review your F5-CA material first.
Notes: WHAT THIS SLIDE TEACHES
Prerequisites and assumed knowledge. Students must have F5-CA and solid networking fundamentals.
SELF-ASSESSMENT ANSWERS:
1. Virtual server = listener (IP:port) that accepts traffic. Virtual address = the IP address object. One virtual address can have multiple virtual servers (different ports).
2. Traffic is redistributed to remaining healthy members. The failed member is removed from LB rotation.
3. SNAT translates the client source IP to a BIG-IP IP. Needed when servers don't route responses through BIG-IP.
4. HTTP (L7 processing), TCP (connection optimization), Client-SSL (decrypt client traffic). Each adds functionality.

## Slide 5
5 © 2026 F5
Course agenda
Day-by-day schedule with time slots, slides, and durations
Day | Section | Slides | Duration
Day 1 — Wednesday | Old Dominion Room |  | 4 hrs
 | Course Housekeeping | 1–7 | 10m
 | Lab 1: Basic Setup, TMSH, SNATs | 8–18 | 70m
 | Lab 2: Profiles, iRules, Multi-tier | 19–30 | 70m
 | Lab 3: AVR and Analytics | 31–38 | 55m
 | Lab 4: Monitors — Concept Slides | 39–43 | 40m
Day 2 — Thursday | Old Dominion Room |  | 5.5 hrs
 | Lab 4: Hands-On + Checkpoints | 44–46 | 25m
 | Lab 5: SSL / TLS | 47–54 | 45m
 | Lab 6: VS + Packet Processing | 55–62 | 50m
 | Lab 7: Load Balancing / Lab 8: Networking | 63–77 | 60m
 | Lab 9: Roles and Partitions | 78–86 | 35m
 | Lab 10: DSC and HA | 87–96 | 55m
 | Lab 11 / Gap-Fill / Final Review | 97–124 | 60m
Notes: WHAT THIS SLIDE TEACHES
Full course agenda with Beta exam mapping and time estimates. Instructor can adjust pacing based on class level.
DELIVERY APPROACH:
- Each lab: 15-20 min slides + 30-45 min hands-on lab
- Gap-fill: slide presentation only (no lab exercises)
- Final review: instructor-led discussion with review questions
- Total: approximately 8.5 hours (can be delivered as 2-day course or self-paced)

## Slide 6
6 © 2026 F5
Lab environment
Two BIG-IP devices, one LAMP server, and a jumpbox
Device | Hostname | Management IP | Client VLAN | Server VLAN | Credentials
BIG-IP 1 | bigip01.f5demo.com | 10.1.1.245 | 10.1.10.245 | 10.1.20.245 | admin / admin.F5demo.com
BIG-IP 2 | bigip02.f5demo.com | 10.1.1.246 | 10.1.10.246 | 10.1.20.246 | admin / admin.F5demo.com
LAMP Server | lamp1 | 10.1.1.252 | — | 10.1.20.11–15 | root / default
Jumpbox | jumpbox | 10.1.1.6 | 10.1.10.199 | — | (browser access)
Network layout
VLAN | Subnet | Interface | Purpose
client_vlan | 10.1.10.0/24 | 1.1 | Client-facing. VIPs: 10.1.10.100, .115
server_vlan | 10.1.20.0/24 | 1.2 | Server-facing. Pool members: .11–.15
vlan-30 (HA) | 10.1.30.0/24 | 1.3 | HA: ConfigSync, failover, mirroring
management | 10.1.1.0/24 | mgmt | Out-of-band management, SSH, GUI
First step in Lab 1: Access bigip01 at https://10.1.1.245 (admin/admin.F5demo.com). Verify you can SSH to 10.1.1.245 (root/default). Build base networking using TMSH.
Notes: WHAT THIS SLIDE TEACHES
Lab environment overview. Students need this reference throughout the course for IP addresses, credentials, and VLAN structure.
TIP: Print this slide or keep it open as a reference tab. You'll look up IPs constantly during labs.

## Slide 7
7 © 2026 F5
Before we begin
Housekeeping, expectations, and how to get the most from this course
Lab access
Verify you can reach bigip01 (https://10.1.1.245) and SSH to it. If not, troubleshoot now — we start building in Lab 1.
Slides + speaker notes
Every slide has detailed speaker notes with full technical explanations, pivot questions, exam patterns, and F5 doc references. Use them for self-study.
Exam checkpoints
After each lab, we pause for exam-style questions. Try to answer BEFORE looking at the speaker notes. This is where the real learning happens.
TMSH first, GUI second
We show both GUI paths and TMSH commands. The exam tests TMSH syntax heavily. Practice typing commands, not just clicking buttons.
Save your work
At key points we'll archive configs with UCS. If something breaks, you can restore and continue. Don't skip the archive steps.
Focus on scenarios
Beta exam questions are scenario-based. We teach with scenarios. Read the full scenario before answering — the setup is more important than the question.
Ready? Let's start with Lab 1 — Basic Setup, TMSH, and SNATs.
Notes: WHAT THIS SLIDE TEACHES
Getting started checklist. Six items covering lab access, materials usage, exam prep strategy, TMSH emphasis, archiving, and scenario-based thinking.
Transition to Lab 1.

## Slide 8
LAB 1
Basic setup, TMSH & SNATs
Build a working LTM application from scratch using TMSH, then explore
SNAT behavior with tcpdump and connection tables.
50 min | 20 min slides + 30 min lab
F5CTSLTM1.01 | U/A | Determine if app can deploy with LTM only
F5CTSLTM1.04 | U/A | Basic device configuration (GUI/CLI)
F5CTSLTM2.06 | R | Original client IP / SNAT / X-Forwarded-For
Notes: SECTION OPENER - Lab 1: Basic Setup, TMSH & SNATs
PURPOSE
This lab establishes the foundational skills for the entire course. Students build a complete LTM application stack from scratch using TMSH (the Traffic Management Shell), then investigate how Source Network Address Translation (SNAT) affects traffic using tcpdump packet captures and the BIG-IP connection table. This is the only lab where students construct the base infrastructure, so it must be completed successfully before all subsequent labs.
BETA BLUEPRINT COVERAGE
- F5CTSLTM1.01 (U/A): "Determine whether or not an application can be deployed with only the LTM module provisioned." By building a working VS/pool/profile stack, students prove firsthand what LTM can deliver standalone.
- F5CTSLTM1.04 (U/A): "Determine how to perform basic device configuration" with the sub-bullet "Determine how to limit administrative access to LTM device (GUI/CLI)." The TMSH challenge forces CLI proficiency; the GUI verification afterward covers the dual-method requirement. This is one of the explicit GUI/CLI callouts in the blueprint.
- F5CTSLTM2.06 (R): "Determine which configuration objects are necessary for applications that need the original client IP address." The SNAT automap vs SNAT pool exercise directly covers all four sub-bullets: when SNAT is required, the required SNAT type, X-Forwarded-For functions, and steps to return traffic without SNAT.
301a OBJECTIVE: 1.01 - Given an expected traffic volume, determine the appropriate SNAT configuration.
DELIVERY TIPS
- Have students attempt the TMSH build from memory FIRST. Only point them to Appendix II in the lab guide if they get stuck after 5+ minutes.
- Emphasize the "save sys config" + "save sys ucs" step - students who skip this lose their work if the lab environment resets.
- The SNAT exercise is where the real learning happens. Make sure every student runs tcpdump and can see the source IP difference between automap and SNAT pool.
TIME MANAGEMENT: 50 minutes total. If students finish the TMSH build quickly (some will if they have prior BIG-IP experience), have them start the SNAT exercise immediately rather than waiting for the class.

## Slide 9
9 © 2026 F5
LTM configuration object hierarchy
Every application deployment follows this dependency chain
Virtual server
Listener - receives client traffic
▼
Profiles
TCP, HTTP, SSL, persistence, etc.
▼
Pool
Group of backend servers + health monitor
▼
Nodes
Individual server IP addresses
Key dependencies
A virtual server requires at least one protocol profile (TCP or UDP) to function. Without it, the VS cannot process traffic.
Pools reference nodes. Deleting a node IP removes it from every pool that contains it as a member.
Health monitors attach to pools or individual pool members, never directly to virtual servers.
A virtual address object is auto-created when you create a virtual server. It controls ARP, ICMP, and route advertisement for the VS IP.
Notes: CONCEPT SLIDE - LTM Configuration Object Hierarchy
WHAT THIS SLIDE TEACHES
This slide introduces the fundamental dependency chain that underlies every LTM application deployment. Understanding this hierarchy is essential because the BIG-IP enforces these dependencies - you cannot create a virtual server without specifying at least a protocol profile, and you cannot assign a pool that references non-existent nodes.
THE DEPENDENCY CHAIN EXPLAINED
1. VIRTUAL SERVER (top): The virtual server is the entry point for all client traffic. It is defined by a destination IP address and port (e.g., 10.1.10.100:80). The virtual server is the "listener" that the BIG-IP uses to intercept traffic destined for your application. When a client sends a request to 10.1.10.100:80, the BIG-IP's TMM (Traffic Management Microkernel) matches it against configured virtual servers and processes it according to the VS configuration.
2. PROFILES (second level): Profiles define HOW the BIG-IP processes the traffic. At minimum, every virtual server needs a transport protocol profile - either TCP, UDP, or FastL4. Additional profiles (HTTP, SSL, persistence, OneConnect, compression) add application-layer intelligence. Profiles use a parent/child inheritance model - you create a custom profile that inherits from a default parent, then override only the settings you need to change.
3. POOL (third level): The pool is a logical group of backend servers (pool members) that the BIG-IP load balances traffic across. Each pool has a load balancing method (Round Robin by default) and can have one or more health monitors assigned to it. The pool is the bridge between the virtual server (what the client sees) and the actual servers (what serves the content).
4. NODES (bottom): Nodes are the individual server IP addresses. A node is automatically created when you add a pool member (IP:port). Multiple pools can reference the same node - for example, 10.1.20.11 might be a member of both an HTTP pool (port 80) and an HTTPS pool (port 443). This is why deleting a node affects all pools that reference it.
KEY CONCEPT - VIRTUAL ADDRESS vs VIRTUAL SERVER
Students often confuse these. The virtual ADDRESS is the IP address itself (10.1.10.100). The virtual SERVER is the combination of that address + port + all configuration (10.1.10.100:80 with its profiles, pool, rules). One virtual address can have multiple virtual servers (different ports). The virtual address controls low-level behavior like ARP responses and ICMP echo replies.
PIVOT QUESTION (ask before advancing)
"If you delete a pool member's node, what happens to the pool? What about the virtual server?"
ANSWER: The node is removed from the pool. If the pool still has other members, the VS continues to work but now load balances across fewer servers. If it was the only member, the pool has no members and the VS will show as unavailable (red) because the monitor will have nothing to check.
F5 DOCUMENTATION
- Virtual server concepts: https://my.f5.com/manage/s/article/K15683
- Pool and node management: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-pools.html

## Slide 10
10 © 2026 F5
Deployment types
How the BIG-IP sits in the network determines traffic processing and IP address behavior
One-arm
BIG-IP connects to a single network segment shared by clients and servers. All traffic enters and exits through the same interface.
SNAT required
Two-arm
BIG-IP sits between separate client and server networks, routing traffic between VLANs. Most common enterprise deployment.
SNAT or routing
nPath / DSR
BIG-IP only handles inbound traffic. Servers respond directly to clients, bypassing the BIG-IP on the return path.
No SNAT
Auto last-hop: Ensures return traffic uses the same path it arrived on. Enabled by default. Critical in two-arm and multi-router deployments to prevent asymmetric routing, which causes the BIG-IP to drop return packets it cannot match to a connection.
Notes: CONCEPT SLIDE - Deployment Types Overview
WHAT THIS SLIDE TEACHES
This is the high-level comparison of the three primary ways a BIG-IP LTM can be positioned in a network. The next three slides dive deep into each one with traffic flow diagrams. This overview establishes the framework so students can compare them side by side before examining each individually.
WHY DEPLOYMENT TYPE MATTERS
The deployment type determines:
1. Whether SNAT is required (and what type)
2. How IP addresses change as packets traverse the BIG-IP
3. What the server sees as the client IP address
4. Whether the BIG-IP can inspect and modify return traffic
5. Network design considerations (routing, VLANs, self IPs)
These decisions are made during the architecture phase and are difficult to change after deployment. The F5-CTS exam tests this heavily under objectives 1.02 (identify deployment differences) and 2.06 (original client IP / SNAT).
THE THREE DEPLOYMENT TYPES AT A GLANCE
- ONE-ARM: Simplest to deploy. BIG-IP has one VLAN with one self IP. Client and server traffic share the same network segment. SNAT is mandatory because without it, server responses bypass the BIG-IP entirely (they go directly to the client since they're on the same subnet). Most common in proof-of-concept or small deployments.
- TWO-ARM: The standard enterprise deployment. BIG-IP has separate client-side and server-side VLANs. Traffic enters on the client VLAN, gets processed, and exits on the server VLAN. This gives full traffic visibility and control. SNAT may or may not be required depending on whether the servers' default gateway points to the BIG-IP.
- nPath/DSR (Direct Server Return): Highest performance, lowest feature set. The BIG-IP only handles the initial client request. The server responds directly to the client without going through the BIG-IP. This means no server-side processing (no response modification, no cookie persistence, no server-SSL). Used for high-throughput scenarios like video streaming or DNS where full proxy features aren't needed.
AUTO LAST-HOP EXPLAINED
Auto last-hop is a BIG-IP feature (enabled by default) that remembers which router/gateway sent a packet to the BIG-IP and ensures the response goes back the same way. Without it, in environments with multiple default gateways or asymmetric routing, the BIG-IP might send return traffic out a different path than it arrived on. This causes the upstream router to drop the packet because it doesn't match any connection in its state table.
Reference: https://my.f5.com/manage/s/article/K13876 (K13876: Overview of the Auto Last Hop setting)
PIVOT QUESTION
"In which deployment type does the server see the real client IP address without any additional configuration?"
ANSWER: nPath/DSR. Because the BIG-IP doesn't modify the source IP (it only does a MAC-level rewrite), the server sees the original client IP. In one-arm and two-arm deployments, SNAT replaces the client IP unless you specifically configure the routing to avoid it.

## Slide 11
11 © 2026 F5
One-arm deployment
Single VLAN | SNAT required | Simplest topology
10.1.10.0/24 (Single VLAN)
Client
10.1.10.50
BIG-IP LTM
VS: 10.1.10.100:80
Self: 10.1.10.245
Server 1
10.1.10.11
Server 2
10.1.10.12
Server 3
10.1.10.13
▶
▶
Request
Src: 10.1.10.50
Dst: 10.1.10.100
After SNAT
Src: 10.1.10.245
Dst: 10.1.10.11
Why SNAT is mandatory
Without SNAT, the server receives a request from 10.1.10.50 (the client). Since the client is on the same subnet, the server responds directly to the client, bypassing the BIG-IP entirely. The BIG-IP never sees the response, cannot track the connection, and the client receives traffic from an unexpected source IP (the server, not the VIP).
Use cases
Proof-of-concept and lab environments
Small deployments with limited network changes
Adding LTM to an existing flat network
Environments where server default gateway cannot change
Notes: DEEP DIVE - One-Arm Deployment
WHAT THIS SLIDE TEACHES
The one-arm (also called "single-arm" or "same-subnet") deployment places the BIG-IP on the same network segment as both the clients and the servers. All traffic enters and exits through a single VLAN and interface. This is the simplest deployment topology but has important limitations that students must understand.
TRAFFIC FLOW - STEP BY STEP
1. Client (10.1.10.50) sends a request to the virtual server IP (10.1.10.100:80)
2. BIG-IP receives the request on its client VLAN
3. BIG-IP selects a pool member (e.g., 10.1.10.11:80) based on the load balancing method
4. BIG-IP applies SNAT - changes the source IP from 10.1.10.50 to its own self IP (10.1.10.245)
5. BIG-IP forwards the request to the server: Src=10.1.10.245, Dst=10.1.10.11
6. Server processes the request and sends the response to 10.1.10.245 (the BIG-IP, not the client)
7. BIG-IP receives the response, reverses the SNAT (restores the original source), and sends it back to the client
WHY SNAT IS MANDATORY IN ONE-ARM
This is the single most important concept on this slide. Without SNAT:
- The server receives a request where Src=10.1.10.50 (client) and Dst=10.1.10.11 (itself)
- The server sends its response directly to 10.1.10.50 (the client) because it's on the same subnet - no routing through the BIG-IP is needed
- The client receives a TCP response from 10.1.10.11 (the server) instead of 10.1.10.100 (the VIP it originally connected to)
- The client's TCP stack rejects this as an unsolicited packet because it doesn't match any open connection
With SNAT:
- The server receives a request where Src=10.1.10.245 (BIG-IP self IP) and Dst=10.1.10.11 (itself)
- The server responds to 10.1.10.245 (the BIG-IP)
- The BIG-IP restores the original source and destination, and the client receives the response from the expected VIP address
LIMITATIONS OF ONE-ARM
- Server logs show the BIG-IP self IP instead of the real client IP (mitigated by X-Forwarded-For for HTTP)
- Ephemeral port exhaustion: SNAT automap is limited to ~65,535 concurrent connections per self IP
- Cannot use nPath/DSR in this topology
- Server-to-server traffic through the BIG-IP can create routing loops if not carefully managed
COMMON EXAM QUESTION PATTERNS
- "Given a one-arm deployment, why do servers log the BIG-IP IP instead of the client IP?" (Answer: SNAT)
- "A one-arm deployment works for HTTP but fails for FTP. Why?" (Answer: FTP active mode requires the FTP profile to handle the data channel NAT)
F5 DOCUMENTATION
- SNAT overview: https://my.f5.com/manage/s/article/K7820
- One-arm deployment guide: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-concepts.html
PIVOT QUESTION
"If you have 100,000 concurrent client connections in a one-arm deployment with SNAT automap, what problem will you hit?"
ANSWER: Ephemeral port exhaustion. SNAT automap uses the floating self IP, which has a maximum of ~65,535 ephemeral ports. With 100K connections, you need a SNAT pool with at least 2 addresses (100,000 / 65,535 = ~1.53, so 2 SNAT addresses minimum).

## Slide 12
12 © 2026 F5
Two-arm deployment
Separate VLANs | SNAT optional | Most common enterprise topology
Client VLAN - 10.1.10.0/24
Server VLAN - 10.1.20.0/24
Client
10.1.10.50
BIG-IP LTM
Client Self: 10.1.10.245
Server Self: 10.1.20.245
Server 1
10.1.20.11
Server 2
10.1.20.12
Server 3
10.1.20.13
▶
▶
SNAT decision matrix
Server default GW | SNAT needed? | Why
Points to BIG-IP | No | Return traffic routes through BIG-IP naturally
Points elsewhere | Yes | Must SNAT so server responds to BIG-IP, not client
Advantages
Full visibility of both client and server traffic
Can apply different security policies per VLAN
Server sees real client IP (if no SNAT)
Supports all LTM features (SSL, compression, etc.)
Notes: DEEP DIVE - Two-Arm Deployment
WHAT THIS SLIDE TEACHES
The two-arm deployment is the most common enterprise topology for BIG-IP LTM. The BIG-IP bridges two separate network segments (VLANs) - a client-facing VLAN and a server-facing VLAN. This provides maximum control over traffic because the BIG-IP sees every packet in both directions.
TRAFFIC FLOW - STEP BY STEP
1. Client (10.1.10.50) sends request to VIP (10.1.10.100:80) on the client VLAN
2. BIG-IP receives the request on client_vlan (interface 1.1)
3. BIG-IP selects a pool member (10.1.20.11:80) and determines the egress VLAN (server_vlan)
4. IF SNAT automap is configured: BIG-IP changes Src IP from 10.1.10.50 to 10.1.20.245 (server-side floating self IP)
5. IF no SNAT: BIG-IP preserves Src IP as 10.1.10.50 (but the server must route back through BIG-IP)
6. BIG-IP forwards the request out server_vlan (interface 1.2) to the pool member
7. Server processes and responds to either the BIG-IP self IP (SNAT) or the original client IP (no SNAT)
8. BIG-IP processes the response, applies profiles, and returns it to the client
THE CRITICAL SNAT DECISION
This is where students often get confused. The rule is simple:
- If the server's default gateway IS the BIG-IP: No SNAT needed. The server's return traffic naturally routes through the BIG-IP because the BIG-IP is its next hop.
- If the server's default gateway is NOT the BIG-IP (e.g., it points to a separate router): SNAT is required. Otherwise, the server sends its response to the client via the router, bypassing the BIG-IP. The BIG-IP never sees the response and the connection fails.
In the lab environment, the servers' default gateway does NOT point to the BIG-IP, so SNAT automap is required. This is why Lab 1 has students configure SNAT automap on the virtual server.
NETWORK REQUIREMENTS
- BIG-IP needs at least two VLANs (client-side and server-side)
- Each VLAN needs a self IP address (one per VLAN minimum; floating self IPs for HA)
- Routing must be configured so client traffic reaches the BIG-IP
- If using SNAT: server default gateway can point anywhere
- If NOT using SNAT: server default gateway MUST point to the BIG-IP self IP on the server VLAN
AUTO LAST-HOP IN TWO-ARM
Auto last-hop becomes important in two-arm deployments with multiple upstream routers. If traffic arrives via Router A but the BIG-IP's default route points to Router B, auto last-hop ensures the response goes back through Router A (the router that sent the original request). Without it, Router B receives a response packet it has no connection state for and drops it.
F5 DOCUMENTATION
- Deployment guide: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-concepts.html
- Auto last-hop: https://my.f5.com/manage/s/article/K13876
- SNAT and routing: https://my.f5.com/manage/s/article/K7820
PIVOT QUESTION
"You deploy a two-arm BIG-IP. HTTP traffic works fine, but the servers log the BIG-IP self IP instead of the client IP. The network team cannot change the server default gateway. How do you let the servers log the real client IP?"
ANSWER: Keep SNAT automap (it's required since the gateway can't change), but enable X-Forwarded-For in the HTTP profile. The server application reads the X-Forwarded-For header to get the original client IP for logging. This only works for HTTP/HTTPS traffic - non-HTTP protocols lose client IP visibility when SNAT is used.

## Slide 13
13 © 2026 F5
nPath / Direct Server Return (DSR)
Inbound only | No SNAT | Highest throughput | Limited feature set
Client
192.168.1.50
BIG-IP LTM
VIP: 10.1.10.100
Server 1
lo0: 10.1.10.100
Server 2
lo0: 10.1.10.100
▶
▶
◀ Direct return (bypasses BIG-IP)
MAC rewrite only
Src: 192.168.1.50
Dst: 10.1.10.100
How nPath works
The BIG-IP rewrites only the destination MAC address (Layer 2) to direct the packet to the selected server. The IP addresses are unchanged. Each server must have the VIP address configured on a loopback interface (non-ARP) so it can accept and respond to traffic destined for that IP. The server responds directly to the client using its own routing table.
Features NOT available
No server-side connection tracking
No cookie persistence (no return traffic to read)
No HTTP response modification
No server-SSL (re-encryption)
No compression of server responses
Notes: DEEP DIVE - nPath / Direct Server Return (DSR)
WHAT THIS SLIDE TEACHES
nPath (also called Direct Server Return or DSR) is the highest-performance BIG-IP deployment mode because the BIG-IP only processes inbound client requests. Server responses go directly back to the client without passing through the BIG-IP. This dramatically reduces the load on the BIG-IP but severely limits which LTM features can be used.
TRAFFIC FLOW - STEP BY STEP
1. Client (192.168.1.50) sends request to VIP (10.1.10.100:80)
2. BIG-IP receives the request and selects a pool member
3. BIG-IP rewrites ONLY the destination MAC address to point to the selected server's MAC - the IP addresses (both source and destination) remain completely unchanged
4. Server receives the packet: Src=192.168.1.50, Dst=10.1.10.100
5. The server accepts the packet because it has 10.1.10.100 configured on its loopback interface (lo0)
6. Server responds directly to the client (192.168.1.50) using its own default gateway - the response NEVER passes through the BIG-IP
7. Client receives the response from 10.1.10.100 (the VIP), which matches its original request
CRITICAL SERVER REQUIREMENT - LOOPBACK INTERFACE
For nPath to work, EVERY server in the pool must have the VIP address (10.1.10.100) configured on a loopback interface. This is necessary because:
- The destination IP in the packet is 10.1.10.100 (the VIP, not the server's real IP)
- If the server doesn't have this IP configured, it drops the packet as "not destined for me"
- The loopback must be configured as NON-ARP (does not respond to ARP requests for this IP) - otherwise the server would compete with the BIG-IP for ARP resolution of the VIP
On Linux: ip addr add 10.1.10.100/32 dev lo
On Windows: Add a loopback adapter with the VIP address, disable "Register this connection's addresses in DNS"
WHY "MAC REWRITE ONLY"
Unlike standard and one-arm deployments where the BIG-IP modifies IP addresses (via SNAT and destination NAT), nPath only changes the Layer 2 (MAC) address. This is why:
- The source IP stays as the client IP (no SNAT) - servers see the real client IP natively
- The destination IP stays as the VIP (no destination NAT to the server's real IP)
- This means no IP-level connection tracking on the BIG-IP for server-side traffic
FEATURES THAT DO NOT WORK WITH nPath
Since the BIG-IP never sees the return traffic:
- Cookie persistence: Requires reading Set-Cookie headers in the response
- HTTP compression: Requires modifying the response body
- Server-SSL: Requires terminating/re-encrypting on the server side
- Response rewriting (iRules operating on HTTP_RESPONSE)
- OneConnect (requires managing server-side connections)
- Content caching (RamCache)
Features that DO work:
- Source address persistence (based on client IP, tracked on inbound)
- Client-SSL termination (decrypt on inbound only)
- iRules that operate on client-side events (HTTP_REQUEST, CLIENT_ACCEPTED)
- Health monitoring (separate monitor connections)
USE CASES
- High-throughput applications: video streaming, CDN edge, DNS
- Applications where the server can handle SSL natively
- When maintaining original client IP is critical and XFF is not sufficient (non-HTTP protocols)
- Environments where BIG-IP throughput is the bottleneck
F5 DOCUMENTATION
- nPath routing: https://my.f5.com/manage/s/article/K7595
- Configuring nPath: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-implementations/configuring-npath-routing.html
- DSR loopback requirements: https://my.f5.com/manage/s/article/K11116
PIVOT QUESTION
"A customer wants nPath for a web application that uses cookie-based session persistence. Will this work?"
ANSWER: No. Cookie persistence requires the BIG-IP to read the Set-Cookie header in the server response, but in nPath the response never passes through the BIG-IP. The customer would need to use source address persistence instead, or switch to a standard (full proxy) deployment if cookie persistence is a hard requirement.

## Slide 14
14 © 2026 F5
SNAT types
Reference table - when to use each source address translation type
Type | Source IP becomes | Use when | Limitation
None | Unchanged (original client IP) | Server default gateway is the BIG-IP, or using nPath/DSR | Servers must route return traffic through BIG-IP
Automap | Floating self IP of the egress VLAN | Simple deployments where server doesn't need client IP in L3 header | ~65,535 connections per self IP (ephemeral port limit)
SNAT pool | Rotates through pool of dedicated SNAT addresses | High connection volume exceeds single-IP ephemeral port limit | Requires additional IP addresses on server VLAN
X-Forwarded-For header
When SNAT replaces the client IP, the server loses visibility of the original source. Enable the X-Forwarded-For (XFF) option in the HTTP profile to insert the original client IP as an HTTP header. The server application can then read this header for logging, access control, or geolocation. XFF only works for HTTP/HTTPS traffic - non-HTTP protocols (FTP, SMTP, DNS) lose client IP visibility entirely when SNAT is used.
SNAT object vs virtual server SNAT: A standalone SNAT object (created under Local Traffic > Address Translation > SNAT) translates outbound server-initiated traffic without a virtual server. The virtual server's Source Address Translation setting (None/Automap/SNAT Pool) translates traffic processed by that VS. They serve different purposes.
Notes: CONCEPT SLIDE - SNAT Types Reference Table
WHAT THIS SLIDE TEACHES
This is a recall-level (R) reference table that students should photograph or screenshot for later study. It covers Beta objective F5CTSLTM2.06: "Determine which configuration objects are necessary for applications that need the original client IP address."
THE THREE SNAT TYPES IN DETAIL
1. NONE (No Source Address Translation)
- The BIG-IP does not modify the source IP address
- The server sees the real client IP in the packet header
- REQUIREMENT: The server's return traffic MUST route through the BIG-IP. This typically means the server's default gateway is the BIG-IP's self IP on the server VLAN
- If the server's default gateway is a different router, the response bypasses the BIG-IP and the connection fails
- Best for: environments where preserving client IP at L3 is critical (non-HTTP protocols) and the network topology supports it
2. AUTOMAP
- The BIG-IP replaces the source IP with its floating self IP on the egress VLAN
- "Floating" is key: in an HA pair, the floating self IP moves with the active device, so failover doesn't break connections
- The ephemeral port limit is ~65,535 per self IP address. Each client connection uses one ephemeral port. Once all ports are exhausted, new connections fail with "SNAT port exhaustion" errors visible in /var/log/ltm
- Best for: simple deployments with moderate connection counts
3. SNAT POOL
- You create a pool of dedicated SNAT IP addresses. The BIG-IP distributes connections across these addresses
- Each SNAT pool address provides an additional ~65,535 ephemeral ports
- Formula: Required SNAT addresses = Ceiling(max_concurrent_connections / 65535)
- Example: 200,000 concurrent connections = Ceiling(200000/65535) = 4 SNAT pool addresses minimum
- The SNAT pool addresses must be routable on the server VLAN (servers must be able to reach them)
- Best for: high-volume deployments or when automap port exhaustion is a concern
X-FORWARDED-FOR (XFF) EXPLAINED
XFF is an HTTP header that the BIG-IP can insert into the request when SNAT is active. It contains the original client IP address. Format: X-Forwarded-For: 10.1.10.50
To enable XFF:
- TMUI: Profiles > HTTP > [profile name] > Insert X-Forwarded-For > Enabled
- TMSH: modify ltm profile http my_http_profile insert-xforwarded-for enabled
Important caveats:
- XFF is an HTTP-layer solution. It only works when an HTTP profile is applied to the virtual server
- The server application must be configured to read the XFF header (e.g., Apache: mod_remoteip; Nginx: set_real_ip_from)
- XFF can be spoofed by clients. If using XFF for security decisions, also configure the "Accept XFF" setting carefully
- For non-HTTP protocols (FTP, SMTP, DNS, SIP), there is no equivalent mechanism - the original client IP is lost
SNAT OBJECT vs VIRTUAL SERVER SNAT
Students often confuse these two distinct features:
- Virtual Server Source Address Translation: Applied to traffic processed by a specific virtual server. Configured on the VS itself. Translates the source IP of client-to-server traffic.
- Standalone SNAT Object (Local Traffic > Address Translation > SNAT): Applied to server-initiated outbound traffic that does NOT match any virtual server. Used when servers need to reach external resources through the BIG-IP (e.g., software updates, API calls) and you want to translate their source IP.
F5 DOCUMENTATION
- SNAT overview: https://my.f5.com/manage/s/article/K7820
- SNAT port exhaustion: https://my.f5.com/manage/s/article/K13637
- X-Forwarded-For: https://my.f5.com/manage/s/article/K4816
- SNAT pool configuration: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-snats.html

## Slide 15
15 © 2026 F5
TMSH syntax orientation
Five verbs cover most operations. The module and component follow the verb.
create
Build a new object
create ltm pool www_pool members add { 10.1.20.11:80 }
modify
Change existing object
modify ltm virtual www_vs source-address-translation { type automap }
list
Show running config
list ltm virtual www_vs
show
Show live status/stats
show ltm pool www_pool members
delete
Remove an object
delete ltm virtual www_vs
Tip: Tab completion works in TMSH. Type the first characters and press Tab. | list shows config (what you typed). show displays live status (what's happening).
Notes: CONCEPT SLIDE - TMSH Syntax Orientation
WHAT THIS SLIDE TEACHES
This slide provides a quick orientation to TMSH (Traffic Management Shell) syntax before students use it to build the lab configuration. TMSH is the primary CLI for BIG-IP administration and is explicitly called out in Beta objective F5CTSLTM1.04: "Determine how to limit administrative access to LTM device (GUI/CLI)."
TMSH SYNTAX PATTERN
Every TMSH command follows this pattern:
verb module component object-name [parameters]
Examples:
create ltm pool www_pool members add { 10.1.20.11:80 }
modify net self server_ip address 10.1.20.245/24
show sys performance all-stats
MODULES: The three most common modules are:
- ltm: Local Traffic Manager objects (virtual servers, pools, profiles, monitors, rules)
- net: Network objects (VLANs, self IPs, routes, trunks, route domains)
- sys: System objects (config, software, performance, DNS, NTP, users, licenses)
THE FIVE VERBS EXPLAINED
1. CREATE - Builds a new object. The object must not already exist (use "modify" to change existing). All required parameters must be specified in the create command.
2. MODIFY - Changes properties of an existing object. You only specify the properties you want to change - everything else stays as-is. Common mistake: using "modify" on an object that doesn't exist yet (use "create" first).
3. LIST - Displays the running configuration of an object exactly as it's stored in bigip.conf. This shows what you configured, including default values. Useful for verifying your configuration matches what you intended.
4. SHOW - Displays real-time operational status and statistics. For a pool, "show" reveals which members are up/down, how many current connections each has, bytes transferred, etc. For a virtual server, "show" reveals the current state (available/unavailable), connection count, and throughput.
KEY DIFFERENCE: "list" vs "show"
This is one of the most commonly tested concepts:
- list ltm pool www_pool = shows the CONFIGURATION (members, monitor, LB method)
- show ltm pool www_pool members = shows the STATUS (up/down, connections, bytes)
Students who confuse these will get exam questions wrong.
5. DELETE - Removes an object. Dependencies are enforced: you cannot delete a pool that is assigned to a virtual server (remove the pool from the VS first). You cannot delete a node that is a member of any pool.
SAVING CONFIGURATION
After making changes in TMSH:
- save sys config: Writes the running configuration to disk (/config/bigip.conf). Without this, changes are lost if the system reboots.
- save sys ucs <filename>: Creates a complete backup archive (UCS) that includes certificates, licenses, and configuration. This is what you restore from if something goes wrong.
F5 DOCUMENTATION
- TMSH reference guide: https://techdocs.f5.com/en-us/bigip-14-1-0/bigip-tmsh-reference.html
- TMSH command syntax: https://my.f5.com/manage/s/article/K13637
PIVOT QUESTION
"What's the difference between 'list ltm pool www_pool' and 'show ltm pool www_pool members'?"
ANSWER: "list" shows the configuration (what you typed when you created the pool - members, monitor assignment, load balancing method). "show" displays live operational data (which members are up/down, how many active connections each has, total bytes transferred). "list" is static config; "show" is dynamic status.

## Slide 16
16 © 2026 F5
Lab 1 - Hands-on exercises
30 minutes | Lab guide: Module 1
# | Activity | Key tasks | Time
1 | TMSH challenge | Build VLANs, Self IPs, pool, virtual server entirely via TMSH. Verify in GUI. | 15 min
2 | SNATs and NATs | Build FTP VS with SNAT automap, create SNAT pool, use tcpdump to compare source IPs, examine connection table. | 15 min
Access credentials
Method | Address | Username | Password
GUI (HTTPS) | https://10.1.1.4 | admin | admin.F5demo.com
SSH (CLI) | ssh root@10.1.1.4 | root | default
Reminder: After building, save your configuration: save sys config then save sys ucs lab1-base-config. TMSH commands are in Appendix II if you get stuck.
Notes: LAB LAUNCH - Leave this slide on screen while students work.
LAB ENVIRONMENT OVERVIEW
Students connect to a BIG-IP VE (Virtual Edition) running TMOS. The environment has:
- Management interface: 10.1.1.4 (used for GUI and SSH access)
- Client VLAN interface: 1.1 (to be configured as client_vlan)
- Server VLAN interface: 1.2 (to be configured as server_vlan)
- Three web servers: 10.1.20.11, 10.1.20.12, 10.1.20.13 (all on port 80)
- One FTP server: 10.1.20.15 (port 21)
- Client workstation: 10.1.10.199 (the jumpbox)
ACTIVITY 1: TMSH CHALLENGE (15 min)
Students build the entire base configuration via TMSH:
1. Create VLANs: client_vlan (interface 1.1), server_vlan (interface 1.2)
2. Create Self IPs: client_ip (10.1.10.245/24 on client_vlan), server_ip (10.1.20.245/24 on server_vlan)
3. Create default route: def_gw (network 0.0.0.0/0, gateway 10.1.10.1)
4. Create pool: www_pool (members 10.1.20.11:80, 10.1.20.12:80, 10.1.20.13:80, monitor http)
5. Create virtual server: www_vs (destination 10.1.10.100:80, pool www_pool, ip-protocol tcp, source-address-translation automap)
6. Save config and create UCS backup
Verification: VS should show green (Available) in GUI. Browse to http://10.1.10.100 from the client.
ACTIVITY 2: SNATs AND NATs (15 min)
Students build an FTP virtual server and experiment with SNAT:
1. Create ftp_pool (member 10.1.20.15:21, monitor tcp)
2. Create ftp_vs (destination 10.1.10.100:21, ftp profile, SNAT automap)
3. Open two SSH sessions: one for tcpdump, one for TMSH
4. Run tcpdump on server_vlan while establishing an FTP connection
5. Observe the source IP in tcpdump (should be the BIG-IP self IP due to SNAT)
6. Check connection table: show sys connection
7. Create a SNAT pool, assign it to the FTP VS, and compare the tcpdump output
Lab guide Q1: "In Request Detail at the top of the page, what is the client IP address and why?"
ANSWER: The client IP shows as 10.1.10.245 (or the SNAT pool address) because SNAT automap replaces the original client IP with the BIG-IP's floating self IP.
COMMON ISSUES
- Students forget to add "ip-protocol tcp" to the virtual server - the VS won't work without it
- Students create the pool without a monitor - the pool shows as available but members aren't health-checked
- SSH session to the management IP (10.1.1.4) won't appear in "show sys connection" because management traffic is handled by the host OS, not TMM

## Slide 17
17 © 2026 F5
Exam checkpoints
These mirror the cognitive level and style of F5-CTS Beta exam questions
Q1
U/A
1.01
You built the virtual server with SNAT automap. Your application works, but you now expect 100,000 concurrent connections. What SNAT configuration change would you make and why?
Q2
U/A
1.04
After building the configuration in TMSH, you verify it in the GUI. The virtual server shows a red circle (Offline). What are two things you would check first?
Q3
R
2.06
A backend server must log the original client IP for compliance. SNAT automap is required for routing. What do you configure to preserve the client IP in HTTP requests?
Notes: EXAM CHECKPOINTS - Debrief after lab completion
These questions should be asked verbally after students complete the lab. Do NOT show the answers on screen - use the speaker notes to guide the discussion.
Q1 ANSWER (U/A - Objective 1.01)
Switch from SNAT automap to a SNAT pool with multiple dedicated IP addresses.
Detailed explanation: SNAT automap uses the floating self IP on the egress VLAN. Each IP address supports approximately 65,535 concurrent connections (limited by the number of ephemeral ports available). With 100,000 expected concurrent connections, a single automap address will exhaust its ports.
Solution: Create a SNAT pool with at least 2 addresses (100,000 / 65,535 = 1.53, round up to 2). For safety margin, use 3 addresses to handle burst traffic. These addresses must be on the server VLAN subnet and must not conflict with any existing IPs.
TMSH: create ltm snatpool my_snat_pool members add { 10.1.20.240 10.1.20.241 10.1.20.242 }
Then: modify ltm virtual www_vs source-address-translation { type snatpool pool my_snat_pool }
Q2 ANSWER (U/A - Objective 1.04)
Two things to check:
1. Pool member health: Go to Local Traffic > Pools > www_pool > Members. If the monitor is failing, members show as red/offline, which makes the pool unavailable, which makes the VS offline. Common cause: monitor is checking the wrong port, or the server application isn't running.
2. Virtual server configuration: Check that the destination IP and port are correct, the pool is assigned, and ip-protocol is set (tcp or udp). A missing ip-protocol is the most common TMSH mistake - the GUI requires it but TMSH lets you omit it, resulting in a VS that doesn't match any traffic.
Additional checks: Verify the self IPs exist on the correct VLANs, verify the default route is configured, check that no other VS is already listening on the same IP:port combination.
Q3 ANSWER (R - Objective 2.06)
Enable the X-Forwarded-For option in the HTTP profile attached to the virtual server.
TMUI: Profiles > HTTP > [profile] > Insert X-Forwarded-For > Enabled
TMSH: modify ltm profile http my_http insert-xforwarded-for enabled
The server application must then be configured to read the X-Forwarded-For header for logging. In Apache, use mod_remoteip. In Nginx, use set_real_ip_from directive. In IIS, use the X-Forwarded-For module.
Important: This only works for HTTP/HTTPS traffic. If the compliance requirement extends to non-HTTP protocols, you'll need to eliminate SNAT entirely (change server routing so return traffic goes through the BIG-IP) or accept that non-HTTP client IPs cannot be preserved.

## Slide 18
18 © 2026 F5
TMSH quick reference - Lab 1 commands
Key commands used in this lab. Practice TMSH-only to build CLI fluency.
Networking
create net vlan client_vlan interfaces add { 1.1 { untagged } }
create net vlan server_vlan interfaces add { 1.2 { untagged } }
create net self client_ip address 10.1.10.245/24 vlan client_vlan
create net self server_ip address 10.1.20.245/24 vlan server_vlan
create net route def_gw network 0.0.0.0/0 gw 10.1.10.1
Pool and virtual server
create ltm pool www_pool members add { 10.1.20.11:80 10.1.20.12:80 10.1.20.13:80 } monitor http
create ltm virtual www_vs destination 10.1.10.100:80 pool www_pool ip-protocol tcp \
source-address-translation { type automap }
Save and backup
save sys config
save sys ucs lab1-base-config
Notes: TMSH REFERENCE - Lab 1 Commands
This slide is a student reference for the key TMSH commands used in Lab 1. Encourage students to:
1. Try building from memory first
2. Use Tab completion in TMSH to discover available parameters
3. Only reference this slide or Appendix II if stuck after 5+ minutes
COMPLETE COMMAND SET FOR THE BASE BUILD
The commands shown cover the minimum required to build a working LTM configuration:
NETWORKING:
create net vlan client_vlan interfaces add { 1.1 { untagged } }
create net vlan server_vlan interfaces add { 1.2 { untagged } }
create net self client_ip address 10.1.10.245/24 vlan client_vlan
create net self server_ip address 10.1.20.245/24 vlan server_vlan
create net route def_gw network 0.0.0.0/0 gw 10.1.10.1
Note: "untagged" means this interface carries traffic for only this VLAN (no 802.1Q tagging). In production, you might use tagged interfaces to carry multiple VLANs on a single physical port.
POOL AND VIRTUAL SERVER:
create ltm pool www_pool members add { 10.1.20.11:80 10.1.20.12:80 10.1.20.13:80 } monitor http
create ltm virtual www_vs destination 10.1.10.100:80 pool www_pool ip-protocol tcp source-address-translation { type automap }
Note: "ip-protocol tcp" is critical and easily forgotten. Without it, the virtual server won't match TCP traffic. The "monitor http" on the pool means the BIG-IP will send HTTP GET requests to each member to verify it's responding.
SAVE:
save sys config - writes running config to /config/bigip.conf
save sys ucs lab1-base-config - creates a UCS archive backup
POST-LAB RECOMMENDATION
After the course, students should re-run this entire lab using ONLY TMSH (no GUI verification until the very end). This builds the muscle memory needed for:
- The exam (which may show TMSH command output you need to interpret)
- Real-world troubleshooting (SSH access when the GUI is unreachable)
- Automation workflows (scripts that use TMSH or tmsh-equivalent API calls)
F5 TMSH REFERENCE
Full TMSH reference: https://techdocs.f5.com/en-us/bigip-14-1-0/bigip-tmsh-reference.html

## Slide 19
F5CTSLTM2.01 | U/A | Determine config objects to deploy an application
F5CTSLTM2.02 | U/A | Choose correct profiles and settings for requirements
F5CTSLTM2.04 | U/A | Architect multi-tier applications using LTM
F5CTSLTM2.10 | A/E | Determine appropriate profile setting modifications
F5CTSLTM3.01 | U/A | Given iRule functionality, determine profiles needed
F5CTSLTM3.05 | A/E | Given traffic + iRule, predict the result
LAB 2
Profiles
Profile types, inheritance, protocol/service/persistence/SSL profiles,
multi-tier placement, HTTP optimization, and iRule dependencies.
75 min | 30 min slides + 45 min lab
Notes: WHAT THIS SLIDE TEACHES
This is the section opener for Lab 2: Profiles — the most content-dense lab in the entire course. It maps six Beta objectives across two exams (F5CTSLTM2-B and F5CTSLTM3-B), including two at the highest cognitive level (A/E). The slide establishes the scope, pacing, and objective coverage for everything that follows.
FULL TECHNICAL EXPLANATION
Lab 2 is where students transition from infrastructure (Lab 1: VLANs, self IPs, pools, virtual servers) to application intelligence (profiles that define HOW the BIG-IP processes traffic). Profiles are the primary mechanism for adding features to the BIG-IP's traffic processing pipeline. Without profiles, the BIG-IP is just a packet forwarder. With profiles, it becomes an application delivery controller.
The lab covers four activities:
1. Working with Profiles — Build secure_vs, discover profile dependencies through deliberate failures
2. Application Acceleration — TCP Express, RamCache, HTTP Compression
3. Securing Web Applications — Custom HTTP profile with fallback host, error cloaking, cookie encryption
4. Using iRules — HTTP-to-HTTPS redirect, profile dependency lesson
BETA BLUEPRINT MAPPING
- F5CTSLTM2.01 (U/A): "Determine which configuration objects are necessary to deploy an application." Students build a secure VS and discover which profiles are required vs optional.
- F5CTSLTM2.02 (U/A): "Choose correct profiles and settings to fit application requirements." Covers TCP, HTTP, SSL, compression, caching, persistence, OneConnect.
- F5CTSLTM2.04 (U/A): "Determine how to architect and deploy multi-tier applications using LTM." The three-tier slide covers SNAT/persistence/SSL placement per tier.
- F5CTSLTM2.10 (A/E): "Given a scenario, determine the appropriate profile setting modifications." Compression vs caching scenario.
- F5CTSLTM3.01 (U/A): "Given iRule functionality, determine profiles and configuration options." iRule HTTP profile dependency.
- F5CTSLTM3.05 (A/E): "Given traffic and configuration containing a simple iRule, determine the result." Predict redirect behavior.
COMMON STUDENT MISTAKES
- Trying to rush through the concept slides to get to the lab. The concept slides establish the profile dependency model that makes the lab exercises make sense.
- Not understanding that profiles are hierarchical — protocol profiles are the foundation, service profiles build on them.
F5 DOCUMENTATION
- Profile overview: https://my.f5.com/manage/s/article/K23843660
- BIG-IP LTM Profiles Reference: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-profiles-reference.html
EXAM QUESTION PATTERNS
The exam will show a scenario (application requirements) and ask which profiles are needed. It will also show an iRule and ask which profiles must be present for it to work. Understanding the dependency chain is the key to answering both types.

## Slide 20
20 © 2026 F5
Profile types and inheritance
Profiles define how the BIG-IP processes traffic. Custom profiles inherit from parent defaults.
Protocol
TCP, UDP, FastL4
Layer 4 transport
Service
HTTP, FTP, DNS
Layer 7 intelligence
Persistence
Cookie, Source, SSL
Session affinity
SSL
Client-SSL, Server-SSL
Encryption handling
Other
OneConnect, Stream
Advanced features
Inheritance model
Default parent (tcp)
▼
Custom child (my-tcp)
Never modify defaults directly
Changes lost on upgrade. Create custom child profiles and override only what you need.
HTTP profile is the universal dependency
Required for: cookie persistence, compression, caching, OneConnect, iRules (HTTP:: commands), XFF, response header scrubbing.
The next four slides break down each profile category. Understand what each provides and its dependencies. Every Layer 7 feature traces back to the TCP profile as the foundation.
Notes: WHAT THIS SLIDE TEACHES
This slide is the roadmap for all profile work in the BIG-IP. It introduces two foundational concepts: (1) profiles are organized into five categories that map to different layers of the network stack, and (2) profiles use a parent/child inheritance model where custom profiles inherit settings from default parents.
FULL TECHNICAL EXPLANATION
BIG-IP profiles are configuration templates that define how the system processes traffic for a specific function. Every virtual server needs at minimum ONE protocol profile (TCP, UDP, or FastL4). Additional profiles layer on more intelligence.
THE FIVE PROFILE CATEGORIES:
1. PROTOCOL (Layer 4): TCP, UDP, FastL4, SCTP. Controls transport-layer behavior. Every VS must have exactly one. TCP enables full proxy mode (two independent connections). FastL4 is pass-through (one connection, no L7).
2. SERVICE (Layer 7): HTTP, FTP, DNS, HTTP/2, SMTP, SIP. Adds application-layer intelligence. Each requires a TCP protocol profile underneath because the BIG-IP must terminate the TCP connection to inspect the application payload. The HTTP profile is the most important — it's required by virtually every other L7 feature.
3. PERSISTENCE: Cookie Insert, Source Address, SSL Session ID, Universal, Destination Address, Hash. Ensures clients return to the same pool member for session duration. Different types have different profile dependencies (cookie requires HTTP; source address works with any protocol).
4. SSL: Client-SSL (terminates client encryption, BIG-IP acts as SSL server) and Server-SSL (re-encrypts to backend, BIG-IP acts as SSL client). Three modes: pass-through (no SSL profiles), offload (Client-SSL only), re-encryption (both).
5. OTHER: OneConnect (server-side connection reuse), Stream (content replacement), Statistics, Request Logging, Rewrite, HTML. Advanced features for specific use cases.
INHERITANCE MODEL — PARENT/CHILD:
Every profile has a parent. Default profiles (provided by F5) are the root parents. When you create a custom profile, you select a parent and then override only the settings you need to change. Everything else inherits from the parent automatically.
Why this matters:
- Software upgrades may change default profile values. Your custom overrides are preserved, and you automatically get the new defaults for settings you didn't override.
- If you modify the DEFAULT profile directly, your changes are lost on upgrade because the upgrade replaces default profiles.
- A custom profile can inherit from another custom profile (grandchild pattern). Useful for managing variations: base-http → secure-http → api-http.
TMSH example:
create ltm profile tcp my-wan-tcp defaults-from tcp-wan-optimized { idle-timeout 600 }
This creates a custom TCP profile that inherits everything from tcp-wan-optimized but overrides idle-timeout to 600 seconds.
THE HTTP PROFILE AS UNIVERSAL DEPENDENCY:
The HTTP profile is required for: cookie persistence, HTTP compression, Web Acceleration (RamCache), OneConnect, iRules using HTTP:: commands, X-Forwarded-For insertion, response header scrubbing, HTTP-to-HTTPS redirect. Without it, the BIG-IP treats traffic as an opaque TCP byte stream.
COMMON STUDENT MISTAKES
- Modifying the default TCP or HTTP profile instead of creating a custom child. This works in the lab but causes problems in production when software is upgraded.
- Assuming all profiles are optional. The protocol profile is REQUIRED — a VS without one won't process traffic.
- Not understanding that adding an HTTP profile to an existing VS requires a TCP profile first. FastL4 and HTTP are mutually exclusive — you can't add HTTP to a Performance (Layer 4) VS.
PIVOT QUESTION
"You create a custom HTTP profile that inherits from the default 'http' parent. You change the XFF setting to Enabled. Later, F5 releases a software update that changes a default HTTP setting for security. What happens to your custom profile?"
ANSWER: Your custom profile keeps XFF Enabled (your override is preserved) AND automatically gets the new security setting (because it inherits from the updated default parent for everything you didn't override). This is why inheritance is powerful — you get the benefits of F5's updates without losing your customizations.
F5 DOCUMENTATION
- Profile overview: https://my.f5.com/manage/s/article/K23843660
- Profile management best practices: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-profiles-reference.html
- Custom profile creation: https://my.f5.com/manage/s/article/K13637
EXAM QUESTION PATTERNS
- "Which profile type is required on every virtual server?" → Protocol (TCP, UDP, or FastL4)
- "What happens to custom profile settings during a software upgrade?" → Custom overrides are preserved; inherited defaults update automatically
- "A VS has a TCP profile. Which additional profile is needed before you can add cookie persistence?" → HTTP profile

## Slide 21
21 © 2026 F5
Protocol profiles: TCP vs UDP vs FastL4
The transport-layer foundation. Every virtual server requires exactly one protocol profile.
 | TCP (full proxy) | UDP | FastL4
Processing | Terminates + re-initiates connections (two independent sessions) | Datagram forwarding with session tracking | Packet-by-packet pass-through, minimal state
L7 features | All: HTTP, SSL, compression, caching, iRules, persistence | Limited: DNS profile, basic iRules | None: no L7 inspection possible
Optimization | TCP Express: wan-optimized (client) + lan-optimized (server) | Buffer tuning | Idle timeout, loose initiation, PVA acceleration
Performance | Moderate (full proxy overhead, most CPU per conn) | Moderate | Highest throughput, lowest CPU
Use case | Web apps, APIs, any app needing L7 intelligence | DNS, syslog, RADIUS, TFTP | Non-HTTP L4 LB, high throughput, nPath
TCP Express
Apply tcp-wan-optimized on client side (larger buffers, delayed ACKs, Nagle enabled) and tcp-lan-optimized on server side (smaller buffers, Nagle disabled). Exam tip: know Nagle, idle timeout, and proxy buffer differences between default, WAN, and LAN profiles.
Notes: WHAT THIS SLIDE TEACHES
This slide covers the foundational comparison required by Beta objective F5CTSLTM2.02: "Compare and contrast different communication protocols (TCP, UDP, FastL4)." Students must understand what each protocol profile enables, the trade-offs between features and performance, and how TCP Express optimizes each side of the connection independently.
FULL TECHNICAL EXPLANATION
TCP PROFILE — FULL PROXY ARCHITECTURE
When a TCP profile is applied to a Standard virtual server, the BIG-IP operates as a FULL PROXY:
1. Client sends SYN to VIP → BIG-IP completes the three-way handshake with the client (client-side connection)
2. BIG-IP receives the first data packet from the client
3. If Layer 7 profiles are present (HTTP), BIG-IP waits for enough data to make a load balancing decision
4. BIG-IP initiates a NEW, INDEPENDENT three-way handshake with the selected pool member (server-side connection)
5. These are two completely separate TCP sessions with different sequence numbers, window sizes, and potentially different TCP options
6. The BIG-IP can optimize each side independently — this is the foundation of TCP Express
This full proxy architecture is what enables ALL Layer 7 features. The BIG-IP has a complete, ordered byte stream on each side, which it can inspect, modify, compress, cache, and rewrite.
FASTL4 PROFILE — PACKET-BY-PACKET
FastL4 does NOT terminate the TCP connection:
1. Client sends SYN → BIG-IP forwards it to the selected pool member (with destination NAT)
2. Server responds with SYN-ACK → BIG-IP forwards it back to the client
3. All subsequent packets pass through with minimal processing
4. The BIG-IP maintains basic connection state (to handle SNAT and destination NAT) but does NOT reconstruct the byte stream
Because FastL4 doesn't reconstruct the byte stream, it CANNOT:
- Parse HTTP headers (no HTTP profile)
- Terminate SSL (no Client-SSL/Server-SSL profiles)
- Apply compression or caching
- Use cookie persistence
- Execute iRules that use HTTP:: commands
FastL4 CAN:
- Perform source address persistence (based on IP, not application data)
- Apply rate limiting
- Use PVA (Packet Velocity ASIC) acceleration on hardware BIG-IP platforms for line-rate performance
TCP EXPRESS — SPLIT PROFILE OPTIMIZATION
The key insight: clients connect over WANs (high latency, potential packet loss), while servers are on LANs (low latency, reliable). Optimizing both sides the same way is suboptimal.
tcp-wan-optimized (client side):
- Larger send/receive buffers: 65535 bytes (vs 32768 default)
- Delayed ACKs: Enabled (reduces ACK traffic over WAN)
- Nagle algorithm: ENABLED — batches small writes into larger segments before sending. Reduces packet count over WAN connections where each packet has overhead (TCP/IP headers, SSL framing).
- Idle timeout: 300 seconds
tcp-lan-optimized (server side):
- Smaller buffers: appropriate for low-latency connections
- Nagle algorithm: DISABLED — sends data immediately. On a LAN, latency is already minimal, so Nagle's buffering only adds unnecessary delay.
- Shorter idle timeout
NAGLE ALGORITHM (EXAM CRITICAL):
Nagle buffers small writes (less than MSS) and waits for either: (a) an ACK for previously sent data, or (b) the buffer fills to MSS. This reduces the number of small packets on the wire.
- GOOD for WAN: reduces packet count, improves throughput for bulk transfers
- BAD for LAN: adds ~200ms latency to small responses (API responses, web page fragments)
- Default TCP profile: AUTO (Nagle is conditionally applied)
- tcp-wan-optimized: ENABLED (always buffer small writes)
- tcp-lan-optimized: DISABLED (never buffer, send immediately)
OneConnect (BLUEPRINT SUB-BULLET — not in lab):
OneConnect pools idle server-side TCP connections for reuse across different clients. Instead of opening a new server connection for every client request, the BIG-IP checks if an idle server connection is available and reuses it.
- Requires: TCP + HTTP profiles (must understand HTTP request boundaries)
- Source mask: 0.0.0.0 = all clients share all connections (most aggressive). 255.255.255.255 = each client IP gets its own connections.
- Dramatically reduces TCP socket load on servers — 50,000 client requests/sec might only need a few hundred server connections.
- Not compatible with NTLM authentication without special configuration (K10477).
- Reference: https://my.f5.com/manage/s/article/K7208
COMMON STUDENT MISTAKES
- Applying tcp-wan-optimized on BOTH client and server sides. The server side should use tcp-lan-optimized. Using WAN optimization on the LAN side adds Nagle latency to server responses.
- Thinking FastL4 is "better" because it's faster. FastL4 is only appropriate when you don't need L7 features. For web applications, TCP is almost always required.
- Confusing "full proxy" with "forward proxy." Full proxy means two independent TCP connections. Forward proxy is a deployment mode (explicit proxy in the HTTP profile).
PIVOT QUESTION
"You apply tcp-wan-optimized on both client and server sides of a virtual server. A developer complains that small API responses take 200ms longer than expected. What's the most likely cause and how do you fix it?"
ANSWER: The tcp-wan-optimized profile has Nagle algorithm ENABLED. On the server side (LAN), Nagle buffers small API responses (~200 bytes) and waits before sending, adding ~200ms of latency. Fix: Apply tcp-lan-optimized on the server side, which has Nagle DISABLED, sending data immediately.
F5 DOCUMENTATION
- TCP profiles: https://my.f5.com/manage/s/article/K23843660
- TCP Express overview: https://my.f5.com/manage/s/article/K3422
- Nagle algorithm: https://my.f5.com/manage/s/article/K7535
- FastL4 profile: https://my.f5.com/manage/s/article/K55185917
- OneConnect: https://my.f5.com/manage/s/article/K7208
EXAM QUESTION PATTERNS
- "Compare TCP and FastL4 virtual server types" → TCP = full proxy, all L7 features, higher CPU. FastL4 = pass-through, no L7, highest performance.
- "Which Nagle setting is appropriate for the server side?" → DISABLED (tcp-lan-optimized)
- "What profile enables server-side connection reuse?" → OneConnect (requires TCP + HTTP)

## Slide 22
22 © 2026 F5
Service profiles
Layer 7 application intelligence. Each requires a TCP protocol profile underneath.
Profile | What it does | Key features | When to use
HTTP | Parses HTTP requests/responses, enables header inspection and modification | XFF, response cloaking, redirect, cookie handling, chunking, proxy modes (reverse/explicit/transparent) | Any web application. Required dependency for compression, caching, OneConnect, cookie persistence
FTP | Manages FTP control and data channel split | Translates PORT/PASV commands, handles data channel NAT across BIG-IP | Load balancing FTP servers. Without it, data channel connections fail through BIG-IP
DNS | DNS-aware processing of queries and responses | DNS caching, DNSSEC validation, DNS express, rapid response mode | DNS load balancing, DNS proxy, GTM/DNS integration
HTTP/2 | Enables HTTP/2 on client or server side | Multiplexed streams, header compression, server push. Can translate HTTP/2 to HTTP/1.1 | Modern web apps where clients support HTTP/2 but servers don't
OneConnect | Pools idle server-side TCP connections for reuse across clients | Source mask controls sharing granularity. Reduces server TCP socket load dramatically | High connection-rate web apps. Requires TCP + HTTP. Not compatible with NTLM without special config
HTTP Compression and Web Acceleration are also service-type profiles but covered on slide 26. Both require the HTTP profile. Compression reduces bytes on the wire (CPU cost). Caching serves repeat requests from BIG-IP RAM (memory cost). They can be combined.
Notes: WHAT THIS SLIDE TEACHES
Service profiles add Layer 7 (application-layer) intelligence to the BIG-IP's traffic processing. They ALL require a TCP protocol profile underneath because the BIG-IP must terminate the TCP connection (full proxy) to inspect the application payload. This slide addresses F5CTSLTM2.02 sub-bullets about determining which profiles are needed and deploying OneConnect.
FULL TECHNICAL EXPLANATION
HTTP PROFILE — THE MOST IMPORTANT SERVICE PROFILE
The HTTP profile enables the BIG-IP to parse HTTP requests and responses at the application layer. Without it, the BIG-IP treats traffic as an opaque TCP byte stream — it can see bytes flowing but cannot interpret them as HTTP.
When the HTTP profile is applied, the BIG-IP can:
- Parse request headers: Host, URI, User-Agent, Cookie, Accept-Encoding, X-Forwarded-For
- Parse response headers: Content-Type, Set-Cookie, Server, Content-Encoding
- Insert/modify/remove headers in both directions
- Handle chunked transfer encoding (reassemble and re-chunk)
- Support HTTP pipelining and request/response pairing
- Enable all downstream HTTP-dependent features
HTTP profile has three proxy modes (Table 5.3 in F5 docs):
1. Reverse (default): BIG-IP manages responses from multiple backend servers. This is standard load balancing mode.
2. Explicit: BIG-IP acts as an HTTP forward proxy. Browser is configured to send all HTTP requests to the BIG-IP, which evaluates them against policies and either forwards or denies. Requires a DNS resolver configuration.
3. Transparent: BIG-IP forwards invalid HTTP traffic to a specified server instead of dropping the connection. Used in service provider environments where non-standard HTTP clients exist.
FTP PROFILE — CONTROL/DATA CHANNEL HANDLING
FTP uses two TCP connections: a control channel (port 21) for commands (LIST, GET, PUT) and a data channel (dynamic port) for actual file transfers. The FTP profile understands the PORT and PASV commands that negotiate the data channel.
Without the FTP profile, the BIG-IP doesn't translate the IP addresses in PORT/PASV commands as they cross the NAT boundary. Result: the control channel works (authentication succeeds) but file transfers fail because the data channel connection can't be established.
Lab connection: Students used an FTP virtual server in Lab 1's SNAT exercise. The FTP profile was applied there.
DNS PROFILE
Required when the BIG-IP needs to understand DNS queries at the application layer. Enables:
- DNS caching: BIG-IP caches DNS responses and serves them for subsequent queries
- DNSSEC validation: BIG-IP validates DNSSEC signatures
- DNS Express: BIG-IP acts as an authoritative DNS server for specific zones
- Works with UDP (most DNS) or TCP (zone transfers, large responses)
OneConnect PROFILE (BLUEPRINT SUB-BULLET)
This is explicitly called out in F5CTSLTM2.02: "Identify LTM profile settings to deploy OneConnect." It is NOT in any lab, so this slide and the checkpoint questions are the only coverage.
How OneConnect works step-by-step:
1. Client A sends request → BIG-IP opens server connection to pool member → response delivered → server connection goes idle
2. Client B sends request → BIG-IP checks for idle server connections → finds the one from step 1 → reuses it instead of opening a new connection
3. Result: many clients share a small pool of server connections
Source mask: Controls which clients can share connections.
- 0.0.0.0: All clients share all connections (most aggressive reuse, best performance)
- 255.255.255.255: Each client IP gets its own connections (no sharing, least benefit)
- Common compromise: 255.255.255.0 (clients from same /24 subnet share)
Limitations:
- Requires TCP + HTTP profiles
- NOT compatible with NTLM authentication (connection-based auth) without the NTLM profile (K10477)
- Pool member cannot rely on client IP in network headers — use XFF to pass client IP
COMMON STUDENT MISTAKES
- Forgetting that FTP requires the FTP profile. They configure FTP load balancing with just TCP and wonder why file transfers fail.
- Not understanding that OneConnect changes the relationship between client connections and server connections. With OneConnect, one server connection may serve requests from many different clients.
- Thinking HTTP/2 replaces HTTP — it doesn't. HTTP/2 is an additional profile that works alongside the HTTP profile.
PIVOT QUESTION
"You configure a web application with TCP + HTTP profiles. The application uses NTLM (Windows Integrated Authentication). Users report authentication failures when OneConnect is enabled. Why?"
ANSWER: NTLM authentication is connection-based — the authentication state is tied to the specific TCP connection. OneConnect reuses server connections across different clients. When Client B's request is sent over a connection that Client A authenticated, the server sees it as Client A's session. Fix: Either disable OneConnect for this VS, or use the NTLM profile which is designed to handle connection-based auth with connection pooling (K10477).
F5 DOCUMENTATION
- HTTP profile: https://my.f5.com/manage/s/article/K4707
- HTTP proxy modes: https://my.f5.com/manage/s/article/K23843660
- FTP profile: https://my.f5.com/manage/s/article/K8024
- OneConnect: https://my.f5.com/manage/s/article/K7208
- NTLM and OneConnect: https://my.f5.com/manage/s/article/K10477
- HTTP/2 profile: https://my.f5.com/manage/s/article/K04412053
EXAM QUESTION PATTERNS
- "Which profile is required before cookie persistence can be enabled?" → HTTP
- "What profile is needed when load balancing FTP servers?" → FTP (in addition to TCP)
- "How does OneConnect reduce server load?" → Reuses idle server connections across clients
- "A VS has TCP + HTTP + OneConnect. Users report authentication failures with NTLM. What's the cause?" → OneConnect breaks connection-based auth; use NTLM profile

## Slide 23
23 © 2026 F5
Persistence profiles
Ensure clients return to the same pool member for the duration of a session
Type | How it works | Requires | Best for | Limitation
Cookie insert | BIG-IP inserts cookie (BIGipServer*) in server response. Client sends it back. | TCP + HTTP | Web apps (most common) | HTTP only. Encrypt cookie for security (K6917).
Source address | Persists based on client source IP. Configurable mask. | Any protocol | Non-HTTP, simple deployments | Clients behind shared NAT get same member.
SSL session ID | Persists based on SSL session ID, survives IP changes. | Client-SSL | SSL pass-through | Unreliable with TLS 1.3 / frequent renegotiation.
Universal | iRule generates custom persistence key from traffic data. | TCP + iRule | Custom protocols, SIP | Requires iRule development.
Dest address | Persists by destination IP. Routes to same member. | Any protocol | Outbound LB (dual WAN) | Not for application LB.
Cookie insert is the recommended default for web applications.
It survives client IP changes (mobile roaming, VPN failover), provides per-session granularity, and doesn't require the BIG-IP to maintain a persistence table in memory. Always encrypt the cookie (HTTP profile > Encrypt Cookies) to prevent information disclosure — the default BIGipServer cookie encodes pool member IP and port (K6917).
Notes: WHAT THIS SLIDE TEACHES
Persistence (session affinity) ensures a client is consistently directed to the same pool member for the duration of a session. This is critical for stateful applications where the server maintains session data. This slide covers five persistence types with their requirements, use cases, and limitations, supporting F5CTSLTM2.01 (understand dependencies) and F5CTSLTM2.02 (choose correct settings).
FULL TECHNICAL EXPLANATION
COOKIE INSERT (most common, recommended default):
When a client first connects, the BIG-IP makes a load balancing decision and selects a pool member. On the server's response, the BIG-IP inserts an additional Set-Cookie header: Set-Cookie: BIGipServerwww_pool=1234567890.20480.0000; path=/
The cookie value encodes the pool member's IP address and port number. On subsequent requests, the client sends this cookie, and the BIG-IP decodes it to route directly to the same pool member without making a new load balancing decision.
Cookie methods:
- Cookie Insert (default): BIG-IP adds cookie. Server doesn't need to know about it. Most common.
- Cookie Passive: Server sets the cookie. BIG-IP reads it. Requires server-side configuration.
- Cookie Rewrite: BIG-IP rewrites an existing server cookie. Requires collaboration with app team.
SECURITY WARNING: The default BIGipServer cookie encodes the pool member IP:port in a predictable format. An attacker can decode it to discover internal server IPs. Always enable cookie encryption in the HTTP profile: HTTP profile > Cookie Encryption section. Reference: K6917 (https://my.f5.com/manage/s/article/K6917) and K14784 for encryption configuration.
SOURCE ADDRESS AFFINITY:
Persists based on the source IP address of the client. Default mask: 255.255.255.255 (one record per IP). Configurable to wider masks (e.g., 255.255.0.0 groups all clients from same /16).
Timeout: 180 seconds default. After this idle time, the persistence record expires and the next request gets a fresh load balancing decision.
Limitation: Clients behind corporate NAT/proxy all share the same source IP → they all persist to the same pool member → uneven distribution. This is why cookie persistence is preferred for web applications.
Memory impact: The BIG-IP maintains a persistence table in memory. Each source address record consumes memory. High-traffic environments with many unique IPs can consume significant memory. Reference: K5779.
SSL SESSION ID:
Tracks the SSL session ID to persist clients, even if their IP address changes between requests. Useful when the BIG-IP doesn't terminate SSL (pass-through mode with FastL4) — in this case, there's no HTTP layer available for cookie persistence.
Limitation: Modern browsers (especially with TLS 1.3) frequently renegotiate sessions, which generates new session IDs and breaks persistence. TLS 1.3 uses a different session resumption mechanism (PSK) that may not be compatible with traditional SSL session ID persistence. This makes SSL session ID persistence increasingly unreliable for modern web traffic.
Reference: K3062 (https://my.f5.com/manage/s/article/K3062)
UNIVERSAL PERSISTENCE:
The most flexible method. You write an iRule that extracts any piece of data from the traffic and uses it as the persistence key. The iRule calls the "persist uie" command with the extracted value.
Example — persist on a custom HTTP header:
when HTTP_REQUEST {
if { [HTTP::header exists "X-Session-ID"] } {
persist uie [HTTP::header "X-Session-ID"]
}
}
Use cases: SIP Call-ID persistence, custom application session tokens, RADIUS Calling-Station-ID.
DESTINATION ADDRESS AFFINITY:
Persists based on the DESTINATION IP, not the source. All traffic to the same destination IP goes to the same pool member. Used for outbound load balancing (dual WAN circuits) or proxy chaining, NOT for application load balancing.
PERFORMANCE COMPARISON:
- Cookie insert: No server-side state table (cookie carries data). Most memory-efficient. Slight increase in HTTP response size (one additional Set-Cookie header).
- Source address: BIG-IP maintains persistence table. Each record consumes ~80 bytes. 100,000 unique clients = ~8MB.
- SSL session ID: BIG-IP maintains table. Session IDs can be large.
- Universal: Depends on key size and iRule complexity.
COMMON STUDENT MISTAKES
- Adding cookie persistence to a VS without an HTTP profile → fails silently. Cookies are HTTP-layer objects.
- Assuming source address persistence uniquely identifies clients → fails behind NAT/proxy.
- Using SSL session ID persistence with modern browsers → unreliable due to TLS 1.3 changes.
- Not encrypting the BIGipServer cookie → information disclosure vulnerability.
PIVOT QUESTION
"A client accesses your web application from a mobile phone on cellular data, then switches to WiFi. Their IP address changes. Which persistence method survives the IP change?"
ANSWER: Cookie insert. The cookie is stored in the browser and sent with every HTTP request regardless of the network interface. Source address persistence would break because the source IP changed. SSL session ID might survive if the TLS session is maintained, but it's unreliable with modern browsers.
F5 DOCUMENTATION
- Cookie persistence: https://my.f5.com/manage/s/article/K6917
- Cookie encryption: https://my.f5.com/manage/s/article/K14784
- Source address persistence: https://my.f5.com/manage/s/article/K5779
- SSL session ID: https://my.f5.com/manage/s/article/K3062
- Persistence overview: https://my.f5.com/manage/s/article/K23843660
EXAM QUESTION PATTERNS
- "Which persistence method works with any protocol profile?" → Source address
- "Which persistence survives client IP changes?" → Cookie insert
- "What dependency does cookie persistence have?" → HTTP profile (plus TCP)
- "Why might source address persistence cause uneven distribution?" → Clients behind NAT share one IP

## Slide 24
24 © 2026 F5
SSL profiles: offload vs re-encryption
Control how the BIG-IP handles encrypted traffic on each side of the connection
SSL pass-through
No SSL profiles
BIG-IP passes encrypted traffic without decryption. Cannot inspect or modify content. Use FastL4 for best performance.
No L7 features
No HTTP inspection
Highest performance
SSL offload
Client-SSL only
BIG-IP decrypts client traffic. Server-side is unencrypted. Offloads CPU-intensive SSL from servers.
Full L7 features
Client ↔ BIG-IP: encrypted
BIG-IP ↔ Server: plain HTTP
SSL re-encryption
Client-SSL + Server-SSL
BIG-IP decrypts, inspects, then re-encrypts to server. End-to-end encryption with L7 intelligence.
Full L7 features
Client ↔ BIG-IP: encrypted
BIG-IP ↔ Server: encrypted
Key SSL profile settings: Certificate + Key (must match), Chain cert (intermediate CA), Ciphers (cipher string), Options (disable SSLv3/TLS 1.0), Client Authentication (mutual TLS). Server-SSL can include client cert for backend auth.
Notes: WHAT THIS SLIDE TEACHES
This slide covers the three SSL deployment modes on the BIG-IP. Students must understand when to use each mode and the trade-offs between security, performance, and feature availability. This directly supports profile selection in multi-tier architectures (next slide) and the SSL lab exercises in Lab 5.
FULL TECHNICAL EXPLANATION
SSL PASS-THROUGH (No SSL profiles):
The BIG-IP does not decrypt traffic. It forwards encrypted packets between client and server without inspecting the content. The BIG-IP acts as a Layer 4 load balancer for HTTPS traffic.
- Use a FastL4 protocol profile for maximum performance
- Cannot apply any L7 features: no HTTP inspection, no compression, no caching, no cookie persistence, no iRules using HTTP:: commands
- Only persistence options: source address or SSL session ID
- Use case: When you ONLY need L4 load balancing and servers handle all SSL processing
- TMSH: No ssl profiles assigned to the VS
SSL OFFLOAD (Client-SSL only):
The BIG-IP terminates the client's SSL/TLS connection and sends unencrypted HTTP to the backend server.
- Client → BIG-IP: HTTPS (encrypted)
- BIG-IP → Server: HTTP (unencrypted, port 80)
- BIG-IP holds the SSL certificate and private key
- All L7 features available because BIG-IP can read decrypted HTTP
- Offloads CPU-intensive SSL operations from servers (significant for high-volume HTTPS)
- SECURITY: Server-side connection is unencrypted. Only use on trusted networks (same data center, behind firewall)
- This is the most common SSL configuration in enterprise deployments
SSL RE-ENCRYPTION (Client-SSL + Server-SSL):
BIG-IP terminates client SSL, inspects/modifies HTTP content, then re-encrypts before sending to server.
- Client → BIG-IP: HTTPS (encrypted with client-facing certificate)
- BIG-IP → Server: HTTPS (encrypted with server-facing certificate, may be different)
- Two SSL handshakes per connection: more CPU overhead than offload
- All L7 features available
- Server-SSL profile can optionally include a client certificate for mutual TLS to the backend — ensures servers only accept connections from the BIG-IP
- Use case: Compliance requirements (PCI DSS, HIPAA) mandate end-to-end encryption
KEY SSL PROFILE SETTINGS (from F5 documentation Table 5.5):
- Certificate: The cert BIG-IP presents. Client-SSL = server cert. Server-SSL = optional client cert.
- Key: Must match the certificate. BIG-IP validates at config time.
- Chain: Intermediate CA cert. Required when BIG-IP's cert is signed by an intermediate CA.
- Ciphers: OpenSSL cipher string. Controls which cipher suites are offered/accepted.
- Options: Selectively disable SSL/TLS versions (disable SSLv3, TLS 1.0, TLS 1.1).
- Client Authentication (Client-SSL): Enable mutual TLS — BIG-IP requests a cert from the client.
- Server Authentication (Server-SSL): Validate the server's cert. Usually disabled by default.
COMMON STUDENT MISTAKES
- Adding a Server-SSL profile without a Client-SSL profile. This creates an odd configuration where the client-side is unencrypted but the server-side is encrypted. It works but is rarely intentional.
- Forgetting the chain certificate. If the BIG-IP's cert is signed by an intermediate CA and you don't include the chain, clients may get "untrusted certificate" errors because they can't verify the full certificate chain.
- Thinking SSL offload is insecure. On a controlled data center network behind firewalls, the server-side traffic is already on a trusted segment. SSL offload is the standard practice for most enterprise deployments.
PIVOT QUESTION
"A security audit requires end-to-end encryption AND HTTP header inspection for PCI compliance. Which SSL configuration do you use?"
ANSWER: SSL re-encryption (Client-SSL + Server-SSL). Client-SSL terminates the client's connection so the BIG-IP can inspect HTTP headers. Server-SSL re-encrypts to the backend, maintaining end-to-end encryption. The BIG-IP can apply HTTP profiles, iRules, and compression between the two encrypted segments.
F5 DOCUMENTATION
- Client-SSL profile: https://my.f5.com/manage/s/article/K14783
- Server-SSL profile: https://my.f5.com/manage/s/article/K14806
- SSL offload: https://my.f5.com/manage/s/article/K23843660 (Figure 5.2)
- SSL re-encryption: https://my.f5.com/manage/s/article/K23843660 (Figure 5.3)
- Cipher strings: https://my.f5.com/manage/s/article/K13171
EXAM QUESTION PATTERNS
- "What profiles are needed for end-to-end encryption with L7 inspection?" → TCP + Client-SSL + Server-SSL + HTTP
- "What is the difference between SSL offload and SSL re-encryption?" → Offload = client-side only. Re-encryption = both sides.
- "Which SSL mode provides the highest performance?" → Pass-through (no decryption overhead)
- "What happens if you add an HTTP profile without a Client-SSL profile to an HTTPS VS?" → The BIG-IP cannot parse the encrypted content. HTTP events never fire because the payload is encrypted gibberish.

## Slide 25
25 © 2026 F5
Three-tier application: profile placement
Web front-end, application logic, and database — each tier has different profile requirements
Clients
HTTPS
▶
Web tier VS
TCP (wan/lan-optimized)
Client-SSL
HTTP
Cookie persistence
OneConnect
HTTP Compression
SNAT automap
▶
HTTP
App tier VS
TCP
HTTP
Source addr persistence
SNAT automap
(No SSL — internal
trusted network)
▶
TCP
DB tier VS
FastL4 or TCP
Source addr persistence
SNAT automap
(No HTTP, no SSL
No compression
Long-lived connections)
▶
DB 1
DB 2
Profile placement by tier
Decision | Web tier | App tier | DB tier | Why
Protocol | TCP (wan/lan) | TCP | FastL4 or TCP | DB: high throughput, no L7 needed
SSL | Client-SSL | None | None | Only client-facing tier needs encryption
Persistence | Cookie insert | Source address | Source address | Cookie requires HTTP; internal tiers use source IP
Service | HTTP, Compress, Cache | HTTP (if app uses it) | None | DB tier is raw TCP
SNAT | Automap | Automap or None | Automap or None | Depends on routing between tiers
Notes: WHAT THIS SLIDE TEACHES
This slide directly addresses Beta objective F5CTSLTM2.04 (U/A): "Determine how to architect and deploy multi-tier applications using LTM." Sub-bullets: "Understand connection-based architecture and when/how to apply SNAT/persistence/SSL settings in a multi-tiered environment" and "Identify which device handles specific configuration objects in a multi-tiered deployment."
FULL TECHNICAL EXPLANATION
THREE-TIER ARCHITECTURE — TIER BY TIER
TIER 1: WEB FRONT-END (Client-facing)
Profile stack: TCP (wan/lan-optimized) + Client-SSL + HTTP + Cookie persistence + OneConnect + HTTP Compression + SNAT automap
- Terminates HTTPS from end users (Client-SSL with server certificate)
- Full HTTP processing: content switching, header manipulation, compression
- Cookie persistence for per-session user affinity
- OneConnect to reduce TCP connection overhead on web servers
- HTTP Compression for bandwidth reduction
- SNAT automap because web servers typically don't gateway through the BIG-IP
TIER 2: APPLICATION LOGIC (Internal)
Profile stack: TCP + HTTP (if app uses HTTP) + Source address persistence + SNAT automap
- No SSL: traffic is on a trusted internal VLAN. Adding SSL wastes CPU with no security benefit.
- Source address persistence: the "client" at this tier is the web server or Tier 1 BIG-IP, not the end user. Cookie persistence is possible if HTTP is available but source address is simpler.
- HTTP profile: only if the application protocol between web and app servers is HTTP/REST. Some apps use proprietary binary protocols — no HTTP profile in that case.
TIER 3: DATABASE (Backend)
Profile stack: FastL4 or TCP + Source address persistence + SNAT automap
- FastL4 preferred: database connections are long-lived and don't need L7 inspection. FastL4 provides highest throughput with lowest overhead.
- No HTTP: database protocols (MySQL 3306, PostgreSQL 5432, MSSQL 1433, Oracle 1521) are NOT HTTP.
- No SSL: internal traffic. If compliance requires encrypted DB connections, handle it at the application/DB level (MySQL SSL, PostgreSQL sslmode).
- No compression: binary protocols don't benefit from HTTP compression.
- Idle timeout: must be set LONGER than default for database connections. DB connections can be idle for minutes during batch processing. Default 300 seconds may be too short.
CRITICAL CONCEPT: SNAT + PERSISTENCE CASCADE
When Tier 1 uses SNAT automap, ALL traffic to Tier 2 appears to come from the BIG-IP's self IP (not the original client IPs). This means:
- Tier 2 source address persistence sees ONE source IP for ALL users → all users persist to the same app server → defeats load balancing
- If Tier 2 also uses SNAT, the same problem cascades to Tier 3
Solutions:
1. Cookie persistence at Tier 2 (if HTTP is available)
2. Universal persistence at Tier 2 using XFF header from Tier 1
3. Eliminate SNAT at Tier 1 (change web server routing to gateway through BIG-IP)
4. Insert a custom header at Tier 1 via iRule with a unique client identifier
COMMON STUDENT MISTAKES
- Applying the same profile stack to all tiers. Each tier has different requirements.
- Adding HTTP profile to the database tier VS. Database protocols are not HTTP — an HTTP profile would attempt to parse MySQL/PostgreSQL packets as HTTP and fail.
- Setting idle timeout too low on the DB tier. Long-running queries and connection pools keep connections idle for extended periods.
PIVOT QUESTION
"Your three-tier app works, but monitoring shows all database connections go to DB1 while DB2 is idle. Tier 2 uses SNAT automap and Tier 3 uses source address persistence. What's the root cause?"
ANSWER: Tier 2 SNAT automap makes all traffic to Tier 3 appear from the same source IP (BIG-IP self IP). Tier 3 source address persistence maps this single IP to DB1. Fix: remove SNAT on Tier 2 (if routing allows), or change Tier 3 to round robin (if app handles it), or use a more granular persistence method.
F5 DOCUMENTATION
- Multi-tier deployment: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-implementations.html
- Connection architecture: https://my.f5.com/manage/s/article/K23843660
EXAM QUESTION PATTERNS
- "In a three-tier deployment, which tier terminates SSL?" → Tier 1 (web front-end)
- "Why would you use FastL4 on the database tier?" → No L7 inspection needed, highest throughput
- "What happens when SNAT automap is used at Tier 1 with source address persistence at Tier 2?" → All traffic appears from one IP, breaking persistence distribution

## Slide 26
26 © 2026 F5
HTTP optimization: compression vs caching
Two approaches to accelerating web applications — choose based on content type and access patterns
HTTP compression
How: BIG-IP compresses each response before sending to client.
Best for: Dynamic content (APIs, HTML) that changes too often to cache.
Cost: CPU — every response compressed on the fly.
Profile: wan-optimized-compression
Web Acceleration (RamCache)
How: BIG-IP caches responses in RAM. Subsequent requests served from cache.
Best for: Static content (images, CSS, JS) that doesn't change frequently.
Cost: RAM — cached content consumes BIG-IP memory.
Profile: optimized-caching
Both require HTTP profile. Can be combined: BIG-IP caches the compressed response. Subsequent requests get compressed content from cache without re-compressing or contacting the server. Images (JPEG, PNG) are already compressed — compression won't help them. Use RamCache for static images instead.
Notes: WHAT THIS SLIDE TEACHES
This slide addresses Beta objective F5CTSLTM2.10 (A/E): "Given a scenario, determine the appropriate profile setting modifications." Students must understand when to apply compression, when to apply caching, and when to use both. This is an Analyze/Evaluate level objective — the exam presents scenarios requiring judgment.
FULL TECHNICAL EXPLANATION
HTTP COMPRESSION — STEP BY STEP
1. Client sends request with header "Accept-Encoding: gzip, deflate" (browser supports compression)
2. BIG-IP forwards request to server (removes Accept-Encoding so server sends uncompressed response)
3. Server responds with uncompressed content (e.g., 50KB HTML page)
4. BIG-IP compresses the response body using gzip (50KB → 12KB)
5. BIG-IP sends compressed response to client with "Content-Encoding: gzip" header
6. Client browser transparently decompresses and renders the content
Key profile settings (wan-optimized-compression):
- Content Type Include: text/html, text/css, application/javascript, application/json (compressible text types)
- Content Type Exclude: image/jpeg, image/png, video/* (already compressed, would waste CPU)
- Minimum Content Length: Don't compress tiny responses (<1KB — compression overhead exceeds savings)
- Gzip Level: 1 (fastest, least compression) to 9 (slowest, most compression). Default: 1. Level 1 provides ~60% size reduction. Level 6 provides ~65%. The extra 5% isn't worth the 3-5x CPU increase. F5 recommends level 1.
- Gzip Memory Level: Controls RAM allocated for compression buffers per connection
WEB ACCELERATION (RAMCACHE) — STEP BY STEP
1. First request for /styles.css → BIG-IP forwards to server → receives response → caches it in RAM → sends to client
2. Second request for /styles.css → BIG-IP checks cache → cache hit → serves directly from RAM → server never contacted
3. Cache entry expires based on HTTP Cache-Control/Expires headers from server, or the profile's Maximum Age setting
Key profile settings (optimized-caching):
- Cache Size: Maximum RAM in MB for cached content. Default: 100MB. Monitor with: show ltm profile ramcache [name]
- Maximum Entries: Maximum number of cached objects
- Maximum Object Size: Largest response to cache (don't cache multi-MB files)
- Cache Aging Rate: Multiplier for expiration acceleration/deceleration
- URI Include/Exclude: Control which URIs are cached
WHEN TO USE WHICH
Dynamic content (login pages, API responses, personalized dashboards) → Compression only. Caching would serve stale/wrong data to users.
Static content (images, CSS, JS, fonts) → Caching. Eliminates server round-trips entirely for cache hits.
Mixed content (typical web app) → Both. The BIG-IP caches the compressed version — most efficient.
COMBINED: When both are enabled, the BIG-IP compresses the response on the first request and caches the COMPRESSED version. Subsequent cache hits serve the pre-compressed content without re-compressing or contacting the server. This provides both bandwidth reduction AND server offload.
IMAGES ARE ALREADY COMPRESSED
JPEG, PNG, GIF, and WebP are already compressed formats. Attempting to gzip them wastes CPU cycles and can actually increase the file size slightly (gzip overhead on incompressible data). The wan-optimized-compression profile's Content Type Include list does NOT include image types by default — but verify this.
For images, use RamCache instead — caching eliminates the server round-trip without attempting futile compression.
COMMON STUDENT MISTAKES
- Enabling compression and expecting images to load faster. Images are already compressed.
- Setting gzip level to 9 thinking "maximum compression is best." Level 1 provides 95% of the benefit at 20% of the CPU cost.
- Forgetting that both profiles require HTTP. Without HTTP, the BIG-IP can't parse HTTP responses to compress or cache them.
- Not checking cache statistics. Students enable caching but don't verify it's working: show ltm profile ramcache [name]
PIVOT QUESTION
"Client reports images load slowly but HTML pages render quickly. The VS has TCP + HTTP + wan-optimized-compression. What do you evaluate first?"
ANSWER: Images (JPEG, PNG) are already compressed formats. The compression profile doesn't help them. The slow loading is a bandwidth issue, not a compression issue. Recommendation: Enable Web Acceleration (RamCache) for static image content. Cached images are served from BIG-IP memory, eliminating server round-trips. Also verify images are excluded from compression Content-Type list (they should be by default).
F5 DOCUMENTATION
- HTTP Compression profile: https://my.f5.com/manage/s/article/K15434
- Web Acceleration profile: https://my.f5.com/manage/s/article/K14903
- show ltm profile ramcache: https://my.f5.com/manage/s/article/K14260
- Gzip levels: https://my.f5.com/manage/s/article/K15270
EXAM QUESTION PATTERNS
- "Which profile reduces bandwidth for dynamic content?" → HTTP Compression
- "Which profile eliminates server load for static content?" → Web Acceleration (RamCache)
- "Both require which profile as a prerequisite?" → HTTP
- "Can they be combined?" → Yes, cached content is stored pre-compressed

## Slide 27
27 © 2026 F5
Three essential iRules patterns
These three patterns solve the most common application delivery problems. All require TCP + HTTP profiles.
1
HTTP-to-HTTPS redirect
when HTTP_REQUEST {
HTTP::redirect \
https://[HTTP::host][HTTP::uri]
}
Redirects all HTTP traffic to HTTPS. Apply to a separate port-80 VS with no pool — traffic goes nowhere except back to the client as a 302 redirect.
2
URI-based content switching
when HTTP_REQUEST {
switch -glob [HTTP::uri] {
"/api/*" { pool api_pool }
"/images/*" { pool static_pool }
default { pool web_pool }
}
}
Routes requests to different pools based on URI path. API calls go to api_pool, static assets to static_pool, everything else to web_pool. The switch -glob enables wildcard matching. This is one of the most common production iRules.
3
HTTP header insertion
when HTTP_REQUEST {
HTTP::header insert "X-Client-IP" \
[IP::client_addr]
}
Inserts a custom header with original client IP. Useful when XFF isn't sufficient or for passing client metadata to the server. Can also insert X-Request-ID for tracing, or remove headers on responses using HTTP_RESPONSE.
Notes: WHAT THIS SLIDE TEACHES
This slide covers three Beta objectives: F5CTSLTM3.01 (U/A) — determine profiles needed for an iRule; F5CTSLTM3.04 (U/A) — explain iRule functionality; F5CTSLTM3.05 (A/E) — given traffic + iRule, predict the result. The exam won't ask students to write iRules, but it WILL show iRule code and ask them to predict behavior or identify missing profiles.
FULL TECHNICAL EXPLANATION
ALL THREE iRULES REQUIRE TCP + HTTP profiles. Without HTTP, the HTTP_REQUEST event never fires and all HTTP:: commands fail silently. This is the single most important takeaway.
iRULE 1: HTTP-TO-HTTPS REDIRECT
when HTTP_REQUEST {
HTTP::redirect https://[HTTP::host][HTTP::uri]
}
Step-by-step execution:
1. Client sends HTTP request to port 80: GET / HTTP/1.1, Host: www.example.com
2. BIG-IP receives request on the redirect VS (port 80)
3. HTTP_REQUEST fires — BIG-IP has parsed the request headers
4. HTTP::redirect constructs a 302 redirect response:
- "https://" — new scheme
- [HTTP::host] reads Host header → "www.example.com"
- [HTTP::uri] reads URI path → "/"
- Combined → "https://www.example.com/"
5. BIG-IP sends HTTP 302 response back to client: Location: https://www.example.com/
6. Client browser follows redirect, connects to port 443 (the HTTPS VS)
Deployment pattern:
- Create a SEPARATE VS on port 80 with the same VIP address as the HTTPS VS
- This VS does NOT need a pool (no server-side traffic)
- This VS does NOT need SNAT (no server connection)
- This VS NEEDS: TCP + HTTP + the redirect iRule
- F5 provides _sys_https_redirect iRule pre-built on every BIG-IP
iRULE 2: URI-BASED CONTENT SWITCHING
when HTTP_REQUEST {
switch -glob [HTTP::uri] {
"/api/*" { pool api_pool }
"/images/*" { pool static_pool }
default { pool web_pool }
}
}
Step-by-step execution:
1. Client requests GET /api/v2/users HTTP/1.1
2. HTTP_REQUEST fires
3. [HTTP::uri] returns "/api/v2/users"
4. switch -glob evaluates patterns with wildcard matching
5. "/api/*" matches "/api/v2/users" (wildcard * matches "v2/users")
6. The "pool api_pool" command overrides the VS's default pool for this request
7. BIG-IP load balances the request to a member of api_pool
NOTE: For simple URI-based routing, BIG-IP LTM policies (Local Traffic > Policies) can achieve the same result without iRules. LTM policies are faster and easier to manage. This connects to F5CTSLTM2.11 (A/E): "Evaluate which iRules can be replaced with a profile or policy setting."
iRULE 3: HTTP HEADER INSERTION
when HTTP_REQUEST {
HTTP::header insert "X-Client-IP" [IP::client_addr]
}
Step-by-step execution:
1. Client (10.1.10.50) sends HTTP request
2. HTTP_REQUEST fires
3. [IP::client_addr] returns "10.1.10.50"
4. HTTP::header insert adds "X-Client-IP: 10.1.10.50" to the request headers
5. Server receives the request with the additional custom header
6. Server application can read X-Client-IP for logging, access control, etc.
Response modification (HTTP_RESPONSE event):
when HTTP_RESPONSE {
HTTP::header remove "Server"
HTTP::header remove "X-Powered-By"
HTTP::header insert "Strict-Transport-Security" "max-age=31536000"
}
This removes server version disclosure headers and adds HSTS. Note: response modification does NOT work with nPath/DSR since the response bypasses the BIG-IP.
COMMON STUDENT MISTAKES
- Creating the redirect VS with an iRule but forgetting the HTTP profile → iRule never fires, no redirect happens, no error message
- Adding the redirect iRule to the HTTPS VS instead of creating a separate port-80 VS
- Not understanding that "pool" command in an iRule overrides the VS default pool for that specific request only
PIVOT QUESTION
"A virtual server has iRule 2 (URI content switching) attached. Client requests https://app.example.com/api/v2/users. The VS default pool is web_pool. Which pool handles this request?"
ANSWER: api_pool. The URI /api/v2/users matches pattern "/api/*" (glob wildcard * matches "v2/users"). The switch evaluates in order, first match wins. The pool command overrides the VS default pool for this request.
F5 DOCUMENTATION
- iRules API reference: https://clouddocs.f5.com/api/irules/
- HTTP::redirect: https://clouddocs.f5.com/api/irules/HTTP__redirect.html
- HTTP::header: https://clouddocs.f5.com/api/irules/HTTP__header.html
- LTM Policies vs iRules: https://my.f5.com/manage/s/article/K04597703
EXAM QUESTION PATTERNS
- "An iRule with HTTP_REQUEST never fires. The VS has TCP only. What's missing?" → HTTP profile
- "Which iRule event requires Client-SSL profile?" → CLIENTSSL_HANDSHAKE
- "Can the URI content switching iRule be replaced with an LTM policy?" → Yes, for simple URI matching

## Slide 28
28 © 2026 F5
Lab 2 - Hands-on exercises
45 minutes | Lab guide: Module 2
# | Activity | Key tasks | Time
1 | Working with Profiles | Build secure_vs, discover profile dependencies through deliberate failures (SSL, HTTP, cookie persistence). | 10m
2 | Application Acceleration | TCP Express (wan/lan profiles), RamCache, HTTP Compression. Compare statistics. | 15m
3 | Securing Web Apps | Custom HTTP profile: fallback host, error cloaking, header scrubbing, cookie encryption, XFF. | 10m
4 | Using iRules | HTTP-to-HTTPS redirect. Deliberate failure without HTTP profile, then fix. | 10m
Sequence matters: Activity 1 first (introduces dependencies through failures). Activity 4 last (reinforces HTTP profile dependency with iRules). Do not skip troubleshooting steps.
Notes: WHAT THIS SLIDE TEACHES
This is the lab launch slide — it stays on screen while students work through the hands-on exercises. The four activities are sequenced deliberately: Activity 1 establishes the profile dependency concept through controlled failures, and Activity 4 reinforces it with iRules.
FULL TECHNICAL EXPLANATION OF EACH ACTIVITY
ACTIVITY 1: WORKING WITH PROFILES (10 minutes)
Students build a new HTTPS virtual server and discover profile dependencies through a series of deliberate failures:
Step-by-step walkthrough:
1. Create secure_pool: members 10.1.20.11:443, 10.1.20.12:443, 10.1.20.13:443, monitor https
2. Create secure_vs at 10.1.10.115:443 with ONLY a TCP profile → Browse to https://10.1.10.115
- Q: Does it work? YES — this is SSL pass-through. The BIG-IP forwards encrypted packets without inspecting them. The server handles SSL.
- Q: Can you use L7 iRules or profiles? NO — BIG-IP can't see inside the encrypted traffic.
3. Switch to www_pool (port 80) → Browse → FAILS. Client sends HTTPS, server expects HTTP. Connection breaks because port 80 servers can't decrypt SSL.
4. Add clientssl profile → NOW BIG-IP terminates SSL from client, forwards unencrypted HTTP to port 80 servers. This is SSL offload.
5. Add cookie persistence → FAILS because there's no HTTP profile. Cookies are HTTP-layer objects.
TEACHING MOMENT: This is the key lesson. Students must add an HTTP profile before cookie persistence works.
6. Switch back to secure_pool (port 443), add serverssl → Full SSL re-encryption.
ACTIVITY 2: APPLICATION ACCELERATION (15 minutes)
TCP Express:
- Apply tcp-wan-optimized (client side) and tcp-lan-optimized (server side) to www_vs
- Examine actual profile settings in GUI: idle timeout, Nagle, buffer sizes
- Lab questions test understanding of WHY settings differ
RamCache:
- Create www-opt-caching profile (parent: optimized-caching)
- Apply to www_vs with HTTP profile
- Browse and refresh — images stop changing (served from cache, not different pool members)
- Check pool stats — some members show no new connections
- CLI: show ltm profile ramcache www-opt-caching
HTTP Compression:
- Create www-compress profile (parent: wan-optimized-compression)
- Remove caching first (avoid interference)
- Apply compression, browse, check headers — Accept-Encoding removed from server-bound request
ACTIVITY 3: SECURING WEB APPLICATIONS (10 minutes)
Create custom HTTP profile "secure-my-website":
- Fallback Host: http://www.f5.com (redirect on error)
- Fallback on Error Codes: 404, 500-505 (server errors redirect to fallback)
- Response Headers Allowed: Content-Type, Set-Cookie, Location (strips all other response headers — prevents info disclosure like Server, X-Powered-By)
- Cookie Encryption: encrypt the BIGipServer cookie (prevents attacker from decoding pool member IP)
- X-Forwarded-For: Enabled (pass original client IP to server)
ACTIVITY 4: USING iRULES (10 minutes)
1. Find _sys_https_redirect iRule in Local Traffic > iRules
2. Create redirect_to_secure_vs at 10.1.10.115:80 with HTTP type
3. Attach the redirect iRule → GET AN ERROR — needs HTTP profile for HTTP_REQUEST event
4. Add HTTP profile → try again → SUCCESS
5. Browse http://10.1.10.115 → automatically redirected to https://10.1.10.115
COMMON STUDENT ISSUES
- Forgetting to switch back to secure_pool after HTTP/HTTPS testing in Activity 1
- Not understanding why the redirect VS doesn't need a pool (traffic goes nowhere — the 302 response goes back to the client)
- Confusion between "VS terminates SSL" (with Client-SSL profile) vs "VS passes SSL through" (no SSL profile)
- SSH session to management IP (10.1.1.4) won't appear in "show sys connection" — management traffic is handled by host OS, not TMM
PIVOT QUESTION
"In Activity 1, step 2, you create a VS with only a TCP profile and browse to https://10.1.10.115. It works. But you can't add cookie persistence. Why does HTTPS work without an SSL profile?"
ANSWER: Without a Client-SSL profile, the BIG-IP is doing SSL PASS-THROUGH. It doesn't terminate or decrypt the SSL — it just forwards the encrypted packets to the server. The server handles all SSL processing. This works for basic load balancing but prevents any L7 features because the BIG-IP can't see inside the encrypted traffic. To add cookie persistence, you need Client-SSL (to decrypt) + HTTP (to parse cookies).
F5 DOCUMENTATION
- Lab reference: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-profiles-reference.html
- HTTP monitor crafting: https://my.f5.com/manage/s/article/K2167
- Cookie encoding: https://my.f5.com/manage/s/article/K6917
EXAM QUESTION PATTERNS
- "An HTTPS VS with only a TCP profile loads the site but you can't add cookie persistence. What profiles are missing?" → Client-SSL + HTTP
- "What is the minimum profile set for an HTTP-to-HTTPS redirect VS?" → TCP + HTTP + iRule (no pool, no SNAT needed)

## Slide 29
29 © 2026 F5
Exam checkpoints
Q1
A/E
2.10
Client reports images load slowly but HTML renders quickly. VS has TCP + HTTP + wan-optimized-compression. What do you evaluate first and what profile change do you recommend?
Q2
U/A
3.01
An iRule with HTTP_REQUEST is attached to a VS with only a TCP profile. Traffic flows but the iRule never executes. Why, and what do you fix?
Q3
U/A
2.04
In a two-tier deployment, Tier 1 uses SNAT automap + cookie persistence. Tier 2 uses source address persistence. Users report getting bounced between app servers. Why?
Dependency chain: Cookie persist → HTTP → TCP. OneConnect → HTTP → TCP. iRule (HTTP::) → HTTP → TCP. Client-SSL → TCP. Every L7 feature traces back to TCP.
Notes: WHAT THIS SLIDE TEACHES
These checkpoint questions test the key concepts from the Lab 2 concept slides at the cognitive levels specified in the Beta blueprint. They are designed to be asked verbally after students complete the lab — do NOT show answers on screen.
Q1 ANSWER (A/E — Objective 2.10)
Images (JPEG, PNG, GIF) are already compressed formats. The HTTP compression profile does NOT help them and wastes CPU attempting to recompress incompressible data. The slow image loading is a bandwidth issue.
Recommended fix: Enable Web Acceleration (RamCache) for static image content. Cached images are served from BIG-IP memory, eliminating server round-trips entirely. Also verify images are excluded from compression Content-Type Include list (they should be by default in wan-optimized-compression).
This tests whether students can distinguish between compression (reduces size of compressible text) and caching (eliminates server round-trips for repeat requests).
Q2 ANSWER (U/A — Objective 3.01)
The virtual server is missing an HTTP profile. The HTTP_REQUEST event only fires when the BIG-IP has parsed HTTP request headers, which requires an HTTP profile. Without it, the BIG-IP treats traffic as raw TCP bytes and never raises HTTP-layer events. The iRule's HTTP_REQUEST handler is registered but never triggered.
Fix: Add an HTTP profile to the VS.
GUI: Virtual Servers > [VS] > HTTP Profile > select "http"
TMSH: modify ltm virtual [vs_name] profiles add { http { } }
This is exactly what happens in Lab Activity 4 — the deliberate failure teaches this lesson.
Q3 ANSWER (U/A — Objective 2.04)
Tier 1 SNAT automap changes ALL source IPs to the BIG-IP self IP. Tier 2 source address persistence sees all traffic from one IP (the BIG-IP), so it persists ALL users to the same app server. When the persistence record expires, a new load balancing decision sends traffic to a different server — users get "bounced."
Fix options:
1. Use cookie persistence at Tier 2 (if app protocol is HTTP) — cookies identify individual users regardless of source IP
2. Use universal persistence at Tier 2 with XFF header from Tier 1 — persist on the original client IP passed in XFF
3. Eliminate SNAT at Tier 1 (change server routing to gateway through BIG-IP) — preserves original client IP at Tier 2
COMMON STUDENT MISTAKES
- Not connecting the SNAT + persistence interaction across tiers
- Answering Q1 by suggesting "higher compression level" — this is wrong; the issue is that images can't be compressed further
F5 DOCUMENTATION
- Profile dependencies: https://my.f5.com/manage/s/article/K23843660
- SNAT overview: https://my.f5.com/manage/s/article/K7820
EXAM QUESTION PATTERNS
All three questions mirror real exam patterns: Q1 is scenario-based (A/E), Q2 is troubleshooting (U/A), Q3 is multi-tier architecture (U/A).

## Slide 30
30 © 2026 F5
Exam checkpoints (continued)
Q4
U/A
2.01
You need cookie persistence on an HTTPS virtual server. What is the minimum set of profiles required for cookie persistence to function?
Q5
U/A
2.02
A web application has 50,000 short-lived HTTP connections per second. Servers are running out of TCP sockets. What profile reduces server connection load, and what does it require?
Persistence method selection guide
HTTP web app → cookie insert (most granular, survives IP changes)
Non-HTTP / FastL4 → source address (only universal option)
SSL pass-through → SSL session ID
Custom protocol → universal persistence (iRule-based)
Mobile users who change IPs → cookie insert (not source address)
Notes: WHAT THIS SLIDE TEACHES
These final checkpoint questions test two critical concepts: the minimum profile set for a common deployment scenario (Q4) and the OneConnect profile that's called out in the blueprint but not exercised in any lab (Q5).
Q4 ANSWER (U/A — Objective 2.01)
Minimum profiles for cookie persistence on an HTTPS virtual server:
1. TCP profile — transport layer foundation
2. Client-SSL profile — decrypt HTTPS from client so BIG-IP can read HTTP content
3. HTTP profile — parse HTTP to read/insert cookies (cookies are HTTP headers)
4. Cookie persistence profile — the persistence method itself
The dependency chain: Cookie persistence → requires HTTP (cookies are HTTP objects) → requires TCP (HTTP requires TCP connection termination). Plus Client-SSL for HTTPS decryption.
Common mistake: Students forget the HTTP profile. They add Client-SSL + cookie persistence and wonder why persistence doesn't work. Client-SSL decrypts the traffic, but without HTTP, the BIG-IP doesn't parse the HTTP layer and cannot read or insert cookies.
If the application also requires SSL to the backend (end-to-end encryption), add a Server-SSL profile. But that's not required for cookie persistence to function — it's a separate requirement.
TMSH for the complete setup:
create ltm profile client-ssl my-clientssl cert my-cert key my-key
create ltm virtual secure_vs destination 10.1.10.115:443 ip-protocol tcp \
profiles add { my-clientssl { context clientside } http { } tcp { } } \
persist add { cookie { } } pool www_pool source-address-translation { type automap }
Q5 ANSWER (U/A — Objective 2.02)
Add a OneConnect profile.
How OneConnect works:
- Without OneConnect: Each client HTTP request creates a new TCP connection to the server. 50,000 requests/second = 50,000 TCP connections = 50,000 sockets on each server.
- With OneConnect: The BIG-IP reuses idle server-side TCP connections. After a server responds to a request and the connection goes idle, instead of closing it, the BIG-IP keeps it open and reuses it for the next client's request.
- Result: 50,000 client requests/second might only need 100-500 server connections (depending on server response time and connection idle timeout).
Requirements: TCP + HTTP profiles (OneConnect must understand HTTP request/response boundaries to know when a server connection is idle and safe to reuse for a different client).
Configuration:
GUI: Create profile under Profiles > Other > OneConnect
TMSH: create ltm profile one-connect my-oneconnect defaults-from oneconnect
Apply to VS: modify ltm virtual [vs_name] profiles add { my-oneconnect { } }
Source mask setting:
- 0.0.0.0: All clients share all server connections (most aggressive reuse, best performance)
- 255.255.255.255: Each client IP gets its own connections (least reuse)
- Default: 0.0.0.0
Warning: Not compatible with NTLM authentication without the NTLM profile (K10477).
This question tests the F5CTSLTM2.02 sub-bullet: "Identify LTM profile settings to deploy OneConnect." Since there's no lab exercise for OneConnect, this checkpoint is the only hands-on coverage.
PERSISTENCE METHOD SELECTION GUIDE (study reference):
- HTTP web application → Cookie insert (most granular, survives IP changes, no server-side state)
- Non-HTTP / FastL4 virtual server → Source address (only option that works without HTTP)
- SSL pass-through → SSL session ID (no HTTP profile available for cookies)
- Custom/proprietary protocol → Universal persistence with iRule (most flexible)
- Mobile users who change IPs frequently → Cookie insert (NOT source address — IP changes break it)
- High-security environment → Cookie insert with encryption (prevent cookie tampering)
F5 DOCUMENTATION
- Cookie persistence: https://my.f5.com/manage/s/article/K6917
- OneConnect: https://my.f5.com/manage/s/article/K7208
- OneConnect + NTLM: https://my.f5.com/manage/s/article/K10477
- Profile dependencies: https://my.f5.com/manage/s/article/K23843660
EXAM QUESTION PATTERNS
- "What is the minimum profile set for cookie persistence on HTTPS?" → TCP + Client-SSL + HTTP + Cookie
- "What profile reduces server TCP connection count?" → OneConnect
- "Which persistence method works for mobile users changing networks?" → Cookie insert

## Slide 31
F5CTSLTM3.06 | U/A | Interpret AVR/Telemetry to identify performance issues or attacks
F5CTSLTM3.07 | U/A | Interpret AVR information to identify LTM device misconfiguration
LAB 3
Application Visibility
and Reporting (AVR)
Provision AVR, build analytics profiles, generate traffic with simulated
clients, and use dashboards to identify latency bottlenecks and traffic patterns.
55 min | 10 min slides + 45 min lab
Notes: SECTION OPENER - Lab 3: Application Visibility and Reporting (AVR)
PURPOSE
This lab teaches students to use BIG-IP's built-in analytics engine to monitor application performance, identify bottlenecks, and detect misconfigurations. AVR (Application Visibility and Reporting) provides real-time and historical dashboards that show transaction rates, latency, throughput, response codes, and client demographics — without requiring external monitoring tools.
The lab uses two iRules (pre-built on the BIG-IP) to simulate diverse client traffic: one randomizes client IPs and user agents, the other introduces artificial server-side delay on one pool member. This creates realistic AVR data that students can then analyze to identify the slow server.
BETA BLUEPRINT COVERAGE
- F5CTSLTM3.06 (U/A): "Interpret AVR and/or Telemetry on application behavior to identify performance issues or application attacks." Sub-bullets: explain how to modify profile settings using AVR data, use advanced filters to narrow output, identify potential latency increases.
- F5CTSLTM3.07 (U/A): "Interpret AVR information to identify LTM device misconfiguration." Sub-bullets: explain how latency trends identify application tier bottlenecks, use AVR to trace application traffic.
TELEMETRY STREAMING GAP
The blueprint mentions "Telemetry" alongside AVR in objective 3.06. F5 Telemetry Streaming (TS) is a separate module that exports BIG-IP telemetry data to external consumers (Splunk, Azure Log Analytics, AWS CloudWatch, Kafka, etc.). It is NOT the same as AVR. TS uses a declarative JSON model deployed via iControl REST. This lab covers AVR only — address Telemetry Streaming briefly during concept slides as a complementary tool.
Reference for TS: https://clouddocs.f5.com/products/extensions/f5-telemetry-streaming/latest/
301a OBJECTIVES: 1.06–1.07
DELIVERY TIPS
- AVR data takes up to 5 minutes to populate. Have students start traffic generation IMMEDIATELY after building the virtual servers, then cover concept slides while data accumulates.
- The "delay_server" iRule introduces 20ms delay on pool member 10.1.20.13 — this is what students will identify in the Server Latency view. Make sure they understand this was artificially introduced for learning purposes.
- If AVR is not provisioned, it must be provisioned first (System > Resource Provisioning > Application Visibility and Reporting = Nominal). This requires a service restart.
TIME MANAGEMENT: 55 min total (10 slides + 45 lab). The lab's traffic generation step can run in the background while you deliver concept slides.

## Slide 32
32 © 2026 F5
What AVR Provides
Built-in analytics engine for real-time application monitoring — no external tools required
Performance
monitoring
Transaction rates (TPS)
Server/client latency
Throughput (bits/sec)
Page load time
Traffic
analysis
Top URLs accessed
Top client IPs / subnets
Response code distribution
HTTP methods breakdown
Troubleshooting
& security
Identify slow pool members
Detect traffic anomalies
Track user agent distribution
Correlate latency to URLs
Setup requirements
Step | What | Where | Notes
1 | Provision AVR module | System > Resource Provisioning | Set to Nominal. Requires service restart. NOT provisioned by default.
2 | Create analytics profile | Local Traffic > Profiles > Analytics | Select metrics (TPS, throughput, page load) and entities (URLs, IPs, countries, codes).
3 | Attach profile to VS | Virtual server > Analytics Profile | Only VS with analytics profile attached will generate data.
4 | View reports | Statistics > Analytics > HTTP | Data appears within 1-5 min. Set Auto Refresh to 1 min.
Notes: CONCEPT SLIDE - What AVR Provides
WHAT THIS SLIDE TEACHES
AVR is BIG-IP's built-in application analytics engine. It collects, stores, and presents traffic data in real-time dashboards. Unlike external monitoring tools (Splunk, Datadog, Grafana), AVR runs entirely on the BIG-IP with no additional infrastructure required.
AVR ARCHITECTURE
- AVR runs as a provisioned module within TMOS. It requires CPU and memory resources.
- Data is collected by TMM (Traffic Management Microkernel) as traffic flows through virtual servers with analytics profiles attached.
- Data is aggregated and stored locally on the BIG-IP in a circular database (older data is overwritten as new data arrives).
- Reports are accessed via the TMUI (GUI) under Statistics > Analytics.
- AVR data can also be exported to external systems using the Analytics Data Export feature or F5 Telemetry Streaming.
PROVISIONING DETAILS
AVR is NOT provisioned by default on a new BIG-IP installation. To enable it:
1. Go to System > Resource Provisioning
2. Set "Application Visibility and Reporting (AVR)" to Nominal
3. Click Submit — this triggers a service restart (TMM restarts)
4. Wait for the system to become active again
IMPORTANT: Provisioning AVR on a production system requires a maintenance window because TMM restarts during the provisioning process, which briefly interrupts traffic.
The lab environment has AVR pre-provisioned to save time. Students should verify this in Step 1 of the lab.
ANALYTICS PROFILE
The analytics profile controls WHAT data is collected. There are two main categories:
1. Collected Metrics: The numerical measurements
- Max TPS (Transactions Per Second): Peak request rate
- Throughput: Bits per second of traffic
- Page Load Time: End-to-end time from client request to full page render (requires JavaScript injection)
2. Collected Entities: The dimensions you can filter and group by
- URLs: Which pages/endpoints are being accessed
- Countries: Geographic origin of clients (based on IP geolocation)
- Client IP Addresses: Individual client IPs
- Client Subnets: Grouped by subnet
- Response Codes: HTTP status code distribution (200, 301, 404, 500, etc.)
- User Agents: Browser/device type distribution
- Methods: HTTP method distribution (GET, POST, PUT, DELETE)
MORE entities = MORE data collection = MORE resource consumption. In production, only enable the entities you actually need.
TELEMETRY STREAMING (BLUEPRINT GAP)
F5 Telemetry Streaming (TS) is a separate iControl LX extension that pushes BIG-IP telemetry data to external analytics platforms. It is complementary to AVR, not a replacement:
- AVR: On-box analytics with built-in dashboards. Good for quick troubleshooting.
- TS: Off-box analytics via external platforms. Good for long-term trending, cross-device correlation, SIEM integration.
TS consumers include: Splunk, Azure Log Analytics, AWS CloudWatch, Kafka, ElasticSearch, Graphite, StatsD.
TS is deployed via declarative JSON POSTed to iControl REST. It is NOT configured in the GUI.
Reference: https://clouddocs.f5.com/products/extensions/f5-telemetry-streaming/latest/
F5 DOCUMENTATION
- AVR overview: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-analytics-implementations.html
- Analytics profile reference: https://my.f5.com/manage/s/article/K13637
- Provisioning modules: https://my.f5.com/manage/s/article/K12111
PIVOT QUESTION
"AVR is not provisioned on the BIG-IP. What happens when you try to create an analytics profile?"
ANSWER: The option to create an analytics profile does not appear in the GUI. The Profiles > Analytics menu item is absent entirely. You must first provision AVR under System > Resource Provisioning before any analytics configuration is available.

## Slide 33
33 © 2026 F5
GUI – Creating an AVR Profile
Local Traffic > Profiles > Analytics > Create
Notes: CONCEPT SLIDE - What AVR Provides
WHAT THIS SLIDE TEACHES
AVR is BIG-IP's built-in application analytics engine. It collects, stores, and presents traffic data in real-time dashboards. Unlike external monitoring tools (Splunk, Datadog, Grafana), AVR runs entirely on the BIG-IP with no additional infrastructure required.
AVR ARCHITECTURE
- AVR runs as a provisioned module within TMOS. It requires CPU and memory resources.
- Data is collected by TMM (Traffic Management Microkernel) as traffic flows through virtual servers with analytics profiles attached.
- Data is aggregated and stored locally on the BIG-IP in a circular database (older data is overwritten as new data arrives).
- Reports are accessed via the TMUI (GUI) under Statistics > Analytics.
- AVR data can also be exported to external systems using the Analytics Data Export feature or F5 Telemetry Streaming.
PROVISIONING DETAILS
AVR is NOT provisioned by default on a new BIG-IP installation. To enable it:
1. Go to System > Resource Provisioning
2. Set "Application Visibility and Reporting (AVR)" to Nominal
3. Click Submit — this triggers a service restart (TMM restarts)
4. Wait for the system to become active again
IMPORTANT: Provisioning AVR on a production system requires a maintenance window because TMM restarts during the provisioning process, which briefly interrupts traffic.
The lab environment has AVR pre-provisioned to save time. Students should verify this in Step 1 of the lab.
ANALYTICS PROFILE
The analytics profile controls WHAT data is collected. There are two main categories:
1. Collected Metrics: The numerical measurements
- Max TPS (Transactions Per Second): Peak request rate
- Throughput: Bits per second of traffic
- Page Load Time: End-to-end time from client request to full page render (requires JavaScript injection)
2. Collected Entities: The dimensions you can filter and group by
- URLs: Which pages/endpoints are being accessed
- Countries: Geographic origin of clients (based on IP geolocation)
- Client IP Addresses: Individual client IPs
- Client Subnets: Grouped by subnet
- Response Codes: HTTP status code distribution (200, 301, 404, 500, etc.)
- User Agents: Browser/device type distribution
- Methods: HTTP method distribution (GET, POST, PUT, DELETE)
MORE entities = MORE data collection = MORE resource consumption. In production, only enable the entities you actually need.
TELEMETRY STREAMING (BLUEPRINT GAP)
F5 Telemetry Streaming (TS) is a separate iControl LX extension that pushes BIG-IP telemetry data to external analytics platforms. It is complementary to AVR, not a replacement:
- AVR: On-box analytics with built-in dashboards. Good for quick troubleshooting.
- TS: Off-box analytics via external platforms. Good for long-term trending, cross-device correlation, SIEM integration.
TS consumers include: Splunk, Azure Log Analytics, AWS CloudWatch, Kafka, ElasticSearch, Graphite, StatsD.
TS is deployed via declarative JSON POSTed to iControl REST. It is NOT configured in the GUI.
Reference: https://clouddocs.f5.com/products/extensions/f5-telemetry-streaming/latest/
F5 DOCUMENTATION
- AVR overview: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-analytics-implementations.html
- Analytics profile reference: https://my.f5.com/manage/s/article/K13637
- Provisioning modules: https://my.f5.com/manage/s/article/K12111
PIVOT QUESTION
"AVR is not provisioned on the BIG-IP. What happens when you try to create an analytics profile?"
ANSWER: The option to create an analytics profile does not appear in the GUI. The Profiles > Analytics menu item is absent entirely. You must first provision AVR under System > Resource Provisioning before any analytics configuration is available.

## Slide 34
34 © 2026 F5
GUI – AVR Statics
Statistics> Analytics : TCP: RTT
Notes: CONCEPT SLIDE - What AVR Provides
WHAT THIS SLIDE TEACHES
AVR is BIG-IP's built-in application analytics engine. It collects, stores, and presents traffic data in real-time dashboards. Unlike external monitoring tools (Splunk, Datadog, Grafana), AVR runs entirely on the BIG-IP with no additional infrastructure required.
AVR ARCHITECTURE
- AVR runs as a provisioned module within TMOS. It requires CPU and memory resources.
- Data is collected by TMM (Traffic Management Microkernel) as traffic flows through virtual servers with analytics profiles attached.
- Data is aggregated and stored locally on the BIG-IP in a circular database (older data is overwritten as new data arrives).
- Reports are accessed via the TMUI (GUI) under Statistics > Analytics.
- AVR data can also be exported to external systems using the Analytics Data Export feature or F5 Telemetry Streaming.
PROVISIONING DETAILS
AVR is NOT provisioned by default on a new BIG-IP installation. To enable it:
1. Go to System > Resource Provisioning
2. Set "Application Visibility and Reporting (AVR)" to Nominal
3. Click Submit — this triggers a service restart (TMM restarts)
4. Wait for the system to become active again
IMPORTANT: Provisioning AVR on a production system requires a maintenance window because TMM restarts during the provisioning process, which briefly interrupts traffic.
The lab environment has AVR pre-provisioned to save time. Students should verify this in Step 1 of the lab.
ANALYTICS PROFILE
The analytics profile controls WHAT data is collected. There are two main categories:
1. Collected Metrics: The numerical measurements
- Max TPS (Transactions Per Second): Peak request rate
- Throughput: Bits per second of traffic
- Page Load Time: End-to-end time from client request to full page render (requires JavaScript injection)
2. Collected Entities: The dimensions you can filter and group by
- URLs: Which pages/endpoints are being accessed
- Countries: Geographic origin of clients (based on IP geolocation)
- Client IP Addresses: Individual client IPs
- Client Subnets: Grouped by subnet
- Response Codes: HTTP status code distribution (200, 301, 404, 500, etc.)
- User Agents: Browser/device type distribution
- Methods: HTTP method distribution (GET, POST, PUT, DELETE)
MORE entities = MORE data collection = MORE resource consumption. In production, only enable the entities you actually need.
TELEMETRY STREAMING (BLUEPRINT GAP)
F5 Telemetry Streaming (TS) is a separate iControl LX extension that pushes BIG-IP telemetry data to external analytics platforms. It is complementary to AVR, not a replacement:
- AVR: On-box analytics with built-in dashboards. Good for quick troubleshooting.
- TS: Off-box analytics via external platforms. Good for long-term trending, cross-device correlation, SIEM integration.
TS consumers include: Splunk, Azure Log Analytics, AWS CloudWatch, Kafka, ElasticSearch, Graphite, StatsD.
TS is deployed via declarative JSON POSTed to iControl REST. It is NOT configured in the GUI.
Reference: https://clouddocs.f5.com/products/extensions/f5-telemetry-streaming/latest/
F5 DOCUMENTATION
- AVR overview: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-analytics-implementations.html
- Analytics profile reference: https://my.f5.com/manage/s/article/K13637
- Provisioning modules: https://my.f5.com/manage/s/article/K12111
PIVOT QUESTION
"AVR is not provisioned on the BIG-IP. What happens when you try to create an analytics profile?"
ANSWER: The option to create an analytics profile does not appear in the GUI. The Profiles > Analytics menu item is absent entirely. You must first provision AVR under System > Resource Provisioning before any analytics configuration is available.

## Slide 35
35 © 2026 F5
Metrics vs entities: what AVR collects
Metrics are the measurements. Entities are the dimensions you filter and group by.
Collected metrics (what you measure)
Max TPS
Peak transactions per second
Capacity planning, detect traffic spikes
Throughput
Bits/sec of traffic volume
Bandwidth consumption, anomaly detection
Page Load Time
Client-perceived render time
End-user experience monitoring
Server Latency
Time server takes to respond
Backend bottleneck identification
Client Latency
Network latency to client
WAN/Internet quality assessment
Collected entities (how you slice data)
URLs
Which pages/endpoints
Find most-requested or slowest pages
Response Codes
HTTP status distribution
Detect error spikes (4xx, 5xx)
Pool Members
Per-server breakdown
Identify which server is slow or failing
Client IPs
Individual client tracking
Find heavy users or attackers
Countries
Geographic distribution
Regional performance analysis
User Agents
Browser/device types
Mobile vs desktop traffic split
Interpretation pattern: Start with the Overview (total TPS, throughput). Drill into Transactions > View By Pool Members to find the problem server. Then drill into that server's URLs and Latency to find the root cause. The lab's delay_server iRule introduces 20ms latency on 10.1.20.13 — students should identify this in the Server Latency view.
Notes: CONCEPT SLIDE - Metrics vs Entities
WHAT THIS SLIDE TEACHES
This slide establishes the mental model for reading AVR dashboards. Students must understand that metrics are WHAT you measure, and entities are HOW you slice/filter/group that data. This distinction maps directly to the blueprint sub-bullets for 3.06 ("use advanced filters to narrow output data from AVR") and 3.07 ("use AVR to trace application traffic").
METRICS IN DETAIL
MAX TPS (Transactions Per Second)
- Measures the peak rate of HTTP transactions processed by the virtual server
- A "transaction" is one complete HTTP request/response cycle
- Use for: capacity planning (am I approaching the BIG-IP's throughput limit?), detecting traffic spikes (DDoS, flash crowds, marketing campaigns)
- AVR shows this as a time-series graph — spikes are immediately visible
THROUGHPUT
- Measures bits per second of traffic (both client-side and server-side)
- Useful for bandwidth planning and detecting unusual traffic volumes
- A sudden spike in throughput with stable TPS may indicate large file downloads or responses
PAGE LOAD TIME
- Measures the end-to-end time from client request to full page render
- REQUIRES JavaScript injection: the HTTP profile must have "Response Analytics" enabled, which injects a small JavaScript snippet into HTML responses. The JavaScript reports back timing data to the BIG-IP.
- This is the MOST end-user-relevant metric but has the most overhead
SERVER LATENCY vs CLIENT LATENCY
- Server latency: time between BIG-IP sending request to pool member and receiving the response. HIGH server latency = backend problem (slow database, overloaded app server, disk I/O).
- Client latency: time between BIG-IP sending response to client and the client acknowledging. HIGH client latency = network problem (WAN congestion, mobile network, geographic distance).
- The ability to SEPARATE server and client latency is one of AVR's most powerful features. Without it, you can't tell whether "slow app" is a backend problem or a network problem.
ENTITIES IN DETAIL
URLs: The most common entity for troubleshooting. "Which pages are slow?" → View Server Latency by URL → Find the URL with the highest average latency → Investigate why that specific endpoint is slow.
Response Codes: Essential for error detection. A spike in 5xx codes indicates server errors. A spike in 4xx codes may indicate client-side issues (broken links, changed URLs) or potential attacks (scanning, probing). The lab should show a mix of 200 codes.
Pool Members: The key entity for identifying which SERVER is the problem. In the lab, the delay_server iRule introduces latency on 10.1.20.13 — when students view Server Latency by Pool Members, 10.1.20.13 should show noticeably higher latency than 10.1.20.11 and 10.1.20.12.
THE DRILL-DOWN PATTERN (EXAM RELEVANT)
The exam may present a scenario: "Users report intermittent slowness. AVR shows overall TPS is normal. How do you identify the problem?"
Answer pattern:
1. Overview → TPS and throughput are normal → not a capacity issue
2. Transactions → View By Pool Members → one member has fewer transactions (it's slower, so load balancer sends it less traffic over time with algorithms like Least Connections)
3. Latency → Server Latency → View By Pool Members → that member shows 20ms+ higher latency
4. Drill into that member → View By URLs → specific URL has the highest latency
5. Root cause: that specific URL on that specific server has a backend issue (slow query, disk I/O, memory pressure)
This drill-down pattern is exactly what the lab exercises.
F5 DOCUMENTATION
- Analytics implementations: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-analytics-implementations.html
- Analytics profile settings: https://my.f5.com/manage/s/article/K14260
- Page Load Time (JavaScript injection): https://my.f5.com/manage/s/article/K13637

## Slide 36
36 © 2026 F5
Using AVR to identify bottlenecks
Follow this workflow to trace performance issues from symptoms to root cause
1 Overview
Check total TPS,
throughput, errors.
Normal? Go deeper.
▶
2 Transactions
View By: Pool Members.
Find which server has
fewer transactions.
▶
3 Server latency
View By: Pool Members.
Identify the member
with highest latency.
▶
4 Drill into member
View By: URLs.
Find which endpoint
is causing the delay.
▶
5 Root cause
Correlate with app logs,
DB queries, or server
resource utilization.
Common AVR patterns and what they mean
AVR observation | Likely cause | Action
High server latency on ONE member | That server has a backend issue (slow DB, resource contention) | Investigate server-level metrics; consider removing from pool temporarily
High server latency on ALL members | Upstream dependency issue (shared database, shared service) | Look at the common dependency, not individual servers
High client latency, normal server latency | Network issue between BIG-IP and clients (WAN, Internet, CDN) | Not a BIG-IP or server issue; check network path
Spike in 5xx response codes | Server errors (app crash, deployment issue, resource exhaustion) | Check server logs; correlate with deployment timeline
TPS spike with latency increase | Traffic overload (DDoS, flash crowd, marketing campaign) | Scale pool, enable rate limiting, check if attack vs legitimate
Uneven transaction distribution | Persistence sending too much traffic to one member, or member is slow | Check persistence settings; review LB method
Notes: CONCEPT SLIDE - Using AVR to Identify Bottlenecks
WHAT THIS SLIDE TEACHES
This slide provides the troubleshooting methodology for AVR — the drill-down workflow that students will use in the lab to find the artificially slow pool member. This directly addresses F5CTSLTM3.06 ("identify potential latency increases") and F5CTSLTM3.07 ("explain how latency trends identify application tier bottlenecks").
THE FIVE-STEP DRILL-DOWN WORKFLOW
STEP 1: OVERVIEW
Start at Statistics > Analytics > HTTP > Overview. This gives you the big picture:
- Total transactions per second: Is the app seeing normal traffic volume?
- Total throughput: Is bandwidth consumption normal?
- Error rate: Are there spikes in error responses?
If everything looks normal here but users still report issues, the problem is localized — go deeper.
STEP 2: TRANSACTIONS BY POOL MEMBER
Go to Transactions tab > View By: Pool Members. This shows how traffic is distributed across servers.
- If one server is handling significantly fewer transactions, it may be slow (least-connections algorithms naturally route less traffic to slower servers).
- If one server has more transactions, check if persistence is sending disproportionate traffic there.
STEP 3: SERVER LATENCY BY POOL MEMBER
Go to Latency > Server Latency > View By: Pool Members. This is the most diagnostic view.
- Server latency measures the time between the BIG-IP sending a request to the server and receiving the response.
- If ONE member has higher latency: that specific server has an issue.
- If ALL members have similar high latency: the problem is a shared dependency (database, external API, DNS).
IN THE LAB: The delay_server iRule adds 20ms delay to member 10.1.20.13. Students should see 10.1.20.13 with noticeably higher server latency in this view.
STEP 4: DRILL INTO THE SLOW MEMBER
Click on the slow member (10.1.20.13:80) in the detail section. Then View By: URLs.
- This reveals which specific URLs/endpoints are slow on that server.
- The delay_server iRule adds extra delay for the URL "/web_site/" — students should see this URL with higher latency.
STEP 5: CORRELATE WITH ROOT CAUSE
AVR tells you WHERE the problem is and WHAT the symptoms are. The root cause requires investigating the server itself:
- Check server CPU, memory, disk I/O
- Check database query performance
- Check application logs for errors or slow queries
- Check if a recent deployment changed behavior
THE PATTERN TABLE
The six patterns in the table cover the most common AVR scenarios. Each maps an observation to a likely cause and an action. Students should memorize these patterns because the exam presents scenarios and asks "what does this AVR data indicate?"
KEY EXAM INSIGHT: SEPARATING CLIENT VS SERVER LATENCY
This is AVR's most powerful diagnostic capability. Without AVR, when users report "the app is slow," you don't know if it's the server, the network, or the BIG-IP. AVR separates these:
- High server latency + normal client latency = server/backend problem
- Normal server latency + high client latency = network problem
- High server latency + high client latency = server problem causing delays that cascade to clients
MODIFYING PROFILE SETTINGS BASED ON AVR (3.06 sub-bullet)
"Explain how to modify profile settings using information from the AVR."
Example: AVR shows high throughput but moderate TPS with large response sizes. This suggests enabling HTTP compression to reduce bandwidth. Or: AVR shows a URL is accessed thousands of times per minute with identical responses — this suggests enabling Web Acceleration (RamCache) for that content.
F5 DOCUMENTATION
- Analytics troubleshooting: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-analytics-implementations.html
- Server latency analysis: https://my.f5.com/manage/s/article/K14260
PIVOT QUESTION (U/A)
"AVR shows server latency of 800ms for pool member 10.1.20.13 but only 50ms for 10.1.20.11 and 10.1.20.12. Client latency is 200ms for all clients. What tier is the problem in?"
ANSWER: The backend/server tier. Specifically, server 10.1.20.13 has an issue. The fact that client latency is consistent across all clients eliminates the network as the cause. The fact that only one pool member is slow eliminates shared dependencies (like a database). The problem is isolated to that specific server — investigate its CPU, memory, application logs, and any server-specific configuration.

## Slide 37
37 © 2026 F5
Lab 3 - Hands-on exercises
45 minutes | Lab guide: Module 3
# | Activity | Key tasks | Time
1 | AVR Lab Setup | Verify AVR provisioning, confirm pre-built iRules (random_client_ip, delay_server) and data group (user_agents) exist. | 5m
2 | Create Analytics Profile | Create custom_analytics profile: enable Max TPS, Throughput, Page Load Time. Collect URLs, Countries, Client IPs, Subnets, Response Codes, User Agents, Methods. | 10m
3 | Create Web App | Build avr_virtual2 (10.1.20.240:80) with analytics profile + delay_server iRule. Build avr_virtual1 (10.1.10.90:80) with random_client_ip iRule. | 10m
4 | Generate Traffic & View Reports | Browse http://10.1.10.90 repeatedly (Ctrl+F5), visit multiple pages. Open Statistics > Analytics > HTTP. Analyze Overview, Transactions, Latency by pool member and URL. | 20m
Time-saver: Start Activity 3 (build virtual servers) ASAP, then generate traffic immediately. AVR data takes 1-5 minutes to populate. Browse the site while reviewing concept slides — data will be ready when you get to Activity 4.
Key lab questions: Q1: Does a particular pool member seem slow? (Yes — 10.1.20.13 due to delay_server iRule) Q2: What country has most transactions? Q3: What are the top user agents?
Notes: LAB LAUNCH - Leave this slide on screen while students work.
LAB 3 EXERCISE DETAILS
THE TWO-VIRTUAL-SERVER ARCHITECTURE
This lab uses a clever two-VS design to simulate diverse client traffic:
avr_virtual1 (10.1.10.90:80) — "Traffic generator" VS
- Receives traffic from the student's browser
- The random_client_ip iRule: (a) generates a random source IP, (b) picks a random user agent from the data group, (c) forwards the request to avr_virtual2 using the "virtual" command
- This simulates hundreds of different clients hitting the application
avr_virtual2 (10.1.20.240:80) — "Application" VS
- This is the VS with the analytics profile attached
- The delay_server iRule introduces 20ms delay specifically for member 10.1.20.13 on certain URLs
- Uses www_pool as the default pool
- All AVR data is collected here
Students browse to avr_virtual1 (http://10.1.10.90), which generates randomized traffic to avr_virtual2. The analytics profile on avr_virtual2 collects the data.
IMPORTANT: avr_virtual2 must be created FIRST because avr_virtual1's iRule references it with the "virtual avr_virtual2" command. If created in the wrong order, the iRule will fail.
ACTIVITY 4: VIEWING REPORTS
Guide students through this sequence:
1. Statistics > Analytics > HTTP > Overview
- Set Auto Refresh to 1 minute
- Set time range to "Last Hour"
- Observe total TPS and throughput graphs
2. Transactions tab > View By: Pool Members
- See how traffic distributes across the three www_pool members
- Member 10.1.20.13 may show fewer transactions (it's slower, so Round Robin still sends equal share, but if using Least Connections it would get less)
3. Latency > Server Latency > View By: Pool Members
- THIS IS THE KEY VIEW — member 10.1.20.13 should show ~20ms higher latency
- Click on 10.1.20.13:80 to drill into its specific URLs
4. View By: URLs
- The URL "/web_site/" should show the highest latency on 10.1.20.13
5. View By: Response Codes
- Should see predominantly 200 OK
6. View By: Countries and User Agents
- Random IPs create diverse geographic distribution
- Random user agents show the distribution from the data group
COMMON ISSUES
- "No data showing": Set Auto Refresh to 1 minute. Data takes 1-5 minutes to appear. Make sure you browsed to 10.1.10.90 (not 10.1.10.100).
- "All latency looks the same": Need more traffic. Have students refresh (Ctrl+F5) 20-30 times across different pages.
- "Analytics menu is missing": AVR is not provisioned. Check System > Resource Provisioning.

## Slide 38
38 © 2026 F5
Exam checkpoints
These mirror the cognitive level and style of F5-CTS Beta exam questions
Q1
U/A
3.06
AVR shows server latency of 800ms for member 10.1.20.13 but only 50ms for the other two members. Client latency is 200ms for all clients. Is this a server problem, a network problem, or a BIG-IP configuration issue? How do you know?
Q2
U/A
3.07
AVR shows high throughput but moderate TPS, with large average response sizes. Which profile change would you evaluate to reduce bandwidth consumption, and what additional profile could eliminate repeat requests for the same content entirely?
Q3
U/A
3.06
AVR shows a sudden spike in 5xx response codes at 2:00 PM on Tuesday. TPS is normal. No configuration changes were made on the BIG-IP. What do you investigate, and where do you look?
Remember: AVR tells you WHERE and WHAT. Root cause analysis requires correlating with server logs, application metrics, and deployment history.
Notes: EXAM CHECKPOINTS - Lab 3
Q1 ANSWER (U/A - 3.06)
This is a SERVER-TIER problem, specifically isolated to server 10.1.20.13.
How to determine this:
- Server latency is the time between the BIG-IP sending a request to the pool member and receiving the response. 800ms on ONE member vs 50ms on the others means that specific server is slow.
- Client latency is the time between the BIG-IP sending the response to the client and the client acknowledging. 200ms is consistent across all clients — this eliminates the network as a cause.
- If this were a BIG-IP configuration issue, ALL pool members would show similar latency (since the BIG-IP processes them all the same way).
Conclusion: The problem is on server 10.1.20.13 itself. Investigate: CPU utilization, memory pressure, disk I/O, application logs, database query performance on that specific server.
In the lab, this is caused by the delay_server iRule introducing artificial 20ms delay. In production, this pattern typically indicates a server-level issue like a slow database query, disk contention, or a memory leak.
Q2 ANSWER (U/A - 3.07)
1. Enable HTTP Compression (wan-optimized-compression profile) to compress text-based responses before sending to clients. This reduces throughput (bandwidth) without reducing TPS (requests still process at the same rate, but each response is smaller on the wire).
2. Enable Web Acceleration (RamCache profile) to cache frequently-accessed static content. This eliminates repeat requests for the same content entirely — the BIG-IP serves from RAM without contacting the server.
Both profiles require the HTTP profile as a prerequisite. They can be combined: the BIG-IP caches the compressed version, so subsequent requests get compressed content from cache without re-compressing or contacting the server.
This question tests the 3.06 sub-bullet: "Explain how to modify profile settings using information from the AVR." The AVR data (high throughput, large responses) directly informs the profile selection (compression for bandwidth, caching for repeat requests).
Q3 ANSWER (U/A - 3.06)
This is a server-side application issue, not a BIG-IP problem.
How to determine this:
- 5xx response codes are generated by the APPLICATION SERVER, not the BIG-IP (unless an iRule or LTM policy generates them)
- Normal TPS means the BIG-IP is still receiving and forwarding requests — it's not a connectivity issue
- No BIG-IP configuration changes eliminates the BIG-IP as the cause
- The timing (2:00 PM Tuesday) suggests a scheduled event: deployment, cron job, batch process, backup
Investigation:
1. AVR: Drill into 5xx codes > View By: Pool Members → Which server is generating the errors?
2. AVR: View By: URLs → Which endpoints are returning 5xx?
3. Server logs: Check the identified server's application logs around 2:00 PM
4. Deployment history: Was a code deployment scheduled at that time?
5. System events: Was there a database maintenance window, certificate expiry, or license check?
The key insight: AVR shows SYMPTOMS (5xx spike). The ROOT CAUSE is in the server-side application/infrastructure. AVR narrows your search to the right server and endpoint, then you correlate with server-side data.

## Slide 39
F5CTSLTM2.13 | U/A | Given a packet capture, identify monitor issues
F5CTSLTM2.14 | U/A | Given a monitor issue, determine an appropriate solution
LAB 4
Monitors and Status
Configure health monitors (ICMP, HTTP, content, EAV, inband, In-TMM),
predict status outcomes, understand member-to-pool-to-VS cascade,
and troubleshoot disabled vs offline states.
60 min | 15 min slides + 45 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 4. Covers F5CTSLTM2.13 (packet capture monitor issues) and F5CTSLTM2.14 (monitor troubleshooting, including when to apply In-TMM monitoring — an explicit sub-bullet). Five lab activities build from basic ICMP monitors through content monitors, status states, EAV external scripts, and inband + active monitor combinations.
301a OBJECTIVES: 1.08–1.10. DELIVERY: 60 min (15 slides + 45 lab).
F5 DOCUMENTATION: K12531 (monitor overview), K2167 (HTTP monitors), K2282 (external monitors), K45753464 (In-TMM monitoring).

## Slide 40
40 © 2026 F5
Monitor types
Choose the type that verifies the specific service your application depends on
Type | What it checks | Use when | Limitation
ICMP | IP address responds to ping | Default node monitor. Verifies host reachable. | Host up but service down passes. Least specific.
TCP | TCP port accepts connections | Non-HTTP services (MySQL, SMTP, custom) | Port open but app unresponsive passes.
HTTP/S | Sends HTTP request, checks response content | Web apps. Most common monitor type. | Must craft correct send/receive strings.
External (EAV) | Runs a custom script on the BIG-IP | Complex: DB queries, API calls, multi-step checks | Script runs on BIG-IP CPU. stdout = UP.
Inband | Monitors actual client traffic responses | Detect load-dependent failures active misses | No traffic = no monitoring. Combine w/ active.
In-TMM | Monitor runs inside TMM process (not host OS) | Monitor must use data plane routing/VLANs | Only supports gateway_icmp, TCP, UDP, HTTP/S.
HTTP monitor send/receive example
Send: GET /health HTTP/1.0\r\n\r\n
Receive: 200 OK
Send string must end with \r\n\r\n (empty line signals end of headers). Receive string is searched in the ENTIRE response (headers + body), NOT case sensitive. No receive string = any response marks member UP.
Notes: WHAT THIS SLIDE TEACHES
This slide covers all monitor types including In-TMM (added per F5CTSLTM2.14 sub-bullet: "Describe when In-TMM monitoring should be applied"). The progression from ICMP to In-TMM represents increasing specificity and sophistication.
FULL TECHNICAL EXPLANATION
MONITOR HIERARCHY (least to most specific):
1. ICMP: Pings the IP. Only verifies network connectivity. A crashed web server with working OS passes ICMP.
2. TCP: Attempts a TCP connection. Verifies the port is listening. An app accepting connections but returning errors passes TCP.
3. HTTP/HTTPS: Sends an HTTP request and checks the response for specific content. The standard for web apps.
4. External (EAV): Runs a custom script. Can check anything — DB queries, multi-step workflows, file existence.
5. Inband: No synthetic traffic. Watches actual client traffic for failures. Detects load-dependent issues active monitors miss.
6. In-TMM: Active monitor that runs inside the TMM data plane process instead of the BIG-IP host OS.
HTTP SEND/RECEIVE STRINGS — CRITICAL DETAILS:
Send string format: METHOD URI HTTP/VERSION\r\n[Headers\r\n]\r\n
- The final \r\n\r\n is MANDATORY — it signals the end of HTTP headers
- Without it, the server waits for more data → monitor times out → member marked DOWN
- Common mistake: "GET /health" without \r\n\r\n → always fails
Receive string: Text searched in the complete response (headers AND body)
- "200 OK" is found in the status line of a successful response
- NOT case sensitive: "200 ok" would also match
- If NO receive string specified: ANY response = UP (even 500 errors)
- If receive string specified but NOT found: member = DOWN
Reverse monitors: Inverts the logic. If receive string IS found → DOWN. Use case: check for error conditions.
IN-TMM MONITORING — EXPLAINED:
By default, BIG-IP health monitors run in the host OS (Linux) network stack, not inside the TMM (Traffic Management Microkernel) data plane. This means monitors use the management/host routing table, not the TMM routing table.
When In-TMM monitoring is needed:
- Pool members are only reachable via TMM data plane routing (e.g., route domains, tunnels, VLANs that the host OS doesn't have routes to)
- Monitor traffic must traverse the same network path as client traffic
- Pool members are behind a firewall that only allows traffic from TMM self IPs (not the host OS management IP)
Supported In-TMM monitor types: gateway_icmp, TCP half-open, UDP, HTTP, HTTPS
NOT supported: ICMP (full), external scripts, inband
Configuration: On the monitor, set "In-TMM Monitoring" to Enabled.
TMSH: modify ltm monitor http my_monitor in-tmm enabled
Performance consideration: In-TMM monitors consume TMM CPU cycles. On heavily loaded systems, this can affect traffic processing. Use In-TMM only when required by the network topology.
Reference: https://my.f5.com/manage/s/article/K45753464
COMMON STUDENT MISTAKES
- Using ICMP as the only pool monitor. ICMP checks the host, not the application.
- Missing \r\n\r\n in HTTP send string. The most common monitor failure cause.
- Not understanding when In-TMM is needed vs default monitoring. In-TMM is only needed when the pool members aren't reachable from the host OS network stack.
PIVOT QUESTION
"Your HTTP monitor works on BIG-IP-1 but fails on BIG-IP-2 in the same HA pair. Both have the same configuration. Pool members show as DOWN on BIG-IP-2 only. What do you check?"
ANSWER: The monitors run from the host OS by default. Check if BIG-IP-2's host routing table has a route to the pool member subnet. If pool members are only reachable via TMM routing (e.g., through a specific VLAN), enable In-TMM monitoring on the monitor so it uses TMM's routing table instead of the host OS.
F5 DOCUMENTATION
- HTTP monitors: https://my.f5.com/manage/s/article/K2167
- In-TMM monitoring: https://my.f5.com/manage/s/article/K45753464
- External monitors: https://my.f5.com/manage/s/article/K2282
- Monitor overview: https://my.f5.com/manage/s/article/K12531
EXAM QUESTION PATTERNS
- "Monitor works on active BIG-IP but fails on standby. Why?" → Host OS routing differs; enable In-TMM
- "When should you enable In-TMM monitoring?" → When pool members are only reachable via TMM data plane routing
- "Which monitor types support In-TMM?" → gateway_icmp, TCP half-open, UDP, HTTP, HTTPS

## Slide 41
41 © 2026 F5
Monitor timing
Interval, timeout, and Time Until Up control failure detection speed and false-positive resilience
Interval
5 sec (default)
How often the BIG-IP sends a health check to each pool member.
Timeout
16 sec (default)
Total time window for a successful response. Must be greater than interval.
Time Until Up
0 sec (default)
How long a recovered member must pass checks before being marked UP.
Failure detection formula
Failed checks before DOWN = Timeout ÷ Interval (rounded down)
Default: 16 ÷ 5 = 3.2 → 3 consecutive failed checks → member marked DOWN after ~16 seconds
Best practice
Timeout = (Interval × 3) + 1
Ensures 3 failed checks before DOWN.
Interval=10 → Timeout=31
Interval=30 → Timeout=91
Never set Timeout ≤ Interval (causes flapping).
Up Interval (for inband combos)
When member is UP: checks every [Interval]
When member is DOWN: checks every [Up Interval]
Use with inband monitors: set Up Interval to 60s so the active monitor detects recovery faster than the inband 300s retry.
Notes: WHAT THIS SLIDE TEACHES
This slide covers the critical timing relationships between interval, timeout, Time Until Up, and Up Interval. This directly addresses F5CTSLTM2.14: "Determine appropriate monitor and monitor timing based on application and server limitations."
FULL TECHNICAL EXPLANATION
INTERVAL: Frequency of health checks. Every N seconds, the BIG-IP sends a check to each pool member.
- Lower = faster detection, more monitor traffic
- Higher = slower detection, less traffic
- Pool with 100 members, interval=5 = 20 monitor requests/second
TIMEOUT: Maximum window for a successful response. NOT the timeout for a single check.
- The BIG-IP sends checks every [interval] seconds
- If no successful response within [timeout] seconds → member DOWN
- Number of failed checks = timeout / interval (rounded down)
- Default: 16/5 = 3.2 → 3 consecutive failures
WHY TIMEOUT > INTERVAL: If timeout ≤ interval, the member is marked DOWN after the FIRST failed check. A single slow response (GC pause, network blip) causes flapping.
TIME UNTIL UP: After a DOWN member starts responding, it must pass checks for this duration before being promoted to UP. Default 0 = immediate promotion. Set to 30+ seconds for servers that need warm-up time (loading caches, establishing DB connections).
UP INTERVAL: Used with inband + active monitor combinations. When a member is UP, the active monitor checks every [interval]. When DOWN, it checks every [Up Interval] (typically shorter than the inband retry timer). This allows faster recovery detection.
COMMON STUDENT MISTAKES
- Setting timeout = interval → instant DOWN on first failure → flapping
- Not understanding the "3+1" formula: timeout = (interval × 3) + 1 gives 3 failures before DOWN
- Confusing Up Interval with Time Until Up: Up Interval = check frequency when DOWN. Time Until Up = how long good responses must continue before promotion to UP.
PIVOT QUESTION
"An HTTP monitor has interval=10 and timeout=16. A server becomes unresponsive. How many failed checks before DOWN?"
ANSWER: 16 ÷ 10 = 1.6 → 1 failed check. This is problematic — a single slow response marks the member DOWN. Should be timeout=31 for 3 failed checks.
F5 DOCUMENTATION: https://my.f5.com/manage/s/article/K2167, https://my.f5.com/manage/s/article/K13148 (Time Until Up)
EXAM QUESTION PATTERNS
- "Interval=5, Timeout=16. Failed checks before DOWN?" → 3
- "Interval=10, Timeout=16. Failed checks?" → 1 (bad config, will flap)
- "What prevents sending traffic to a server still warming up?" → Time Until Up

## Slide 42
42 © 2026 F5
Status icons and colors
Shape indicates monitor status. Color indicates administrative state.
Shape = monitor result
●
Circle
Monitor reports member is UP and available to receive traffic
◆
Diamond
Monitor reports member is DOWN or not responding to health checks
■
Square
No monitor assigned, or monitor status is unknown/pending
▲
Triangle
Member is available but status is degraded or partially available
Color = admin state
Green
Object is enabled by admin AND monitor reports available
Yellow
Object is enabled but status is degraded or approaching threshold
Red
Object is enabled but monitor reports offline/unavailable
Black
Object has been disabled by administrator
Blue
Status is unknown — no monitor assigned or pending
Key combinations to memorize
Icon | Meaning | Traffic impact | Action required
● | Available (green circle) | Receiving traffic normally | None — healthy state
■ | Unknown (blue square) | Receiving traffic (treated as available) | Assign a monitor for visibility
◆ | Offline — Enabled (red diamond) | NO new traffic. BIG-IP sends RST. | Investigate monitor failure / server health
◆ | Disabled (black diamond) | NO new traffic. Existing conns continue. | Admin chose to disable — intentional
Notes: WHAT THIS SLIDE TEACHES
This dedicated slide breaks down the BIG-IP status icon system into its two dimensions: shape (monitor result) and color (admin state). Students must be able to read status icons in the GUI, Network Map, and CLI output to diagnose issues. This is tested frequently on the exam — scenarios often include "the pool member shows a [color] [shape]" and ask what it means.
FULL TECHNICAL EXPLANATION
THE TWO-DIMENSIONAL ICON SYSTEM:
BIG-IP uses shape AND color together to communicate two independent pieces of information:
1. SHAPE tells you what the MONITOR says about the object's health
2. COLOR tells you what the ADMINISTRATOR has done to the object's state
SHAPES:
- Circle: Monitor says UP. The health check succeeded — the service responded correctly.
- Diamond: Monitor says DOWN. The health check failed — the service didn't respond or responded incorrectly.
- Square: Monitor status is UNKNOWN. Either no monitor is assigned, or the monitor hasn't completed its first check yet.
- Triangle: Status is somewhere between fully available and fully offline — approaching a threshold or partially degraded.
COLORS:
- Green: Enabled AND available. The object is enabled by the admin AND the monitor reports it as healthy. This is the normal operating state.
- Yellow: Enabled but showing a warning condition. The object works but may be approaching a problem (connection count approaching limit, pool member count approaching minimum).
- Red: Enabled but offline. The admin has NOT disabled the object, but the monitor reports it as unhealthy. The BIG-IP actively refuses new traffic (sends TCP RST).
- Black: Disabled by administrator. The admin has manually taken the object out of service. Existing connections continue, but no new connections are accepted.
- Blue: Unknown. No monitor assigned, or the first health check hasn't completed yet. The BIG-IP treats these objects as available by default (sends traffic to them).
KEY INSIGHT: BLUE SQUARE = UNCHECKED = STILL RECEIVES TRAFFIC
Students often assume blue square means "not working." In fact, it means "not monitored" — and unmonitored members receive traffic by default. This is why assigning monitors is critical. Without monitors, a failed server continues to receive traffic, causing errors for clients.
COMMON STUDENT MISTAKES
- Confusing red diamond (monitor failure) with black diamond (admin disabled). Red = something broke. Black = someone chose to disable it.
- Assuming blue square means "offline." Blue square means unchecked — the member receives traffic but isn't being health-checked.
- Not understanding that color and shape convey INDEPENDENT information. Green circle = good. Red circle doesn't exist (a healthy member can't be red). Black diamond = disabled regardless of health.
PIVOT QUESTION
"A pool member shows a blue square. Is it receiving traffic? Should you be concerned?"
ANSWER: Yes, it IS receiving traffic (blue square = unchecked, treated as available by default). Yes, you SHOULD be concerned — without a health monitor, the BIG-IP will continue sending traffic to this member even if the application crashes. Assign an appropriate health monitor immediately.
F5 DOCUMENTATION
- Status icons: https://my.f5.com/manage/s/article/K13132
- Colored status icons: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-pools.html
EXAM QUESTION PATTERNS
- "What does a blue square indicate?" → No monitor assigned, member is unchecked but receiving traffic
- "What does a red diamond indicate?" → Monitor reports DOWN, but admin has NOT disabled it
- "What does a black diamond indicate?" → Admin has disabled the object
- "A member shows green circle. The admin disables it. What icon appears?" → Black diamond

## Slide 43
43 © 2026 F5
Status cascade and state behavior
Monitor results cascade upward: member → pool → virtual server
Cascade rules
Pool status = combined member status
If ANY member is available → pool is available
If ALL members are down → pool is offline
VS status depends on its default pool
If default pool is offline → VS shows offline (red)
Traffic to the VS gets a TCP RST
Node status affects ALL pools
A node monitor (ICMP) marks the node DOWN → ALL pool members using that node IP are marked DOWN across every pool.
Disabled vs Offline
 | Disabled (admin) | Offline (monitor)
Cause | Admin action | Monitor failure
Icon | ◆ Black diamond | ◆ Red diamond
Existing conns | Continue | Continue
New conns | Refused (silent drop) | Refused (RST sent)
Persistence | Honored | Honored
tcpdump | SYN in, no response | SYN in, RST out
Ping VIP | Responds (addr active) | Responds (addr active)
tcpdump is the definitive test: Disabled = SYN arrives, no response leaves (silent drop). Offline = SYN arrives, RST goes back immediately. This is how you tell the difference from the network perspective when the GUI is not accessible.
Force Offline: Immediately terminates ALL connections (existing + new). Use only for emergencies. Regular Disable is graceful — existing connections drain naturally. Check connection count: show ltm pool [name] members | grep -i cur
Notes: WHAT THIS SLIDE TEACHES
This slide covers two critical concepts: (1) how monitor results cascade from member to pool to virtual server, and (2) the behavioral difference between Disabled and Offline states. The cascade model and the Disabled/Offline distinction are among the most frequently tested concepts on the exam.
FULL TECHNICAL EXPLANATION
CASCADE MODEL:
The BIG-IP object hierarchy has dependencies: Virtual Server → Pool → Members → Nodes
Member status: Determined by the health monitor assigned to the pool (or to the individual member if member-specific monitors are configured).
Pool status: Determined by the combined status of its members.
- If at least ONE member is available → pool is available (green)
- If ALL members are unavailable → pool is offline (red)
- If the pool has a minimum active members setting and the count falls below it → pool is offline
Virtual Server status: Determined by the status of its default pool.
- If default pool is available → VS is available
- If default pool is offline → VS is offline
- A VS with no pool assigned → status depends only on its admin state
Node status: A node represents the IP address itself (not the service). Node monitors (ICMP, TCP Echo) check the node. If a node is marked DOWN, ALL pool members using that node's IP are affected across ALL pools. This is a cross-pool dependency — one failed node can take down members in multiple pools.
DISABLED vs OFFLINE — EXAM CRITICAL:
Disabled (Black Diamond):
- CAUSE: Administrator manually disables the object
- EXISTING CONNECTIONS: Continue until client closes them (graceful drain)
- NEW CONNECTIONS: Silently dropped (SYN arrives, BIG-IP doesn't respond — no RST)
- PERSISTENCE: Honored for current session
- tcpdump: SYN packet arrives, NO outgoing packet (silent)
- Use case: Planned maintenance. Disable → wait for connections to drain → perform work.
Offline (Red Diamond):
- CAUSE: Health monitor detects failure (or all members of a pool fail)
- EXISTING CONNECTIONS: Continue (assuming the server is still partially responding)
- NEW CONNECTIONS: BIG-IP sends TCP RST back to client
- tcpdump: SYN arrives, RST goes back to client
- The active RST tells the client immediately that the service is unavailable (vs silent drop where the client waits for timeout)
Force Offline:
- Immediately terminates ALL connections — existing AND new
- More aggressive than Disable
- Use only when you need to take a member out of service immediately (security incident, data corruption)
- TMSH: modify ltm pool [pool] members modify { [ip]:[port] { session user-disabled state user-down } }
COMMON STUDENT MISTAKES
- Thinking Disabled means the server is broken. It's an intentional admin action.
- Expecting ping to fail when a VS is disabled. Ping hits the virtual ADDRESS, which is still active.
- Not understanding that existing connections survive BOTH states. Only new connections are affected.
- Confusing Force Offline with Disable. Force Offline kills everything immediately.
PIVOT QUESTION
"You disable a pool member for maintenance. 30 minutes later, 'show ltm pool [name] members' still shows active connections. Is this a bug?"
ANSWER: No. Disabled members allow existing connections to continue. Long-lived connections (WebSocket, database, FTP) can persist for hours. To verify drain progress, check the 'Cur Sessions' counter. To force drain: either wait, reduce the VS idle timeout temporarily, or use Force Offline (kills all connections immediately).
F5 DOCUMENTATION
- Disabled vs Offline: https://my.f5.com/manage/s/article/K13132
- Force Offline: https://my.f5.com/manage/s/article/K13132
- Pool member status: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-pools.html
EXAM QUESTION PATTERNS
- "All pool members show red diamond. VS status?" → Offline (red) — no available members
- "VS disabled, can you ping VIP?" → Yes — virtual address still active
- "tcpdump shows SYN in, no response. Disabled or Offline?" → Disabled (silent drop)
- "tcpdump shows SYN in, RST out. Disabled or Offline?" → Offline (active RST)

## Slide 44
44 © 2026 F5
Lab 4 — Hands-on exercises
45 minutes | Lab guide: Module 4
# | Activity | Key tasks | Time
1 | Basic Monitoring | ICMP default node monitor, custom HTTP monitor www_test (send/receive strings), reverse monitor test. | 10m
2 | VS Status | Disable/enable VS, tcpdump disabled vs offline, connection limits, existing connections survive disable. | 10m
3 | Pool Member Effects | Apply mysql_monitor (will fail all members). Observe cascade: member DOWN → pool offline → VS offline. Member-specific monitors. | 10m
4 | EAV Monitors | Import external monitor script (curl-based). Apply to pool. Verify members UP via custom script. | 5m
5 | Inband Monitors | Inband + active combo. Stop Apache via Webmin. Observe inband detection. Start Apache, Up Interval recovery. | 10m
Activity 3 is key: mysql_monitor on web servers deliberately fails. Q: How long before pool goes offline? A: timeout=46 seconds. This teaches interval/timeout through direct observation.
Webmin access for Activity 5: https://10.1.1.252:10000 (root/default). Use jump box browser, not UDF TMUI. Stop/Start Apache under Servers > Apache Webserver.
Notes: WHAT THIS SLIDE TEACHES
Lab launch slide with five activities. See Lab 4 v1 notes for complete activity walkthroughs.
KEY TEACHING MOMENTS:
- Activity 1: ICMP vs HTTP content monitors — specificity matters
- Activity 2: Disabled (silent drop) vs Offline (RST) — tcpdump proves it
- Activity 3: mysql_monitor cascade failure — timeout calculation in action
- Activity 4: EAV external scripts — custom health checks
- Activity 5: Inband + active with Up Interval — faster recovery detection
F5 DOCUMENTATION: K2167, K12531, K2282, K45753464

## Slide 45
45 © 2026 F5
Exam checkpoints
Q1
U/A
An HTTP monitor has interval=10 and timeout=16. How many failed checks before the member is marked DOWN? Is this a good configuration?
Q2
U/A
You create an HTTP monitor with send string 'GET /health' (no \r\n\r\n) and receive string '200 OK'. The server is running. Why does the monitor fail?
Q3
U/A
Your active HTTP monitor shows all pool members UP, but users report intermittent errors under load. What monitor type detects this, and how does it work?
Q4
U/A
Monitors work on the active BIG-IP but fail on the standby. Both have identical config. Pool members are on a VLAN with TMM routing only. What do you enable?
Web app → HTTP content monitor | DB → TCP or EAV | Load-dependent failures → Inband | TMM-only routing → In-TMM
Notes: WHAT THIS SLIDE TEACHES
Four checkpoint questions covering timing, send string format, inband monitoring, and In-TMM.
Q1 ANSWER: 16÷10 = 1.6 → 1 failed check. This is a BAD configuration — a single slow response marks the member DOWN. Should be timeout=31 for 3 failures (formula: (10×3)+1=31).
Q2 ANSWER: Missing \r\n\r\n at the end of the send string. Without the empty line that terminates HTTP headers, the server waits for more data. The monitor times out because the server never sends a response. Fix: "GET /health HTTP/1.0\r\n\r\n"
Q3 ANSWER: Inband monitor. It watches actual client traffic for failures instead of sending synthetic health checks. If the server fails only under load (resource exhaustion, thread pool depletion), the active monitor's lightweight check passes while real requests fail. Combine inband with an active monitor + Up Interval for faster recovery.
Q4 ANSWER: Enable In-TMM monitoring on the health monitor. By default, monitors run from the BIG-IP host OS, which has its own routing table. If pool members are only reachable via TMM data plane routing (VLANs, route domains, tunnels), the host OS can't reach them. In-TMM monitoring runs the monitor check inside the TMM process, using TMM's routing table. TMSH: modify ltm monitor http [name] in-tmm enabled. Reference: K45753464.
F5 DOCUMENTATION: K2167, K12531, K45753464, K2282

## Slide 46
46 © 2026 F5
Exam checkpoints (continued)
Q5
U/A
A pool member shows a blue square icon. Is it receiving traffic? What should you do?
Q6
U/A
You disable a pool member. tcpdump shows SYN packets arriving at the VIP but no response leaving. A colleague says the VS is offline. Are they correct? How do you know?
Monitor selection decision tree
Web application → HTTP monitor with send/receive content check
HTTPS backend → HTTPS monitor
Database (MySQL, PostgreSQL) → TCP monitor on DB port, or EAV with SQL query
Complex multi-step health check → External (EAV) monitor with custom script
Reduce synthetic monitor traffic → Inband + active with Up Interval
Pool members only reachable via TMM routing → Enable In-TMM on the monitor
Basic node reachability → ICMP (default node monitor, least specific)
Notes: WHAT THIS SLIDE TEACHES
Final checkpoint questions testing status icon interpretation and disabled vs offline diagnosis.
Q5 ANSWER: YES, it IS receiving traffic. Blue square = unchecked (no monitor assigned). The BIG-IP treats unmonitored members as available and sends traffic to them. This is dangerous — if the application crashes, the BIG-IP continues sending traffic. Assign an appropriate health monitor (HTTP for web apps, TCP for other services).
Q6 ANSWER: The colleague is WRONG. The tcpdump shows SYN in, NO response — this is the signature of a DISABLED state (admin action), not OFFLINE. If the VS were OFFLINE (monitor failure), tcpdump would show SYN in, RST out. The silent drop (no response) indicates an administrator has disabled the object. Check: show ltm virtual [name] — look for "State: disabled" vs "Availability: offline".
F5 DOCUMENTATION
- Status icons: https://my.f5.com/manage/s/article/K13132
- Monitor overview: https://my.f5.com/manage/s/article/K12531
- In-TMM: https://my.f5.com/manage/s/article/K45753464

## Slide 47
F5CTSLTM6.01 | A/E | Given headers/captures, determine HTTP/HTTPS solution
F5CTSLTM6.02 | A/E | Given packet capture through LTM, determine root cause
F5CTSLTM6.03 | A/E | Given packet capture, determine HTTPS problem solution
F5CTSLTM6.04 | U/A | Determine where to collect protocol analyzer data
LAB 5
SSL Certificates and Profiles
Create and import SSL certificates, build custom Client-SSL and Server-SSL
profiles, walk through TLS negotiation, and capture decrypted traffic
with tcpdump --f5 ssl provider.
50 min | 20 min slides + 30 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 5: SSL. Maps to exam F5CTSLTM6-B (three A/E objectives + one U/A). The expanded version now includes a full TLS negotiation walkthrough and replaces the legacy ssldump tool with the modern tcpdump --f5 ssl provider for decrypted packet capture.
FULL TECHNICAL EXPLANATION
This lab teaches the complete SSL workflow on the BIG-IP: certificate management, SSL profile configuration, and TLS troubleshooting. The concept slides go deeper than the lab exercises, covering the full TLS 1.2 negotiation step-by-step and the F5 SSL provider for tcpdump that captures decrypted application data alongside encrypted traffic.
301a OBJECTIVES: 1.11–1.12
F5 DOCUMENTATION
- Client-SSL: https://my.f5.com/manage/s/article/K14783
- Server-SSL: https://my.f5.com/manage/s/article/K14806
- tcpdump SSL provider: https://my.f5.com/manage/s/article/K50557518
- Cipher suites: https://my.f5.com/manage/s/article/K15194

## Slide 48
48 © 2026 F5
SSL certificate lifecycle
Manage certificates on the BIG-IP: create, import, renew, and monitor expiration
1 Create or import
Self-signed: System > SSL Certificate List > Create. CA-signed: generate CSR, submit to CA, import signed cert. Import key FIRST, then certificate.
2 Assign to profile
Client-SSL or Server-SSL profile. Select cert + key in Certificate Key Chain. Click Add before Finish (11.6+). Can add RSA + ECDSA dual certs.
3 Attach to VS
Client-SSL: context clientside. Server-SSL: context serverside. Test with browser. Verify cert details via padlock icon.
4 Renew / monitor
Track expiration dates. Replace cert in profile — no restart needed. New conns use new cert immediately. Use iCall scripts for alerts.
Certificate types
Type | Issued by | Browser trust | Use case
Self-signed | BIG-IP itself | Not trusted (warning) | Lab, testing, internal apps, server-side re-encryption
CA-signed | Certificate Authority (DigiCert, Let's Encrypt) | Trusted ✔ | Production external-facing applications
Wildcard | CA — covers *.domain.com | Trusted ✔ | Multiple virtual servers on same domain
SAN / UCC | CA — multiple CN entries | Trusted ✔ | Multiple different domains on one certificate
Notes: WHAT THIS SLIDE TEACHES
Covers the complete SSL certificate lifecycle on the BIG-IP (301a 1.12). See Lab 5 v1 slide 2 notes for the full standalone documentation including CSR process, import order, and zero-downtime renewal.
KEY POINTS: Import KEY first then cert. Click "Add" in Certificate Key Chain. Self-signed triggers browser warning but still encrypts. CA-signed requires CSR workflow. Replace cert in profile for zero-downtime renewal.
F5 DOCUMENTATION: K14620 (cert management), K13838 (CSR), K15564 (cert/key validation)

## Slide 49
49 © 2026 F5
SSL profile settings
Key options in Client-SSL and Server-SSL profiles
Setting | Client-SSL | Server-SSL | What it controls
Certificate | Server cert for clients | Client cert for backend (opt) | Identity the BIG-IP presents to the connecting party
Key | Private key (must match cert) | Private key (must match cert) | BIG-IP validates cert/key match at configuration time
Chain | Intermediate CA cert(s) | N/A | Completes trust chain for client verification. Client-SSL only.
Ciphers | Cipher string for clients | Cipher string for servers | OpenSSL format. Controls which suites are offered/accepted.
Options | Disable SSLv3, TLS 1.0/1.1 | Disable old versions | Protocol version control. Modern: TLS 1.2 + 1.3 only.
Client Auth | Verify client certificates | N/A | Mutual TLS — BIG-IP requests cert from client.
Server Auth | N/A | Validate server cert | BIG-IP verifies backend cert. Disabled by default.
Cipher hardening: DEFAULT:!SSLv3:!TLSv1:!TLSv1_1:!RC4:!3DES | Test before applying: tmm --clientciphers 'cipher_string'
SNI (Server Name Indication)
Allows multiple certificates on one VIP. Client sends hostname in ClientHello; BIG-IP selects matching cert. Configure multiple cert/key chains in one Client-SSL profile, or use separate profiles with SNI matching. Required when hosting multiple HTTPS sites on the same IP:443.
Notes: WHAT THIS SLIDE TEACHES
SSL profile settings reference from F5 operations guide Table 5.5. See Lab 5 v1 slide 3 notes for complete standalone documentation including cipher string syntax, mTLS, Server Authentication implications, and SNI configuration.
KEY EXAM POINTS: Chain cert = intermediate CA for trust chain (Client-SSL only). Server Auth disabled by default = BIG-IP accepts any backend cert. Cipher string tested with tmm --clientciphers. SNI allows multiple certs per VIP.
F5 DOCUMENTATION: K14783 (Client-SSL), K14806 (Server-SSL), K15194 (ciphers), K13452 (SNI)

## Slide 50
50 © 2026 F5
TLS 1.2 negotiation walkthrough
Every TLS connection follows this sequence. Understanding each message is essential for troubleshooting.
1
▶
ClientHello
Client
TLS versions, cipher suites, SNI hostname, random bytes, session ID, extensions (ALPN for HTTP/2)
2
◀
ServerHello
BIG-IP
Chosen TLS version + cipher suite, server random bytes, session ID
3
◀
Certificate
BIG-IP
BIG-IP sends its server certificate (from Client-SSL profile) + chain certs
4
◀
ServerKeyExchange
BIG-IP
DH/ECDHE parameters for key exchange (not sent with RSA key exchange)
5
◀
CertificateRequest
BIG-IP
Only if mutual TLS (Client Auth) is enabled. Asks client for its certificate.
6
◀
ServerHelloDone
BIG-IP
Signals end of server's hello messages. Client can now respond.
7
▶
ClientKeyExchange
Client
Client's key exchange data (pre-master secret encrypted with server's public key, or DH params)
8
▶◀
ChangeCipherSpec + Finished
Both
Both sides switch to encrypted communication. Finished messages verify handshake integrity.
✔ Application data now flows encrypted | TLS 1.3 simplifies this to 1 round-trip (ClientHello + ServerHello with key share = immediate encryption)
Notes: WHAT THIS SLIDE TEACHES
This slide walks through the complete TLS 1.2 handshake message-by-message. Students must understand this flow to diagnose failures in packet captures, which is the core skill tested in F5CTSLTM6-B (objectives 6.01, 6.02, 6.03). Every handshake failure maps to a specific point in this sequence.
FULL TECHNICAL EXPLANATION
MESSAGE 1: ClientHello (Client → BIG-IP)
The client initiates the TLS connection by sending:
- Supported TLS versions: e.g., TLS 1.0, 1.1, 1.2 (listed from highest to lowest preference)
- Cipher suites: Ordered list of algorithms the client supports (e.g., TLS_ECDHE_RSA_WITH_AES_256_GCM_SHA384)
- SNI extension: The hostname the client wants to connect to (e.g., www.example.com). This allows the BIG-IP to select the correct certificate when multiple sites share one VIP.
- Client random: 32 bytes of random data used for key derivation
- Session ID: For session resumption (empty on first connection)
- Compression methods: Usually just "null" (TLS compression is deprecated)
- Extensions: ALPN (Application-Layer Protocol Negotiation — used for HTTP/2), supported groups (for ECDHE curves), signature algorithms
WIRESHARK FILTER: tls.handshake.type == 1
WHAT TO CHECK IN ClientHello:
- Which TLS versions does the client offer? If it only offers TLS 1.0 and the BIG-IP has it disabled → handshake fails
- Which cipher suites? If none overlap with the BIG-IP's cipher string → "no shared cipher" error
- Is SNI present? If the BIG-IP uses SNI-based certificate selection and the client doesn't send SNI → wrong cert presented
MESSAGE 2: ServerHello (BIG-IP → Client)
The BIG-IP selects from the client's offerings:
- Chosen TLS version: The highest version both sides support
- Chosen cipher suite: The BIG-IP's preferred cipher from the client's list (server preference by default)
- Server random: 32 bytes of random data
- Session ID: For session resumption or a new session
WIRESHARK FILTER: tls.handshake.type == 2
IF NO ServerHello IS SENT: The BIG-IP couldn't find any acceptable combination of TLS version + cipher suite. It sends a fatal "handshake_failure" alert instead, which terminates the connection.
MESSAGE 3: Certificate (BIG-IP → Client)
The BIG-IP sends its server certificate (from the Client-SSL profile's Certificate Key Chain):
- The certificate itself (contains the public key, CN, SAN, validity dates)
- Chain certificates (intermediate CA certs that bridge to the root CA)
- The client validates the certificate: checks the issuer chain, expiration, CN/SAN match, revocation status
COMMON FAILURES AT THIS POINT:
- Certificate CN doesn't match the requested hostname → ERR_CERT_COMMON_NAME_INVALID
- Certificate is expired → ERR_CERT_DATE_INVALID
- Missing chain certificate → ERR_CERT_AUTHORITY_INVALID (client can't verify the issuer)
- Self-signed certificate → ERR_CERT_AUTHORITY_INVALID (no trusted root)
MESSAGE 4: ServerKeyExchange (BIG-IP → Client)
Only sent for DHE and ECDHE key exchanges (Perfect Forward Secrecy). Contains the server's DH/ECDHE parameters.
NOT sent for RSA key exchange — the client encrypts the pre-master secret directly with the server's RSA public key from the certificate.
WHY THIS MATTERS: ECDHE provides PFS — even if the private key is compromised later, past sessions can't be decrypted. RSA key exchange does NOT have this property.
MESSAGE 5: CertificateRequest (BIG-IP → Client) — OPTIONAL
Only sent if mutual TLS (Client Authentication) is enabled in the Client-SSL profile. The BIG-IP requests a certificate from the client and specifies:
- Acceptable certificate types
- Acceptable certificate authorities (CAs the client cert must be signed by)
If the client doesn't have a valid certificate → handshake fails with "certificate_required" or "bad_certificate" alert.
MESSAGE 6: ServerHelloDone (BIG-IP → Client)
A simple message indicating the BIG-IP has finished sending its hello messages. The client can now respond.
MESSAGE 7: ClientKeyExchange (Client → BIG-IP)
The client sends its key exchange data:
- For RSA: A pre-master secret encrypted with the server's public key. Only the server (with its private key) can decrypt it.
- For ECDHE: The client's DH public value. Combined with the server's DH parameters, both sides can compute the same shared secret.
If the certificate and key in the Client-SSL profile DON'T MATCH → the BIG-IP can't decrypt the pre-master secret → handshake fails
MESSAGE 8: ChangeCipherSpec + Finished (Both)
Both sides:
1. Send ChangeCipherSpec: "From now on, all messages are encrypted"
2. Send Finished: A hash of all handshake messages, encrypted with the new session key. This proves:
- Neither side's messages were tampered with during the handshake
- Both sides computed the same session key
After Finished, application data flows encrypted.
TLS 1.3 DIFFERENCES:
TLS 1.3 reduces the handshake to 1 round-trip:
- ClientHello includes key_share extension (client's DH public value)
- ServerHello includes the server's key_share
- Both sides can derive keys after just 1 exchange
- The Certificate and Finished messages are encrypted in TLS 1.3 (in TLS 1.2 they're plaintext)
COMMON STUDENT MISTAKES
- Not understanding that the ServerKeyExchange message is only present for DHE/ECDHE, not RSA
- Confusing ClientHello (from the client) with ServerHello (from the BIG-IP) in packet captures
- Not checking the SNI extension in ClientHello when troubleshooting wrong-certificate issues
PIVOT QUESTION
"In Wireshark, you see ClientHello → ServerHello → Certificate → Alert (fatal: bad_certificate). At what stage did the negotiation fail, and what's the likely cause?"
ANSWER: The failure occurred after the BIG-IP sent its Certificate message. The "bad_certificate" alert means the client rejected the BIG-IP's certificate. Common causes: certificate CN/SAN doesn't match the hostname, certificate is expired, self-signed without the client trusting the CA, or missing chain certificate. Check the certificate's CN, SAN, expiration, and chain in the Client-SSL profile.
F5 DOCUMENTATION
- TLS handshake: https://my.f5.com/manage/s/article/K15292
- TLS 1.3 on BIG-IP: https://my.f5.com/manage/s/article/K44134926
- Wireshark TLS analysis: https://wiki.wireshark.org/TLS
EXAM QUESTION PATTERNS
- "What message does the BIG-IP send its certificate in?" → Certificate (message 3)
- "What triggers a CertificateRequest?" → Client Authentication (mutual TLS) enabled in Client-SSL
- "ServerKeyExchange is missing from the capture. Is this normal?" → Yes, if RSA key exchange is used (no PFS)

## Slide 51
51 © 2026 F5
Capturing decrypted SSL with tcpdump
Use the F5 SSL provider to capture decrypted application data alongside encrypted traffic
Capture with F5 SSL provider
tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/ssl_capture.pcap --f5 ssl
-nni 0.0:nnnp
Capture on all VLANs (0.0) with the :nnnp modifier that adds peer flow data to each packet. This captures both client-side and server-side traffic in one file.
-s0
Full packet capture — no truncation. Required for TLS analysis where you need complete handshake messages.
-w /var/tmp/file.pcap
Write to file for Wireshark analysis. Do NOT output to screen for SSL troubleshooting — use Wireshark.
--f5 ssl
Enables the F5 SSL provider. TMM intercepts the SSL flow and writes DECRYPTED application data into the capture alongside the encrypted packets. Works with ALL cipher suites including ECDHE/PFS.
Why tcpdump --f5 ssl replaces ssldump
 | ssldump (legacy) | tcpdump --f5 ssl (modern)
PFS/ECDHE | Cannot decrypt ✘ | Decrypts all ciphers ✔
TLS 1.3 | Not supported ✘ | Fully supported ✔
Process | Capture, then decrypt offline | Decrypted data captured inline
Key needed | Requires private key file | No key needed — TMM provides data
Notes: WHAT THIS SLIDE TEACHES
This slide introduces the F5 SSL provider for tcpdump — the modern method for capturing decrypted SSL traffic on the BIG-IP. This replaces the legacy ssldump tool and directly addresses F5CTSLTM6.04: "Explain how to decrypt SSL traffic for protocol analysis."
FULL TECHNICAL EXPLANATION
THE F5 SSL PROVIDER (tcpdump --f5 ssl):
Starting in BIG-IP 14.0+, the tcpdump utility includes an F5-specific provider that hooks into TMM's SSL processing pipeline. When you add --f5 ssl to a tcpdump command, TMM intercepts the SSL flow and injects the DECRYPTED application data into the packet capture alongside the encrypted traffic.
THE COMMAND:
tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/ssl_capture.pcap --f5 ssl
BREAKDOWN:
- -nni 0.0: Capture on all VLANs (0.0 is a special BIG-IP interface that captures all TMM-processed traffic)
- :nnnp: A BIG-IP-specific modifier that adds peer flow information to each packet. This is critical because it shows BOTH the client-side and server-side of the same flow in one capture, with annotations showing which side each packet belongs to.
- -s0: Full packet capture (no truncation). Essential for TLS — truncated packets can't be analyzed.
- -w /var/tmp/ssl_capture.pcap: Write to file for Wireshark analysis
- --f5 ssl: Enable the SSL provider. This is the key flag.
WHAT THE CAPTURE CONTAINS:
When you open the .pcap in Wireshark (with the F5 Wireshark plugin installed), you see:
1. The encrypted TLS packets (ClientHello, ServerHello, etc.) — as you'd see in any capture
2. PLUS decrypted "inner" packets showing the actual HTTP requests and responses in plaintext
3. PLUS F5 metadata showing which VLAN, virtual server, and pool member processed each packet
This means you can see BOTH the encrypted handshake AND the decrypted application data in the same file — no separate decryption step needed.
WHY THIS REPLACES ssldump:
1. PFS/ECDHE support: ssldump requires the server's private key to decrypt traffic. With ECDHE (Perfect Forward Secrecy), the private key alone cannot decrypt — each session uses unique ephemeral keys. The F5 SSL provider works because it captures the decrypted data directly from TMM's memory, not by decrypting the capture offline.
2. TLS 1.3: ssldump does not support TLS 1.3. The F5 SSL provider fully supports it.
3. No key file needed: ssldump requires you to specify -k /path/to/key. The F5 SSL provider gets the decrypted data from TMM directly — no private key file needed on the command line.
4. Inline capture: ssldump is a separate offline process (capture first, then decrypt). The F5 SSL provider captures decrypted data in real-time as part of the tcpdump.
USING THE CAPTURE IN WIRESHARK:
1. Install the F5 Wireshark plugin (available from downloads.f5.com or the F5 GitHub repo)
2. Open the .pcap in Wireshark
3. The plugin adds F5-specific columns: F5 Virtual Server, F5 Flow, F5 Peer
4. Decrypted HTTP data appears as separate "inner" packets alongside the encrypted outer packets
5. You can filter on HTTP methods, status codes, headers — even though the traffic was TLS-encrypted on the wire
ALTERNATIVE CAPTURE VARIATIONS:
- Capture on specific VLAN: tcpdump -nni client_vlan:nnnp -s0 -w /var/tmp/client.pcap --f5 ssl
- Capture for specific VIP: tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/capture.pcap --f5 ssl host 10.1.10.115
- Capture without SSL provider (encrypted only): tcpdump -nni client_vlan -s0 -w /var/tmp/encrypted.pcap host 10.1.10.115 and port 443
COMMON STUDENT MISTAKES
- Forgetting --f5 ssl flag and wondering why the capture only shows encrypted data
- Not using :nnnp modifier — without it, you don't see the peer flow data (client-side vs server-side)
- Capturing on a specific VLAN instead of 0.0 — you miss the other side of the connection
- Not installing the F5 Wireshark plugin — without it, the F5 metadata and decrypted packets don't display properly
PIVOT QUESTION
"You need to capture and analyze the HTTP request/response flowing through an HTTPS virtual server that uses ECDHE ciphers. What tcpdump command do you use?"
ANSWER: tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/ssl_capture.pcap --f5 ssl host 10.1.10.115
The --f5 ssl provider captures the decrypted HTTP data inline, regardless of cipher suite (including ECDHE). No private key needed. Open in Wireshark with the F5 plugin to see both encrypted TLS and decrypted HTTP.
F5 DOCUMENTATION
- tcpdump SSL provider: https://my.f5.com/manage/s/article/K50557518
- F5 Wireshark plugin: https://my.f5.com/manage/s/article/K03590185
- tcpdump on BIG-IP: https://my.f5.com/manage/s/article/K411
- Packet capture best practices: https://my.f5.com/manage/s/article/K4714
EXAM QUESTION PATTERNS
- "How do you decrypt ECDHE/PFS traffic on the BIG-IP?" → tcpdump --f5 ssl (not ssldump)
- "What does the :nnnp modifier do?" → Adds peer flow data showing both sides of the connection
- "What Wireshark plugin is needed for F5 captures?" → F5 Wireshark plugin (f5-wireshark-plugin)

## Slide 52
52 © 2026 F5
Lab 5 — Hands-on exercises
30 minutes | Lab guide: Module 5
# | Activity | Key tasks | Time
1 | Create client cert | Self-signed, CN=ltm301a.f5demo.com, 2048-bit RSA, 365 days. | 5m
2 | Import server cert | Import KEY first (import_ssl_cert), then CERT with same name. | 5m
3 | Create SSL profiles | my-client-ssl + my-server-ssl. Click Add in Certificate Key Chain. | 10m
4 | Apply and test | Replace default SSL profiles on secure_vs. Browse https://10.1.10.115. Verify cert in browser. | 10m
Import KEY first: Validates cert/key match. If cert imported first, a mismatched key with the same name could be accepted without validation.
Click 'Add': In BIG-IP 11.6+, selecting a cert/key in the Certificate Key Chain is NOT enough. You must click 'Add' to save the pair. Without it, the profile has no cert attached.
Notes: WHAT THIS SLIDE TEACHES
Lab launch for the SSL hands-on exercises. See Lab 5 v1 slide 5 notes for complete activity walkthroughs.
KEY TEACHING MOMENTS: Import key first, click Add, verify cert in browser padlock. Lab uses 2048-bit for client-facing, 1024-bit for server-facing (intentional to show different key strengths per side).
F5 DOCUMENTATION: K14620, K14783, K14806

## Slide 53
53 © 2026 F5
Exam checkpoints
Q1
A/E
tcpdump shows ClientHello from client, then TCP RST from BIG-IP. No ServerHello sent. What is the most likely cause?
Q2
A/E
Users report ERR_CERT_AUTHORITY_INVALID. The cert is CA-signed and not expired. What configuration is missing?
Q3
U/A
You need to capture decrypted HTTP flowing through an HTTPS VS using ECDHE ciphers. What tcpdump command captures the decrypted data?
Q4
A/E
After enabling Server Authentication on Server-SSL, all traffic fails. Backend uses self-signed certs. What happened?
Exam F5CTSLTM6-B is entirely scenario-based. You must read packet captures and diagnose SSL problems, not just recall settings.
Notes: WHAT THIS SLIDE TEACHES
Four checkpoint questions matching the A/E level of F5CTSLTM6-B.
Q1 ANSWER: No common TLS version or cipher suite. BIG-IP received ClientHello, found no overlap with its cipher string, sent fatal alert (appears as RST). Fix: broaden cipher string or update client. Test: tmm --clientciphers 'string'.
Q2 ANSWER: Missing chain certificate in Client-SSL profile. Browser can't verify trust chain without intermediate CA cert. Fix: add chain cert to profile.
Q3 ANSWER: tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/ssl.pcap --f5 ssl host <VIP>
The --f5 ssl provider captures decrypted HTTP alongside encrypted TLS. Works with ECDHE/PFS — no private key needed. Open in Wireshark with F5 plugin.
Q4 ANSWER: Server Authentication validates backend cert. Self-signed certs aren't in any trusted CA list → validation fails → all server-side connections rejected. Fix: import backend self-signed certs as Trusted Server CAs, or disable Server Authentication.
F5 DOCUMENTATION: K15292 (handshake troubleshooting), K50557518 (tcpdump SSL provider), K13302 (chain certs), K14806 (Server-SSL)

## Slide 54
54 © 2026 F5
SSL troubleshooting reference
Commands and Wireshark filters for SSL analysis on the BIG-IP
Pass-through
No SSL profiles
No L7. FastL4.
Offload
Client-SSL only
Full L7. HTTP to server.
Re-encryption
Client-SSL + Server-SSL
Full L7. End-to-end.
Essential commands
Task | Command
Capture with SSL decryption | tcpdump -nni 0.0:nnnp -s0 -w /var/tmp/ssl.pcap --f5 ssl host <VIP>
Capture client-side only | tcpdump -nni client_vlan:nnnp -s0 -w /var/tmp/client.pcap --f5 ssl host <VIP> and port 443
Capture server-side only | tcpdump -nni server_vlan:nnnp -s0 -w /var/tmp/server.pcap --f5 ssl host <member> and port 443
Test cipher string | tmm --clientciphers 'DEFAULT:!SSLv3:!RC4:!3DES'
Check cert expiration | openssl x509 -in /config/ssl/ssl.crt/<cert>.crt -noout -dates
Verify cert/key match | openssl x509 -noout -modulus -in cert.crt ¦ md5sum && openssl rsa -noout -modulus -in key.key ¦ md5sum
View SSL errors in log | tail -f /var/log/ltm ¦ grep -i ssl
Test TLS connection | openssl s_client -connect <VIP>:443 -showcerts -servername <hostname>
Wireshark display filters for TLS
tls.handshake.type==1 (ClientHello) | tls.handshake.type==2 (ServerHello) | tls.alert_message (errors) | http (decrypted)
Notes: WHAT THIS SLIDE TEACHES
Quick-reference slide with the three SSL modes, essential troubleshooting commands (using tcpdump --f5 ssl, NOT ssldump), and Wireshark filters.
KEY CHANGES FROM v1:
- ALL ssldump references removed
- Replaced with tcpdump --f5 ssl provider
- Added openssl s_client for testing TLS connections
- Added :nnnp modifier to all tcpdump commands for peer flow data
THE F5 SSL PROVIDER ADVANTAGE:
tcpdump --f5 ssl captures decrypted application data inline, regardless of cipher suite. It works with ECDHE/PFS and TLS 1.3 because it hooks into TMM's SSL processing pipeline — it doesn't try to decrypt offline like ssldump.
WIRESHARK FILTERS:
- tls.handshake.type == 1: ClientHello (client's initial message)
- tls.handshake.type == 2: ServerHello (server's response with chosen cipher)
- tls.handshake.type == 11: Certificate (server's certificate message)
- tls.handshake.type == 12: ServerKeyExchange (DHE/ECDHE parameters)
- tls.alert_message: Any TLS alert (errors, warnings)
- http: Decrypted HTTP traffic (visible with F5 SSL provider captures)
- f5ethtrailer.ingress: 1 (ingress packets) or 0 (egress packets) — F5 plugin filter
F5 DOCUMENTATION
- tcpdump SSL provider: https://my.f5.com/manage/s/article/K50557518
- F5 Wireshark plugin: https://my.f5.com/manage/s/article/K03590185
- openssl s_client: https://my.f5.com/manage/s/article/K15292
- Cipher testing: https://my.f5.com/manage/s/article/K15194
EXAM QUESTION PATTERNS
- "How do you capture decrypted HTTPS traffic?" → tcpdump --f5 ssl
- "What Wireshark filter shows TLS handshake errors?" → tls.alert_message
- "How do you verify a cert/key pair match?" → Compare MD5 of modulus values

## Slide 55
F5CTSLTM2.03 | U/A | Choose VS type and LB type for application requirements
F5CTSLTM2.05 | U/A | Distinguish packet-based vs connection-based load balancing
F5CTSLTM2.07 | U/A | Identify matching order of multiple virtual servers
F5CTSLTM2.08 | U/A | Determine how to secure virtual servers
LAB 6
Virtual Servers and
Packet Processing
Compare VS types (Standard, Performance L4, Forwarding IP), understand
the packet processing order, predict VS matching with wildcards, and
distinguish packet-based vs connection-based load balancing.
60 min | 15 min slides + 45 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 6. This lab is described in the lab guide as "a review but an important one — these concepts are vital to passing the 301a." It covers virtual server types, the packet processing order, VS matching precedence, and packet filters.
FULL TECHNICAL EXPLANATION
Lab 6 has four activities:
1. Packet Processing: tcpdump and connection table to observe client-side/server-side flows, SNAT behavior
2. Packet Filter: Create and test packet filters, learn the 7-step packet processing order
3. VS Packet Processing: Wildcard VS, host VS vs wildcard matching, source address filtering
4. Forwarding VS: IP forwarding and transparent (Performance L4) virtual servers
BETA BLUEPRINT COVERAGE
- F5CTSLTM2.03 (U/A): "Choose virtual server type and load balancing type." Sub-bullets: L2-L3 VS types, Standard vs FastL4, LB methods.
- F5CTSLTM2.05 (U/A): "Distinguish packet-based vs connection-based load balancing." Sub-bullets: when to use each.
- F5CTSLTM2.07 (U/A): "Identify the matching order of multiple virtual servers." Sub-bullets: which VS processes traffic, why VS fails to receive traffic.
- F5CTSLTM2.08 (U/A): "Determine how to secure virtual servers." Sub-bullets: limit access, compare VS types.
301a OBJECTIVES: 1.13–1.15
F5 DOCUMENTATION
- VS types: https://my.f5.com/manage/s/article/K55185917
- Packet processing order: https://my.f5.com/manage/s/article/K8082
- VS matching: https://my.f5.com/manage/s/article/K14800
EXAM QUESTION PATTERNS
- "Which VS type should you use for a web application?" → Standard
- "What is the packet processing order?" → Existing conns → Packet filter → VS → SNAT → NAT → Self IP → Drop

## Slide 56
56 © 2026 F5
Virtual server types
Choose the type based on the level of traffic intelligence your application requires
Type | Profile | Processing | L7 features | Use case
Standard | TCP, HTTP, SSL, etc. | Full proxy: two independent TCP connections | All: HTTP, SSL, compression, iRules, persistence | Web apps, APIs — any app needing L7
Performance (L4) | FastL4 | Packet-by-packet pass-through | None: no L7 inspection possible | High throughput L4 LB, non-HTTP
Forwarding (IP) | FastL4 or none | Route based on dest IP, no pool | None: acts as a router | Allow traffic to backend network
Forwarding (L2) | None | Bridge based on MAC, no pool | None: acts as a bridge | L2 transparent deployment
Reject | None | Sends RST (TCP) or ICMP unreachable (UDP) | None: actively refuses traffic | Block specific ports with proper reset
Standard vs Performance (L4)
Standard (full proxy)
Client SYN → BIG-IP completes handshake → reads HTTP → makes LB decision → opens NEW connection to server with different seq numbers. Two fully independent TCP sessions.
Performance L4 (packet-by-packet)
Client SYN → BIG-IP makes LB decision on FIRST packet → forwards SYN to server (with NAT). No separate handshake. Packets pass through with address translation only.
Notes: WHAT THIS SLIDE TEACHES
This slide covers all virtual server types on the BIG-IP, supporting F5CTSLTM2.03: "Choose virtual server type and load balancing type to fit application requirements." Students must understand the trade-offs: Standard gives full L7 intelligence at the cost of CPU; Performance L4 gives maximum throughput but no L7.
FULL TECHNICAL EXPLANATION
STANDARD VIRTUAL SERVER — FULL PROXY:
When a Standard VS with a TCP profile receives a connection:
1. Client sends SYN to VIP → BIG-IP completes the three-way handshake (SYN-ACK, ACK)
2. BIG-IP waits for client data (if HTTP profile is present, it waits for the HTTP request)
3. BIG-IP parses the request and makes a load balancing decision
4. BIG-IP opens a NEW, INDEPENDENT TCP connection to the selected pool member
5. The two connections have different sequence numbers, window sizes, and potentially different TCP options
6. The BIG-IP can modify data between the two connections (HTTP headers, compression, SSL)
This full proxy architecture enables ALL L7 features: HTTP inspection, SSL termination, compression, caching, cookie persistence, iRules, OneConnect, content switching.
PERFORMANCE (LAYER 4) VIRTUAL SERVER — PACKET-BY-PACKET:
1. Client sends SYN to VIP → BIG-IP makes LB decision immediately (on first packet)
2. BIG-IP forwards the SYN to the selected pool member with destination NAT
3. Server responds with SYN-ACK → BIG-IP forwards back to client with source NAT
4. All subsequent packets pass through with address translation — no TCP reassembly
5. The BIG-IP does NOT maintain a complete TCP state machine — it tracks connections minimally
Because there's no L7 inspection, Performance L4 is MUCH faster for raw throughput. On hardware platforms with PVA (Packet Velocity ASIC), connections can be offloaded to dedicated hardware for line-rate performance.
FORWARDING (IP) VIRTUAL SERVER:
- No pool, no load balancing
- Uses the BIG-IP's routing table to forward traffic based on destination IP
- Acts like a router — allows traffic from specific sources to reach specific networks
- Lab exercise: Create a Forwarding IP VS that allows 10.1.10.0/24 to reach 10.1.20.0/24
- Must set Protocol to "All Protocols" (not just TCP) for general forwarding
- The VS is green only if there's a route to the destination network
FORWARDING (L2) VIRTUAL SERVER:
- Operates at Layer 2 (MAC addresses)
- Bridges traffic between VLANs without routing
- Used in transparent deployments where the BIG-IP sits inline but doesn't change IP addresses
- Rare in modern deployments
REJECT VIRTUAL SERVER:
- No pool, no forwarding
- Actively refuses connections: sends TCP RST or ICMP unreachable
- Use case: Block specific traffic to a VIP with a proper rejection (instead of silent drop)
- Example: Create a reject VS on port 23 (Telnet) to actively refuse Telnet connections
TRANSPARENT VS (from lab activity 4):
A Performance (Layer 4) VS with a wildcard port (*) and Address Translation enabled but Port Translation disabled. Traffic is sent to the pool using the ORIGINAL destination port. This allows multiple services (HTTP, HTTPS, SSH, DNS) to pass through to the same pool without creating separate VS per port.
COMMON STUDENT MISTAKES
- Using Standard when Performance L4 would suffice (wastes CPU for non-HTTP traffic)
- Using Performance L4 when they need HTTP features (compression, iRules, SSL offload)
- Forgetting to set Protocol to "All Protocols" on Forwarding IP VS — defaults to TCP only
- Not understanding that Forwarding IP VS has no pool — it uses the routing table
PIVOT QUESTION
"You need to load balance MySQL database connections on port 3306. You don't need to inspect the MySQL protocol. Which VS type do you use, and why?"
ANSWER: Performance (Layer 4) with a FastL4 profile. MySQL is not HTTP — you don't need L7 inspection, SSL, or HTTP profiles. Performance L4 provides maximum throughput with minimum CPU overhead. Use a TCP monitor on port 3306 for health checking.
F5 DOCUMENTATION
- VS types: https://my.f5.com/manage/s/article/K55185917
- Standard VS TCP flow: https://my.f5.com/manage/s/article/K8082
- Performance L4 VS: https://my.f5.com/manage/s/article/K55185917
- Forwarding VS: https://my.f5.com/manage/s/article/K7595
EXAM QUESTION PATTERNS
- "Which VS type for web applications?" → Standard (need L7)
- "Which VS type for maximum throughput without L7?" → Performance (Layer 4)
- "Which VS type acts as a router?" → Forwarding (IP)
- "What's the difference between Standard and Performance L4?" → Standard = full proxy (two TCP connections). L4 = packet-by-packet (one flow with NAT)

## Slide 57
57 © 2026 F5
Packet processing order
The BIG-IP evaluates inbound packets in this exact priority order
1
Existing connections
If the packet matches an existing connection in the connection table, it follows that connection. No further processing.
▼
2
Packet filters (AFM)
If packet filters are enabled, the packet is evaluated against filter rules. If a filter matches with Discard, the packet is dropped before reaching any VS.
▼
3
Virtual server
The BIG-IP matches the packet against configured virtual servers using the VS matching order (most specific first). If a match is found, the VS processes the traffic.
▼
4
SNAT
If no VS matches but a SNAT object matches the source address, the BIG-IP translates the source IP and forwards the packet.
▼
5
NAT
If no VS or SNAT matches but a NAT object matches, the packet is forwarded with address translation.
▼
6
Self IP
If the destination IP matches a BIG-IP self IP, TMM processes the packet locally (management, routing protocols, health monitor responses).
▼
7
Drop
If nothing matches, the packet is silently dropped. No RST, no ICMP unreachable. The packet disappears.
Packet filters are evaluated BEFORE virtual servers. A filter can block traffic that would otherwise match a VS.
Notes: WHAT THIS SLIDE TEACHES
The packet processing order is one of the most fundamental concepts on the BIG-IP and one of the most frequently tested topics on the exam. Students must be able to prioritize the 7 steps and understand why existing connections take precedence over everything else.
FULL TECHNICAL EXPLANATION
THE SEVEN-STEP PROCESSING ORDER:
STEP 1: EXISTING CONNECTIONS (highest priority)
When a packet arrives, the BIG-IP first checks its connection table. If the packet matches an existing connection (by source IP, source port, destination IP, destination port, protocol), the packet follows that connection — no further evaluation happens.
This is why:
- Disabling a VS doesn't disconnect existing sessions — they're already in the connection table
- Changing a VS configuration doesn't affect active connections until they're re-established
- Packet filters enabled AFTER connections are established don't affect those connections
TMSH: show sys connection cs-client-addr 10.1.10.199
STEP 2: PACKET FILTERS (AFM)
If packet filters are enabled (Network > Packet Filters > General > Enable), each new packet (not matching an existing connection) is evaluated against packet filter rules.
- Rules are evaluated in order (First, Second, Third...)
- If a rule matches with Action: Discard → packet is silently dropped
- If a rule matches with Action: Accept → packet continues to Step 3
- If no rule matches → default action (Accept or Discard based on configuration)
KEY EXAM POINT: Packet filters are evaluated BEFORE virtual servers. This means a packet filter can block traffic that would otherwise be handled by a VS. In the lab, students create a filter blocking FTP to 10.1.10.100 and observe that the ftp_vs never sees the traffic.
STEP 3: VIRTUAL SERVER
The BIG-IP matches the packet against configured virtual servers using the VS matching order (next slide). The most specific match wins.
STEP 4: SNAT (Source NAT)
If no VS matches, the BIG-IP checks for SNAT objects. SNATs translate source addresses for outbound traffic. This allows internal servers to access the internet through the BIG-IP.
STEP 5: NAT
Similar to SNAT but maps one IP to another (1:1 translation).
STEP 6: SELF IP
If the destination IP matches a BIG-IP self IP (the BIG-IP's own address on a VLAN), TMM processes it locally. This handles: routing protocol traffic (BGP, OSPF), health monitor responses (when servers respond to monitors), management traffic through TMM interfaces.
STEP 7: DROP
If no match at any step, the packet is silently dropped. No RST is sent. The client will eventually time out.
WHY MANAGEMENT SSH ISN'T IN THE CONNECTION TABLE:
Lab question: "Why are SSH sessions to the management IP not in the connection table?"
Answer: Management traffic (to the MGMT interface on 10.1.1.4) is handled by the BIG-IP's host OS (Linux), not TMM. The connection table only shows TMM-processed connections. Management traffic never enters TMM's processing pipeline.
COMMON STUDENT MISTAKES
- Not understanding that existing connections are checked FIRST — this is why disabling a VS doesn't disconnect active users
- Thinking packet filters are checked after VS — they're checked BEFORE
- Assuming unmatched packets get a RST — they're silently dropped (no response)
PIVOT QUESTION
"You enable a packet filter to block port 21 (FTP). An existing FTP session continues to work. Why?"
ANSWER: Existing connections (Step 1) are checked before packet filters (Step 2). The FTP session is already in the connection table, so packets for it bypass the packet filter entirely. Only NEW FTP connections will be blocked. To block existing connections, you'd need to clear the connection table: delete sys connection cs-client-addr [ip]
F5 DOCUMENTATION
- Packet processing order: https://my.f5.com/manage/s/article/K8082
- Connection table: https://my.f5.com/manage/s/article/K13637
- Packet filters: https://my.f5.com/manage/s/article/K2250
EXAM QUESTION PATTERNS
- "What is the order?" → Existing connections → Packet filter → VS → SNAT → NAT → Self IP → Drop
- "Packet filter enabled after FTP session established. Does it block the session?" → No (existing connections take priority)
- "Unmatched traffic to VIP. What happens?" → Silently dropped (no RST)

## Slide 58
58 © 2026 F5
Virtual server matching order
When multiple virtual servers could match, the most specific wins
1
Host + port
10.1.10.100:80
Most specific: exact IP + exact port. This is a standard VS like www_vs.
2
Host + wildcard port
10.1.10.100:*
Exact IP but any port. This is wildcard_vs from the lab.
3
Network + port
10.1.10.0/24:80
Subnet match + exact port. Matches any IP in the subnet on that port.
4
Network + wildcard port
10.1.10.0/24:*
Subnet match + any port. Broadest network-specific match.
5
Wildcard + port
0.0.0.0/0:80
Any IP + exact port. Catches all port 80 traffic not matched above.
6
Wildcard + wildcard
0.0.0.0/0:*
Least specific: any IP, any port. Catches everything not matched above.
Source address tiebreaker: If two VS have the same destination specificity, the one with a more specific Source address wins. Example: VS-A allows 10.1.10.0/24, VS-B allows 0.0.0.0/0. A client from 10.1.10.199 matches VS-A because /24 is more specific than /0. This is tested in Lab Activity 3.
Notes: WHAT THIS SLIDE TEACHES
This slide covers F5CTSLTM2.07: "Identify the matching order of multiple virtual servers." The exam presents scenarios with multiple VS configured on the same VIP and asks which one handles a specific request. Understanding the specificity hierarchy is critical.
FULL TECHNICAL EXPLANATION
VS MATCHING SPECIFICITY:
The BIG-IP evaluates virtual servers from most specific to least specific. When a packet arrives, it checks destination address specificity first, then port specificity.
The hierarchy (from most to least specific):
1. Host address (exact IP) + specific port → e.g., 10.1.10.100:80
2. Host address + wildcard port → e.g., 10.1.10.100:*
3. Network address + specific port → e.g., 10.1.10.0/24:80
4. Network address + wildcard port → e.g., 10.1.10.0/24:*
5. Wildcard address + specific port → e.g., 0.0.0.0/0:80
6. Wildcard address + wildcard port → e.g., 0.0.0.0/0:*
THE LAB SCENARIO:
Students have these VS configured on 10.1.10.100:
- www_vs: 10.1.10.100:80 (host + port)
- ftp_vs: 10.1.10.100:21 (host + port)
- wildcard_vs: 10.1.10.100:* (host + wildcard port)
Traffic to:
- http://10.1.10.100 (port 80) → www_vs wins (most specific: host + port 80)
- ftp 10.1.10.100 (port 21) → ftp_vs wins (most specific: host + port 21)
- http://10.1.10.100:8080 → wildcard_vs wins (host + wildcard port, since no VS has port 8080)
SOURCE ADDRESS AS TIEBREAKER:
When two VS have the same destination specificity (same IP:port or same wildcard pattern), the BIG-IP uses the Source Address field to break the tie:
- A VS with Source 10.1.10.0/24 is more specific than Source 0.0.0.0/0
- A client from 10.1.10.199 matches the /24 source first
- A client from 10.2.20.50 doesn't match /24 → falls through to /0
Lab Activity 3 tests this: students modify wildcard_vs Source to 10.1.10.0/24, then browse from 10.1.10.199 → wildcard_vs matches (same dest specificity as www_vs for non-80 ports, but /24 source is more specific than www_vs's default /0).
COMMON STUDENT MISTAKES
- Assuming wildcard VS always handles traffic — it only handles traffic that no more specific VS matches
- Not understanding that source address breaks ties — when two VS have the same dest, source specificity wins
- Thinking port-specific beats host-specific — the hierarchy is destination address first, then port
PIVOT QUESTION
"You have www_vs (10.1.10.100:80) and wildcard_vs (10.1.10.100:*). A client browses to https://10.1.10.100 (port 443). Which VS processes the request?"
ANSWER: wildcard_vs. There is no VS matching 10.1.10.100:443 specifically. The wildcard_vs (10.1.10.100:*) matches because the host address is exact and the wildcard port includes 443. If there were also a secure_vs on 10.1.10.100:443, it would win over wildcard_vs because host+port is more specific than host+wildcard.
F5 DOCUMENTATION
- VS matching order: https://my.f5.com/manage/s/article/K14800
- VS types and precedence: https://my.f5.com/manage/s/article/K55185917
EXAM QUESTION PATTERNS
- "VS-A is 10.1.10.100:80, VS-B is 10.1.10.100:*. Client requests port 8080. Which VS?" → VS-B
- "VS-A has source 10.1.10.0/24, VS-B has source 0.0.0.0/0, same dest. Client from 10.1.10.50?" → VS-A
- "Why doesn't my VS receive traffic?" → A more specific VS is matching first

## Slide 59
59 © 2026 F5
Packet-based vs connection-based
Two fundamentally different approaches to processing traffic through the BIG-IP
Packet-based (Performance L4)
How it works
Each packet is processed independently. LB decision made on FIRST packet (SYN). Subsequent packets forwarded with address translation. No TCP reassembly, no L7 inspection.
Advantages
• Highest throughput, lowest latency
• PVA hardware acceleration (applicable platforms)
• Minimal CPU per connection
• Supports loose initiation (mid-flow pickup)
Limitations
• No HTTP inspection or modification
• No SSL termination
• No cookie persistence
• No iRules with HTTP:: commands
• No compression or caching
Connection-based (Standard)
How it works
Full proxy: BIG-IP terminates client TCP, opens new server TCP. Reassembles byte stream for L7 inspection. LB decision can be deferred until HTTP data arrives.
Advantages
• Full L7 intelligence (HTTP, SSL, iRules)
• Content switching, compression, caching
• TCP optimization (wan/lan split)
• Cookie persistence, OneConnect
• Protocol enforcement and security
Limitations
• Higher CPU per connection
• Higher latency (full proxy overhead)
• Cannot do mid-flow pickup
• More memory per connection
Decision rule: If you need ANY L7 feature (HTTP, SSL, compression, cookie persistence, iRules with HTTP:: commands) → connection-based (Standard). If you only need L4 load balancing with maximum throughput → packet-based (Performance L4).
Notes: WHAT THIS SLIDE TEACHES
This slide covers F5CTSLTM2.05: "Distinguish between packet-based versus connection-based load balancing." Students must understand when to use each approach and the trade-offs involved.
FULL TECHNICAL EXPLANATION
PACKET-BASED (Performance L4 / FastL4):
The BIG-IP processes each packet individually without reassembling the TCP byte stream:
1. First packet (SYN) arrives → BIG-IP makes LB decision based on L3/L4 info only (source/dest IP and port)
2. BIG-IP translates addresses and forwards the SYN to the selected pool member
3. All subsequent packets in the flow are forwarded with the same translation — no inspection
4. The BIG-IP maintains minimal connection state (just the address translation mapping)
Loose initiation: Performance L4 can pick up mid-flow connections (connections that started before the BIG-IP was inserted into the path). Standard VS cannot do this because it needs to see the SYN to establish full proxy state.
PVA acceleration: On hardware BIG-IP platforms with PVA ASIC, Performance L4 flows can be offloaded to dedicated hardware. This removes TMM CPU from the processing path entirely, achieving line-rate throughput.
CONNECTION-BASED (Standard / Full Proxy):
The BIG-IP terminates the client's TCP connection and establishes a new, independent connection to the server:
1. Client SYN → BIG-IP completes three-way handshake (client-side connection)
2. Client sends data → BIG-IP buffers and reassembles the byte stream
3. If HTTP profile: BIG-IP parses HTTP request, can inspect headers, URI, cookies
4. BIG-IP makes LB decision (can be based on L7 data like URI, Host header, cookie)
5. BIG-IP opens new TCP connection to pool member (server-side connection)
6. BIG-IP can modify data between the two connections
The two connections are fully independent — different sequence numbers, different window sizes, potentially different TCP options (wan-optimized on client side, lan-optimized on server side).
KEY EXAM DISTINCTION:
The exam may present a scenario and ask whether packet-based or connection-based is appropriate:
- "Load balance MySQL connections" → Packet-based (no L7 needed, FastL4 profile)
- "Load balance web application with cookie persistence" → Connection-based (need HTTP for cookies)
- "Forward traffic to a backend network" → Packet-based (Forwarding IP VS with FastL4)
- "Load balance HTTP with content switching" → Connection-based (need to read HTTP URI)
COMMON STUDENT MISTAKES
- Thinking connection-based is always better. For non-HTTP traffic that doesn't need L7 inspection, packet-based is more efficient.
- Not understanding that packet-based VS cannot do cookie persistence. Cookies are L7 (HTTP) objects — you need to parse the byte stream to read them.
- Confusing "packet-based" with "stateless." Packet-based still tracks connections (for NAT translation) — it just doesn't reassemble the byte stream.
PIVOT QUESTION
"An application requires HTTP header insertion (X-Forwarded-For) and cookie persistence. The network team wants maximum throughput and suggests Performance L4. Can this work?"
ANSWER: No. HTTP header insertion and cookie persistence both require the BIG-IP to parse HTTP — which requires a TCP + HTTP profile on a Standard VS (connection-based). Performance L4 doesn't reassemble the byte stream and cannot inspect or modify HTTP headers. The network team must accept the overhead of connection-based processing for these L7 features.
F5 DOCUMENTATION
- Packet vs connection processing: https://my.f5.com/manage/s/article/K55185917
- FastL4 profile: https://my.f5.com/manage/s/article/K55185917
- Standard VS: https://my.f5.com/manage/s/article/K8082
EXAM QUESTION PATTERNS
- "Which processing mode supports cookie persistence?" → Connection-based (Standard)
- "Which processing mode provides maximum throughput?" → Packet-based (Performance L4)
- "Application needs HTTP inspection. Can you use FastL4?" → No (need Standard with TCP + HTTP)

## Slide 60
60 © 2026 F5
Lab 6 — Hands-on exercises
45 minutes | Lab guide: Module 6
# | Activity | Key tasks | Time
1 | Packet Processing | tcpdump + connection table (show sys conn). Observe client-side/server-side flows, SNAT automap in action. | 10m
2 | Packet Filters | Create block_ftp filter. Test: existing FTP survives, new FTP blocked. Learn packet processing order. Check logs. | 10m
3 | VS Matching Order | Create wildcard_vs (10.1.10.100:*). Test which VS handles port 80, 21, 8080. Modify source address and retest. | 15m
4 | Forwarding VS | Create Forwarding IP VS (10.1.10.0/24 → 10.1.20.0/24). Create transparent VS (Performance L4, wildcard port). Test multi-protocol. | 10m
Activity 2 key question: Prioritize the packet processing order: Existing Connections(1) → AFM/Pkt Filter(2) → Virtual Server(3) → SNAT(4) → NAT(5) → Self IP(6) → Drop(7)
Activity 4 gotcha: Forwarding IP VS defaults to Protocol: TCP. Change to 'All Protocols' for general forwarding. Also need a route on the jumpbox: route add 10.1.20.0 mask 255.255.255.0 10.1.10.245
Notes: WHAT THIS SLIDE TEACHES
Lab launch for the VS and packet processing exercises. See the full activity walkthroughs in the speaker notes of the corresponding v1 deck.
KEY TEACHING MOMENTS:
- Activity 1: Management SSH not in connection table (host OS, not TMM)
- Activity 2: Packet filter doesn't affect existing connections (Step 1 > Step 2)
- Activity 3: Most specific VS wins (host+port > host+wildcard)
- Activity 4: Forwarding IP VS has no pool; uses routing table. Protocol must be "All Protocols."
F5 DOCUMENTATION: K8082, K14800, K55185917, K7595

## Slide 61
61 © 2026 F5
Exam checkpoints
Q1
U/A
You have www_vs (10.1.10.100:80), ftp_vs (10.1.10.100:21), and wildcard_vs (10.1.10.100:*). A client browses to http://10.1.10.100:8080. Which VS handles it?
Q2
U/A
An application needs cookie persistence and HTTP compression. Can you use a Performance (Layer 4) VS? Why or why not?
Q3
U/A
You need to allow web administrators from 10.1.10.0/24 to SSH, HTTP, and ping servers on 10.1.20.0/24 without creating separate VS per service. What VS type and configuration do you use?
Q4
U/A
You enable a packet filter blocking port 21. An active FTP session continues to work. A new FTP connection fails. Why does the existing session survive?
Most specific VS wins: host+port > host+wildcard > network+port > network+wildcard > 0.0.0.0:port > 0.0.0.0:*
Notes: WHAT THIS SLIDE TEACHES
Four checkpoint questions testing VS matching, packet vs connection-based, VS type selection, and packet processing order.
Q1 ANSWER: wildcard_vs (10.1.10.100:*). No VS matches 10.1.10.100:8080 specifically. www_vs matches port 80, ftp_vs matches port 21. wildcard_vs matches any port on that IP, including 8080.
Q2 ANSWER: No. Cookie persistence requires HTTP (cookies are HTTP headers). HTTP compression requires HTTP. Both need the BIG-IP to parse the HTTP byte stream, which requires a Standard VS with TCP + HTTP profiles (connection-based). Performance L4 doesn't reassemble the byte stream.
Q3 ANSWER: Forwarding (IP) virtual server with Source: 10.1.10.0/24, Destination: 10.1.20.0/24, Port: *, Protocol: All Protocols. This allows all traffic types (SSH, HTTP, ICMP) from the admin subnet to the server subnet without separate VS per service. A route to 10.1.20.0/24 via the BIG-IP must exist on the admin workstations.
Q4 ANSWER: Existing connections (Step 1 in packet processing order) are checked before packet filters (Step 2). The FTP session is already in the connection table, so its packets bypass the packet filter. Only new connections are evaluated against the filter. To clear existing connections: delete sys connection cs-client-addr [ip]
F5 DOCUMENTATION: K14800 (VS matching), K55185917 (VS types), K8082 (packet processing), K2250 (packet filters)

## Slide 62
62 © 2026 F5
Exam checkpoints (continued)
Q5
U/A
What is the key difference between a Standard VS and a Performance (Layer 4) VS in terms of how TCP connections are handled?
Q6
U/A
Two virtual servers match the same destination IP:port. VS-A has Source 10.1.10.0/24, VS-B has Source 0.0.0.0/0. A client from 10.1.10.50 connects. Which VS processes the traffic?
Packet processing order (memorize this)
1. Existing connections (already in connection table → follow existing flow)
2. Packet filters / AFM (evaluated before VS — can block traffic from reaching VS)
3. Virtual server (matched by specificity: host+port > host+wildcard > network > wildcard)
4. SNAT (source address translation for outbound traffic)
5. NAT (1:1 address translation)
6. Self IP (traffic destined to BIG-IP's own addresses)
7. Drop (no match anywhere → silently dropped, no RST sent)
Notes: WHAT THIS SLIDE TEACHES
Final checkpoints plus the packet processing order study reference that students should memorize.
Q5 ANSWER: Standard VS operates as a FULL PROXY — it terminates the client's TCP connection (completes the three-way handshake) and opens a NEW, INDEPENDENT TCP connection to the server. These are two separate connections with different sequence numbers. This enables all L7 features.
Performance (Layer 4) VS processes traffic PACKET-BY-PACKET — it forwards the client's SYN directly to the server (with address translation) without terminating the connection. There's ONE flow through the BIG-IP with minimal state tracking. This provides maximum throughput but no L7 capability.
The key visual: Standard = two TCP handshakes (client↔BIG-IP and BIG-IP↔server). Performance L4 = one TCP handshake (client↔server, with BIG-IP translating addresses in the middle).
Q6 ANSWER: VS-A. When two VS have the same destination specificity (same IP:port), the BIG-IP uses Source address as a tiebreaker. VS-A's source (10.1.10.0/24) is more specific than VS-B's source (0.0.0.0/0) for a client from 10.1.10.50. The /24 mask matches the client, so VS-A wins.
If the client were from 10.2.20.100 (outside the /24), VS-A would NOT match and VS-B (0.0.0.0/0) would handle the traffic.
F5 DOCUMENTATION: K8082 (packet processing), K14800 (VS matching), K55185917 (VS types)

## Slide 63
F5CTSLTM2.03 | U/A | Choose VS type and load balancing type for requirements
F5CTSLTM2.09 | U/A | Determine how config changes affect existing and new connections
LAB 7
Load Balancing and Pools
Compare load balancing methods (Round Robin, Ratio, Least Connections),
configure priority groups for DR failover, understand member vs node scope,
and test persistence interaction with disabled and force-offline members.
45 min | 15 min slides + 30 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 7. This lab explores how load balancing methods, priority groups, and persistence profiles interact to determine where traffic goes. It directly addresses the 301a objective 1.16: "Explain the effect of LTM device configuration parameters on load balancing decisions."
FULL TECHNICAL EXPLANATION
Three lab activities:
1. Ratio Load Balancing: Change www_pool from Round Robin to Ratio (Member), set one member's ratio to 3, observe weighted distribution. Then revert to Round Robin and see that ratio settings are ignored.
2. Priority Groups: Configure priority group activation (<2 members), assign priorities, disable members to trigger DR failover to low-priority group.
3. Source Address Persistence: Create persistence profile, observe records, test Disable (persistence honored) vs Force Offline (persistence broken).
BETA BLUEPRINT COVERAGE
- F5CTSLTM2.03 (U/A): "Compare and contrast different load balancing methods" and "Identify different load balancing method use cases."
- F5CTSLTM2.09 (U/A): "Determine how configuration changes affect existing and new connections." Sub-bullets: predict persistence for existing connections, calculate when changes affect connections, predict LB and persistence for new connections.
F5 DOCUMENTATION: K16649 (LB methods), K14358 (priority groups), K5779 (persistence)

## Slide 64
64 © 2026 F5
Load balancing methods
The algorithm that determines which pool member receives the next connection
Method | How it works | Best for | Limitation
Round Robin | Rotates through members sequentially. Default method. | Equal-capacity servers. Simplest config. | Ignores server load — overloaded server still gets connections.
Ratio | Static weights. Member with ratio 3 gets 3x connections vs ratio 1. | Servers with known different capacities. | Static — doesn't adapt to real-time load.
Least Connections | Sends to member with fewest active connections. | Varying request duration. Most common dynamic method. | New member gets ALL traffic until balanced (use Slow Ramp).
Fastest | Sends to member with fewest L7 requests (not TCP conns). | Servers across different network segments. | Requires L7 profile (TCP + HTTP). More overhead.
Observed | Ranks members by connection count over time, creates dynamic ratio. | Rare — use Least Connections instead. | Not recommended for large pools.
Predictive | Like Observed, but factors in performance trend (improving/declining). | Rare — use Least Connections instead. | Complex, not recommended for most deployments.
Member vs Node scope
Ratio (Member)
LB decision per pool member (IP:port). Same server on port 80 and 443 can have different ratios in different pools.
Ratio (Node)
LB decision per node (IP only). Weight applies across ALL pools. If node has ratio 3, it gets 3x in every pool it belongs to.
Notes: WHAT THIS SLIDE TEACHES
This slide covers the load balancing methods available on the BIG-IP, supporting F5CTSLTM2.03: "Compare and contrast different load balancing methods" and "Identify different load balancing method use cases."
FULL TECHNICAL EXPLANATION
ROUND ROBIN (default):
The simplest method. The BIG-IP cycles through pool members in order: A → B → C → A → B → C.
- No awareness of server load, response time, or capacity
- Works well when all servers are identical in capacity and request processing time
- The "baseline" method — use this unless you have a reason to choose something else
RATIO (Member) and RATIO (Node):
Static weight-based distribution. If member A has ratio 3 and members B and C have ratio 1, the distribution is: A, A, A, B, C, A, A, A, B, C...
- The ratio is set PER MEMBER (in the pool member properties) or PER NODE (in the node properties)
- Ratio is STATIC — it doesn't change based on server load
- Useful when you know servers have different capacities (e.g., a 16-core server should get 4x the traffic of a 4-core server)
LAB EXERCISE: Set member 10.1.20.11 ratio to 3, others default to 1. With Ratio (Member) method, 10.1.20.11 should get approximately 3/5 (60%) of connections.
IMPORTANT: Ratio settings are ONLY used when the LB method is Ratio. If you switch back to Round Robin, the ratio values still exist on the members but are IGNORED.
LEAST CONNECTIONS (Member) and LEAST CONNECTIONS (Node):
Dynamic method. The BIG-IP sends each new connection to the member with the fewest active connections.
- Adapts to real-time load — slow members accumulate connections, fast members clear them quickly
- Most commonly used dynamic method in production
- OneConnect interaction: If OneConnect is enabled, Least Connections counts only ACTIVE connections (not idle pooled connections)
SLOW RAMP TIME (critical interaction):
When a new member comes online (or recovers from a health check failure), it has ZERO active connections. Least Connections will send ALL new traffic to it until it reaches the same connection count as other members. This can overwhelm the new member.
Slow Ramp Time: Gradually increases the rate of new connections to a newly available member.
- Default: 10 seconds
- During the ramp period, the BIG-IP sends connections to the new member at a reduced rate
- After the ramp period, the member participates fully in Least Connections
TMSH: modify ltm pool [pool] slow-ramp-time 30
FASTEST:
Similar to Least Connections but counts Layer 7 requests instead of TCP connections. A member processing many long-running HTTP requests might have few TCP connections but high L7 load.
- Requires TCP + HTTP profiles (L7 profile needed to track request count)
- Less commonly used than Least Connections
MEMBER vs NODE SCOPE:
Every LB method has two variants: (Member) and (Node).
- Member: Decision per pool member (IP:port combination). The same physical server can have different weights in different pools.
- Node: Decision per node (IP address only). The weight applies across ALL pools that include that node.
Example: Server 10.1.20.11 is in www_pool (port 80) and api_pool (port 8080).
- Ratio (Member): You can set ratio 3 for 10.1.20.11:80 in www_pool and ratio 1 for 10.1.20.11:8080 in api_pool.
- Ratio (Node): You set ratio 3 on the NODE 10.1.20.11, and it gets 3x traffic in BOTH pools.
COMMON STUDENT MISTAKES
- Changing to Ratio but forgetting to set member ratios (default ratio is 1 — all members equal)
- Switching back to Round Robin and expecting ratio weights to still matter (they don't)
- Using Least Connections without Slow Ramp — new members get hammered
- Confusing Member vs Node scope — Node affects ALL pools using that server
PIVOT QUESTION
"You change the pool LB method from Round Robin to Ratio (Member) but don't set any ratio values. What happens?"
ANSWER: All members have the default ratio of 1. Ratio with equal weights behaves identically to Round Robin — connections are distributed evenly. You must explicitly set different ratio values on individual members for Ratio to have any effect.
F5 DOCUMENTATION
- LB methods: https://my.f5.com/manage/s/article/K16649
- Slow ramp time: https://my.f5.com/manage/s/article/K13637
- Member vs Node: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-local-traffic-manager-basics/ltm-pools.html
EXAM QUESTION PATTERNS
- "Default LB method?" → Round Robin
- "Server load varies. Which dynamic method?" → Least Connections
- "Servers have different capacities (known)?" → Ratio
- "New member gets overwhelmed with Least Connections. What setting?" → Slow Ramp Time

## Slide 65
65 © 2026 F5
Priority groups and slow ramp
Control failover between primary and DR members, and protect recovering members from traffic spikes
Priority group activation
How it works:
Assign each pool member a priority group number (higher = preferred). Set a minimum member threshold. Traffic goes only to the highest priority group unless available members fall below the minimum.
Lab scenario:
Primary DC: 10.1.20.11, 10.1.20.12 → Priority Group 10
DR site: 10.1.20.13 → Priority Group 0 (default)
Activation: Less than 2 available members
Behavior:
Normal: traffic goes to .11 and .12 only (.13 idle)
One primary fails: still 1 primary left — but below threshold of 2 → .13 activated
Both primaries recover: .13 returns to standby
Slow ramp time
The problem:
With Least Connections, a newly available member has 0 connections → gets ALL new traffic → overwhelmed before it warms up.
The solution:
Slow Ramp Time gradually increases the connection rate to new members.
Default: 10 seconds
Set per pool:
modify ltm pool [name]
slow-ramp-time 30
Applies to: Least Connections, Weighted LC, Observed, Predictive. Does NOT apply to Round Robin or Ratio (static methods).
Priority groups + Slow Ramp interaction
When a primary member recovers and the DR member is deactivated, the recovering member has 0 connections. If using Least Connections, it gets ALL traffic immediately. Set Slow Ramp Time on the pool to prevent this. Also consider using Time Until Up on the health monitor to delay the member's promotion until it has warmed up.
Notes: WHAT THIS SLIDE TEACHES
This slide covers priority-based member activation and slow ramp time — two features that control how traffic distribution changes during failure and recovery scenarios. This directly supports F5CTSLTM2.09: "Predict load balancing and persistence for new connections" and "Calculate when changes will affect the connections."
FULL TECHNICAL EXPLANATION
PRIORITY GROUP ACTIVATION:
Each pool member can be assigned a priority group number (0-65535). Higher numbers have higher priority.
- Priority Group Activation: Set on the pool (not the member). Specifies the minimum number of available members required in the highest priority group before lower priority groups are activated.
- When available members in the highest group fall BELOW the threshold, the next lower group is activated.
- When enough members recover to meet the threshold, lower priority groups are deactivated.
Configuration:
GUI: Pool > Members > Load Balancing section > Priority Group Activation > Less Than [N] Available Members
Then edit each member to set its Priority Group number.
TMSH:
modify ltm pool www_pool min-active-members 2
modify ltm pool www_pool members modify { 10.1.20.11:80 { priority-group 10 } 10.1.20.12:80 { priority-group 10 } 10.1.20.13:80 { priority-group 0 } }
Lab scenario walkthrough:
1. All three members UP: .11 (PG10), .12 (PG10), .13 (PG0). Threshold = 2.
- Highest group (PG10) has 2 members ≥ threshold → only PG10 receives traffic
- .13 is idle (PG0 not activated)
2. Disable .11: PG10 now has 1 member < threshold of 2
- PG0 activated → .12 (PG10) + .13 (PG0) both receive traffic
3. Re-enable .11: PG10 now has 2 members ≥ threshold
- PG0 deactivated → .13 returns to standby
SLOW RAMP TIME:
When using dynamic LB methods (Least Connections, Weighted LC), a newly available member has 0 active connections. The LB algorithm immediately selects it for ALL new connections until its count catches up with other members. This can overwhelm the member, especially if it needs warm-up time.
Slow Ramp Time introduces a grace period:
- During the ramp period, the BIG-IP gradually increases the rate of new connections to the member
- The ramp is linear: at time 0, the member gets minimal connections. At the end of the ramp period, it participates fully.
- Default: 10 seconds (usually sufficient for most applications)
- For applications with long warm-up (JVM, cache loading): set to 30-60 seconds
Important: Slow Ramp only applies to DYNAMIC methods. Round Robin and Ratio distribute connections based on static rules — they don't consider connection count, so there's no "thundering herd" problem.
COMMON STUDENT MISTAKES
- Setting priority group numbers but forgetting to set the activation threshold (min-active-members). Without it, priority groups have no effect — all members receive traffic regardless of priority.
- Not understanding that priority groups work with ANY LB method — Round Robin, Ratio, Least Connections all respect priority groups.
- Forgetting slow ramp when using Least Connections with priority groups — the recovery scenario is exactly when slow ramp matters most.
PIVOT QUESTION
"Pool has 4 members: A (PG10), B (PG10), C (PG5), D (PG5). Min-active-members is 2. A and B are UP. You disable A. What happens?"
ANSWER: PG10 now has 1 member (B) — below the threshold of 2. The next lower group (PG5) is activated. Traffic goes to B (PG10), C (PG5), and D (PG5). When A recovers, PG10 has 2 members again and PG5 is deactivated.
F5 DOCUMENTATION
- Priority groups: https://my.f5.com/manage/s/article/K14358
- Slow ramp time: https://my.f5.com/manage/s/article/K13637
- LB methods: https://my.f5.com/manage/s/article/K16649
EXAM QUESTION PATTERNS
- "Priority Group Activation set to <2. Highest group has 3 members. One fails. Is the lower group activated?" → No (2 remaining ≥ threshold of 2)
- "New member comes online with Least Connections. Gets overwhelmed. What setting?" → Slow Ramp Time
- "Priority groups configured but all members get traffic. What's missing?" → min-active-members not set

## Slide 66
66 © 2026 F5
Persistence and load balancing interaction
Persistence overrides the LB method for existing sessions — but what happens when the member is taken offline?
Decision flow for each new connection
1. Check persistence record for this client → Record found? Send to persisted member (skip LB) → No record? Use LB method to select member → Create persistence record
What happens to persistence when a member is taken offline?
Action | Existing connections | Persisted new connections | Non-persisted new connections
Disable | Continue ✔ | Honored — sent to disabled member ✔ | Refused — LB selects other member
Force Offline | Terminated ✘ | Broken — LB selects new member ✘ | Refused — LB selects other member
Monitor failure | Continue (until timeout) ✔ | Honored (member still in table) ✔ | Refused — LB selects other member
Disable = graceful. Existing connections and persistence sessions continue. Use for planned maintenance. Force Offline = immediate. Everything stops. Use only for emergencies.
Viewing persistence records
GUI: Statistics > Module Statistics > Local Traffic > Persistence Records
TMSH: show ltm persistence persist-records
Notes: WHAT THIS SLIDE TEACHES
This slide covers the critical interaction between persistence and load balancing, directly supporting F5CTSLTM2.09: "Predict persistence for existing connections" and "Predict load balancing and persistence for new connections." The exam frequently presents scenarios where a member is disabled or goes offline and asks what happens to persisted clients.
FULL TECHNICAL EXPLANATION
PERSISTENCE vs LOAD BALANCING — DECISION FLOW:
When a new connection arrives at a virtual server with persistence enabled:
1. BIG-IP checks for an existing persistence record matching this client
2. If a record exists → traffic goes to the persisted member (LB method is BYPASSED)
3. If no record exists → LB method selects a member → BIG-IP creates a new persistence record
This means persistence OVERRIDES load balancing for returning clients. A member could have 10x the connections of others if persistence keeps sending the same clients back.
THE THREE OFFLINE SCENARIOS:
1. DISABLE (admin action):
- Existing connections: Continue normally (already in connection table)
- Persistence records: HONORED. If a client has an active persistence record to the disabled member, new connections from that client still go to the disabled member. The BIG-IP respects the persistence record.
- Non-persisted new connections: Refused. The LB method skips the disabled member and selects another.
- Use case: Planned maintenance. Disable the member, wait for persistence records to expire (check timeout), then perform maintenance.
2. FORCE OFFLINE:
- Existing connections: Immediately terminated (RST sent)
- Persistence records: BROKEN. All persistence records pointing to this member are invalidated. Clients are re-load-balanced to a different member on their next connection.
- Non-persisted new connections: Refused.
- Use case: Emergency removal. Security incident, data corruption, unresponsive server.
3. MONITOR FAILURE (member goes offline):
- Existing connections: Continue (the server may still be partially responding)
- Persistence records: Honored in most configurations. The persistence record still exists in the table — the BIG-IP will attempt to send traffic to the offline member, which may result in failures for the client. This depends on the "Action On Service Down" setting.
- Action On Service Down options: None (default — connections remain), Reset (send RST), Drop (silently drop), Reselect (pick another member).
ACTION ON SERVICE DOWN:
This pool-level setting determines what happens to connections when a pool member's monitor fails:
- None: Default. Existing connections remain. New connections go elsewhere.
- Reset: Send TCP RST to all connections to the failed member.
- Drop: Silently drop connections to the failed member.
- Reselect: Rebalance active connections to other members. Best for stateless applications.
PERSISTENCE RECORD TIMEOUT:
Source address persistence records have a configurable timeout (default 180 seconds). After the timeout, the record expires and the client gets a fresh LB decision on the next connection. During planned maintenance:
1. Disable the member (persistence is still honored)
2. Wait for persistence records to expire (check Statistics > Persistence Records)
3. When no records remain → all clients have been naturally moved to other members
4. Perform maintenance safely
COMMON STUDENT MISTAKES
- Thinking Disable breaks persistence immediately. It doesn't — persisted clients continue to be sent to the disabled member.
- Not understanding Action On Service Down. Default "None" means monitor failure doesn't reset connections.
- Forgetting to check persistence records before maintenance — disabling a member doesn't mean clients have moved.
PIVOT QUESTION
"You disable member 10.1.20.11 for maintenance. Source address persistence is configured with a 180-second timeout. A client who was persisted to .11 refreshes the page 30 seconds later. What happens?"
ANSWER: The client's request is sent to the disabled member 10.1.20.11. Disable honors persistence records. The client continues to use .11 until either: (a) the persistence record expires (180 seconds of idle), or (b) the admin uses Force Offline instead of Disable. To ensure the client moves to another member, either wait for the persistence timeout or use Force Offline.
F5 DOCUMENTATION
- Persistence and member state: https://my.f5.com/manage/s/article/K13132
- Action On Service Down: https://my.f5.com/manage/s/article/K10530
- Persistence records: https://my.f5.com/manage/s/article/K5779
EXAM QUESTION PATTERNS
- "Member disabled, client has persistence record. Where does traffic go?" → Still to the disabled member
- "Member force-offlined, client has persistence record. Where?" → LB selects a new member
- "What setting controls behavior when a monitor marks a member down?" → Action On Service Down

## Slide 67
67 © 2026 F5
Lab 7 — Hands-on exercises
30 minutes | Lab guide: Module 7
# | Activity | Key tasks | Time
1 | Ratio Load Balancing | Change to Ratio (Member), set .11 ratio to 3. Observe 3:1:1 distribution. Revert to Round Robin — ratios ignored. | 10m
2 | Priority Groups | Set activation to <2. Assign .11/.12 PG10, .13 PG0. Disable .11 → .13 activates. Re-enable → .13 returns to standby. | 10m
3 | Source Persistence | Create my-src-persist (timeout 120s). Attach to www_vs. Observe persistence records. Test Disable vs Force Offline behavior. | 10m
Browser tip: Close ALL browser windows between tests. An existing connection uses the old LB settings. Open a new incognito window for each test to ensure a completely fresh connection.
Activity 3 key test: While persisted, Disable the member → you can still access the site (persistence honored). Force Offline the member → site fails then recovers on another member (persistence broken).
Notes: WHAT THIS SLIDE TEACHES
Lab launch for load balancing exercises. Three activities testing ratio distribution, priority group failover, and persistence interaction with member state changes.
KEY TEACHING MOMENTS:
- Activity 1: Ratio weights only matter when LB method is Ratio. Switching back to Round Robin ignores them.
- Activity 2: Priority groups provide active/standby member pools. Threshold controls activation.
- Activity 3: The critical Disable vs Force Offline persistence lesson — Disable honors persistence, Force Offline breaks it.
IMPORTANT: Students must close browser windows between tests. HTTP keep-alive and browser connection pooling can reuse existing connections, making it look like LB settings didn't change.
F5 DOCUMENTATION: K16649 (LB methods), K14358 (priority groups), K5779 (persistence), K13132 (member states)

## Slide 68
68 © 2026 F5
Exam checkpoints
Q1
U/A
You change the LB method to Ratio (Member) but forget to set ratio values on any member. How is traffic distributed?
Q2
U/A
A newly recovered pool member gets overwhelmed with connections when using Least Connections. What pool setting prevents this?
Q3
U/A
Source persistence is active. You Disable the member a client is persisted to. The client refreshes. Can they access the site? Why?
Q4
U/A
Same scenario, but you Force Offline the member instead. The client refreshes. What happens now?
LB method selection: Equal servers → Round Robin | Known capacities → Ratio | Varying load → Least Connections | DR failover → Priority Groups
Notes: WHAT THIS SLIDE TEACHES
Four checkpoint questions testing LB method behavior, slow ramp, and the critical Disable vs Force Offline persistence interaction.
Q1 ANSWER: Traffic is distributed evenly — identical to Round Robin. All members have the default ratio of 1. Ratio with equal weights produces the same result as Round Robin. You must explicitly change ratio values on individual members for Ratio to differ from Round Robin.
Q2 ANSWER: Slow Ramp Time. Set on the pool (modify ltm pool [name] slow-ramp-time 30). Gradually increases the connection rate to newly available members during the ramp period. Default is 10 seconds. For applications with long warm-up (JVM, cache), set to 30-60 seconds.
Q3 ANSWER: YES, the client can still access the site. Disable honors persistence records. The BIG-IP sees the client's persistence record pointing to the disabled member and sends the traffic there anyway. The disabled member continues to serve existing connections and persisted clients. Only NON-persisted new connections are redirected to other members.
Q4 ANSWER: The first request FAILS (the member is immediately taken offline and the persistence record is invalidated). The client's browser retries or refreshes → the BIG-IP makes a new LB decision → traffic goes to a different member → the client can access the site again. Force Offline breaks persistence immediately, unlike Disable which honors it.
F5 DOCUMENTATION: K16649, K13637 (slow ramp), K13132 (member states), K5779 (persistence)

## Slide 69
69 © 2026 F5
Exam checkpoints (continued)
Q5
U/A
Pool has 4 members: A (PG10), B (PG10), C (PG5), D (PG5). Min-active-members is 2. Member A fails. Is PG5 activated?
Q6
U/A
What is the difference between Least Connections (Member) and Least Connections (Node)? When does the distinction matter?
Load balancing decision tree
All servers equal capacity → Round Robin (default, simplest)
Servers with known different capacities → Ratio (Member)
Varying request duration / server load → Least Connections (most common dynamic)
DR / backup site failover → Priority Groups + any LB method
Newly recovered members overwhelmed → Slow Ramp Time on pool
Persistence required → LB method for first connection, persistence overrides for returning clients
Notes: WHAT THIS SLIDE TEACHES
Final checkpoints plus the LB decision tree reference.
Q5 ANSWER: YES, PG5 is activated. With A failed, PG10 has only 1 available member (B). The min-active-members threshold is 2. Since 1 < 2, the BIG-IP activates the next lower priority group (PG5). Traffic now goes to B (PG10), C (PG5), and D (PG5). When A recovers, PG10 has 2 members again ≥ threshold, and PG5 is deactivated.
Q6 ANSWER:
- Least Connections (Member): Counts active connections per pool member (IP:port). Server 10.1.20.11 running on port 80 and port 443 has separate connection counts.
- Least Connections (Node): Counts active connections per node (IP address), aggregating across ALL pools and ports. Server 10.1.20.11 with connections on port 80 AND port 443 has one combined count.
The distinction matters when: a server is a member of multiple pools or serves multiple ports. With (Node), the BIG-IP considers the server's total load across all services. With (Member), it only considers the load for that specific pool member.
Example: Server A has 50 connections on port 80 and 200 connections on port 443.
- LC (Member) for the port-80 pool: only sees 50 connections → might send more traffic
- LC (Node): sees 250 total connections → sends less traffic to balance overall server load
F5 DOCUMENTATION: K14358 (priority groups), K16649 (LB methods)

## Slide 70
F5CTSLTM1.03 | U/A | Determine how to secure self IPs (port lockdown)
F5CTSLTM1.04 | U/A | Determine how to perform basic device configuration
F5CTSLTM1.05 | U/A | Understand route domains
LAB 8
Networking
Self IP port lockdown configuration, VLANs (tagged/untagged), trunks,
route domains for multi-tenancy, management vs TMM interfaces,
DNS/NTP, and HA network preparation.
50 min | 20 min slides + 30 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 8: Networking. Maps to F5CTSLTM1-B exam. 301a OBJECTIVES: 2.01–2.02.
F5 DOCUMENTATION: K13250 (port lockdown), K7595 (VLANs), K13284 (self IPs), K26588 (route domains)

## Slide 71
71 © 2026 F5
Self IP port lockdown
Controls access to BIG-IP self IPs. Default is None (most secure).
None (default)
Most secure
ICMP only
modify net self 10.1.10.245/24
allow-service none
Allow Defaults
Moderate
SSH, HTTPS, SNMP,
NTP, DNS, HA ports
modify net self 10.1.10.245/24
allow-service default
Allow Custom
Targeted
Only ports you specify
modify net self 10.1.10.245/24
allow-service add {
tcp:22 tcp:443 }
Allow All
Least secure
All TCP/UDP ports
modify net self 10.1.10.245/24
allow-service all
Allow Defaults opens these specific ports
Protocol | Port | Service | Why it's needed
TCP | 22 | SSH | CLI management access to BIG-IP through TMM interface
TCP | 443 | HTTPS | Configuration utility (GUI) access
TCP | 4353 | iQuery / CMI | ConfigSync, GTM communication, HA state mirroring
UDP | 1026 | Network failover | HA heartbeat between BIG-IP peers
UDP | 53 | DNS | Name resolution through TMM interfaces
UDP | 161 | SNMP | Monitoring and polling from NMS platforms
UDP | 123 | NTP | Time synchronization (critical for HA)
Notes: WHAT THIS SLIDE TEACHES
This slide covers F5CTSLTM1.03: "Determine how to secure Self IPs" with full configuration examples for each port lockdown mode. The four TMSH code blocks show the exact commands, and the Allow Defaults port table details every port with its purpose.
FULL TECHNICAL EXPLANATION
PORT LOCKDOWN CONFIGURATION:
NONE (default, most secure):
GUI: Network > Self IPs > [self IP] > Port Lockdown: None
TMSH: modify net self 10.1.10.245/24 allow-service none
Effect: Only ICMP (ping) is allowed. All TCP and UDP ports are blocked. You cannot SSH or access the GUI through this self IP. This is the DEFAULT setting for all new self IPs.
ALLOW DEFAULTS:
GUI: Network > Self IPs > [self IP] > Port Lockdown: Allow Default
TMSH: modify net self 10.1.10.245/24 allow-service default
Effect: Opens the predefined port list shown in the table. This is the minimum setting for self IPs that need admin access or HA communication.
ALLOW CUSTOM:
GUI: Network > Self IPs > [self IP] > Port Lockdown: Allow Custom > Add ports
TMSH: modify net self 10.1.10.245/24 allow-service add { tcp:22 tcp:443 }
Effect: Only the specific ports you list. Everything else remains blocked. Use this when you want fine-grained control — for example, allow SSH but not HTTPS GUI.
ALLOW ALL:
GUI: Network > Self IPs > [self IP] > Port Lockdown: Allow All
TMSH: modify net self 10.1.10.245/24 allow-service all
Effect: All TCP and UDP ports are accessible. NEVER use in production. Only for troubleshooting.
HA MINIMUM REQUIREMENTS:
For DSC to function, the HA self IP must allow at minimum:
- TCP 4353: ConfigSync (CMI)
- UDP 1026: Network failover heartbeat
Without these, config sync fails and failover doesn't work.
Recommended: Use "Allow Defaults" on the HA VLAN. It opens all necessary HA ports plus management ports. Or use "Allow Custom" with: tcp:22 tcp:443 tcp:4353 udp:1026 udp:4353
COMMON STUDENT MISTAKES
- Assuming "None" means the self IP doesn't work. It works for ICMP and for traffic passing through virtual servers — it just doesn't allow administrative access.
- Setting Allow All to "fix" a connectivity issue and forgetting to lock it back down.
- Not understanding that port lockdown ONLY affects the self IP itself — traffic to virtual servers on the same VLAN is NOT affected by port lockdown.
PIVOT QUESTION
"A self IP has Allow Custom with only TCP 22. Can you access the GUI on that self IP?"
ANSWER: No. The GUI uses HTTPS (TCP 443), which is not in the custom list. SSH (TCP 22) works, but HTTPS does not. Add TCP 443 to the custom list, or change to Allow Defaults.
F5 DOCUMENTATION
- Port lockdown: https://my.f5.com/manage/s/article/K13250
- Self IP management: https://my.f5.com/manage/s/article/K13284
- HA ports: https://my.f5.com/manage/s/article/K13946
EXAM QUESTION PATTERNS
- "Self IP responds to ping but not SSH?" → Port lockdown is None
- "What ports does Allow Defaults open?" → The table above
- "HA self IP set to None — what breaks?" → ConfigSync (4353) and failover (1026)

## Slide 72
72 © 2026 F5
Network objects overview
The building blocks of BIG-IP network configuration
Object | What it does | Key settings | Exam tip
VLAN | Layer 2 broadcast domain mapped to interfaces | Name, tag (802.1Q), interface (tagged/untagged) | Tagged = multiple VLANs per interface. Untagged = one per interface.
Self IP | BIG-IP's own IP on a VLAN | IP, mask, VLAN, port lockdown, traffic group | Floating = moves with HA failover. Non-floating = device-specific.
Trunk | Link aggregation (LACP) | Interfaces, LACP mode, distribution hash | Bandwidth aggregation + link redundancy. If one link fails, others continue.
Route | Static route for non-connected networks | Destination, gateway, VLAN | TMM routes and management routes are SEPARATE tables.
Management interface vs TMM interfaces
 | Management (MGMT port) | TMM interfaces (1.1, 1.2, etc.)
Handled by | Host OS (Linux) | TMM (Traffic Management Microkernel)
Purpose | Device administration only | Application traffic + management via self IPs
Connection table | Not visible in show sys connection | Visible in show sys connection
Port lockdown | N/A — always allows SSH + HTTPS | Controlled per self IP
Routing table | System > Platform > Routes | Network > Routes
Notes: WHAT THIS SLIDE TEACHES
Network objects overview and the critical management vs TMM distinction. See Lab 8 v1 slide 3 notes for full standalone documentation.
KEY EXAM POINTS: Tagged VLANs = 802.1Q multiple VLANs per interface. Self IPs: floating (HA) vs non-floating (device-specific). TMM and management routing tables are SEPARATE. Management SSH not in connection table (host OS, not TMM).
F5 DOCUMENTATION: K7595 (VLANs), K13284 (self IPs), K3938 (trunks)

## Slide 73
73 © 2026 F5
Route domains
Segment traffic to allow overlapping IP addresses for different tenants or applications
What route domains provide
Separate routing tables per domain
Each route domain has its own routing table, ARP cache, and forwarding database. Traffic in RD1 never crosses into RD2 unless explicitly routed.
Overlapping IP address spaces
Tenant A and Tenant B can both use 10.10.10.0/24 without conflict. The BIG-IP distinguishes them by route domain ID.
When to use route domains
✔ Multi-tenant environments
Different customers on the same BIG-IP with overlapping private IPs
✔ Mergers and acquisitions
Two companies with conflicting IP schemes consolidated on one BIG-IP
✔ Lab / dev / prod segmentation
Same IP ranges for lab and prod without cross-contamination
✘ Don't use for simple traffic separation
Use partitions or VLANs if IPs don't overlap
Configuration example
# Create route domains
create net route-domain 1 vlans add { tenant-a-vlan } strict enabled
create net route-domain 2 vlans add { tenant-b-vlan } strict enabled
# Create self IPs with %RD notation
create net self tenant-a-self address 10.10.10.245%1/24 vlan tenant-a-vlan
create net self tenant-b-self address 10.10.10.245%2/24 vlan tenant-b-vlan
# Create pools and VS with %RD notation
create ltm pool tenant-a-pool members add { 10.10.10.11%1:80 }
create ltm virtual tenant-a-vs destination 10.10.10.100%1:80 pool tenant-a-pool
Route domain 0 is the default. Objects without %RD notation belong to RD0. Strict isolation prevents cross-domain traffic unless parent RD is configured.
Notes: WHAT THIS SLIDE TEACHES
This slide covers F5CTSLTM1.05: "Understand route domains" with full configuration examples and clear use-case guidance. Route domains are a key concept for multi-tenant BIG-IP deployments.
FULL TECHNICAL EXPLANATION
ROUTE DOMAIN FUNDAMENTALS:
A route domain is a container that provides traffic isolation on the BIG-IP. Each route domain maintains its own:
- Routing table (separate from other route domains)
- ARP cache
- Connection table entries
- Forwarding database
Route domain 0 is the DEFAULT. All objects that don't specify a route domain belong to RD0. You don't need to use route domains unless you have overlapping IP addresses.
IP ADDRESS NOTATION:
Objects in non-default route domains use the %RD notation: IP_ADDRESS%ROUTE_DOMAIN_ID
- 10.10.10.100%1 = IP 10.10.10.100 in route domain 1
- 10.10.10.100%2 = IP 10.10.10.100 in route domain 2
- 10.10.10.100 (no %RD) = IP 10.10.10.100 in route domain 0 (default)
CONFIGURATION STEPS:
1. Create the route domain: create net route-domain [ID] vlans add { [vlan-list] }
2. Assign VLANs to the route domain. Each VLAN can only belong to ONE route domain.
3. Create self IPs using %RD notation: create net self [name] address [IP]%[RD]/[mask] vlan [vlan]
4. Create pools and virtual servers using %RD notation for all IP addresses
STRICT ISOLATION:
When "strict" is enabled on a route domain, traffic CANNOT cross between route domains. This is the recommended setting for multi-tenant environments.
When "strict" is disabled, traffic can be forwarded between route domains if routing permits. This is useful when you need controlled inter-domain communication (e.g., shared services).
PARENT ROUTE DOMAIN:
A route domain can have a parent. When a route in the child domain doesn't match, the BIG-IP checks the parent's routing table. This enables a hierarchy: tenant-specific routes in child RDs, shared routes (like internet gateway) in the parent RD.
WHEN TO USE ROUTE DOMAINS:
1. Multi-tenant environments: ISPs, managed service providers hosting multiple customers on one BIG-IP. Customers often use the same private IP ranges (10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16).
2. Mergers/acquisitions: Two companies with conflicting IP schemes need to be consolidated on one BIG-IP during integration.
3. Dev/Test/Prod on one BIG-IP: Same IP ranges for different environments without cross-contamination.
WHEN NOT TO USE:
- If IP addresses don't overlap, use VLANs and partitions for separation — they're simpler.
- Route domains add operational complexity. Every object must use %RD notation, and troubleshooting requires awareness of which RD you're working in.
COMMON STUDENT MISTAKES
- Forgetting %RD notation when creating objects in non-default route domains → objects end up in RD0
- Assigning a VLAN to multiple route domains → a VLAN can only belong to ONE RD
- Not understanding that RD0 is the default and doesn't need %0 notation
- Enabling strict on a parent RD that children depend on → breaks inter-domain routing
PIVOT QUESTION
"Two tenants both use 10.10.10.0/24. You create virtual servers 10.10.10.100:80 for both tenants. Without route domains, what happens?"
ANSWER: IP conflict. The BIG-IP can only have one object at 10.10.10.100:80. The second virtual server creation fails with a duplicate address error. With route domains, you create 10.10.10.100%1:80 (Tenant A) and 10.10.10.100%2:80 (Tenant B) — they coexist because they're in separate routing domains.
F5 DOCUMENTATION
- Route domains: https://my.f5.com/manage/s/article/K26588
- Route domain configuration: https://techdocs.f5.com/en-us/bigip-14-1-0/big-ip-tmos-routing-administration.html
- Strict vs non-strict: https://my.f5.com/manage/s/article/K26588
EXAM QUESTION PATTERNS
- "Two tenants use same subnet. How?" → Route domains
- "What is %2 in 10.10.10.100%2?" → Route domain 2
- "What is route domain 0?" → The default RD. Objects without %RD belong here.
- "What does strict mode do?" → Prevents traffic from crossing between route domains

## Slide 74
74 © 2026 F5
Lab 8 — Hands-on exercises
30 minutes | Lab guide: Module 8
# | Activity | Key tasks | Time
1 | Port Lockdown | Ping self IP (works). SSH (fails — None). Change to Allow Defaults (SSH + GUI work). Allow Custom TCP 22 (SSH works, GUI blocked). | 10m
2 | DNS and NTP | Configure DNS (8.8.8.8). Verify with dig. Configure NTP (pool.ntp.org). Required for HA clock sync. | 10m
3 | VLAN Tagging | Create vlan-30 (tag 30) and vlan-40 (tag 40) on interface 1.3 (Tagged). Create HA-IP 10.1.30.245/24 on vlan-30. | 10m
Activity 3 prepares for Lab 10 (HA): The HA-IP on vlan-30 is used for config sync and failover in the DSC lab. Ensure the interface is in the Tagged box, not Untagged.
NTP is critical for HA: DSC requires synchronized clocks. Clock skew > a few minutes breaks config sync and certificate validation. Always configure NTP before building device trust.
Notes: WHAT THIS SLIDE TEACHES
Lab launch for networking exercises. Three activities covering port lockdown, DNS/NTP, and tagged VLANs for HA.
Note: Route domains are not exercised in the lab (no overlapping IPs in the lab environment) but are covered conceptually on slide 4 because they're in the Beta blueprint (F5CTSLTM1.05).
F5 DOCUMENTATION: K13250, K13284

## Slide 75
75 © 2026 F5
Exam checkpoints
Q1
U/A
Self IP 10.1.10.245 responds to ping but SSH fails. What port lockdown setting is configured, and what TMSH command changes it to allow SSH?
Q2
U/A
You're building a DSC pair. The HA self IP has port lockdown None. Config sync fails. What TMSH command fixes it, and which specific ports are required?
Q3
U/A
Two tenants use 10.10.10.0/24 for their servers. How do you deploy both on one BIG-IP? What notation distinguishes the addresses?
Q4
U/A
You add a route in Network > Routes for 10.1.20.0/24. SSH to the management IP can't reach 10.1.20.0/24. Why?
Port lockdown: None (ICMP only) → Allow Defaults (SSH+GUI+HA) → Allow Custom (specific ports) → Allow All (everything, never in prod)
Notes: WHAT THIS SLIDE TEACHES
Four checkpoint questions covering port lockdown config, HA requirements, route domains, and TMM vs management routing.
Q1 ANSWER: Port lockdown is "None" (default). ICMP is allowed, TCP 22 (SSH) is blocked.
Fix: modify net self 10.1.10.245/24 allow-service default
Or for SSH only: modify net self 10.1.10.245/24 allow-service add { tcp:22 }
Q2 ANSWER: Config sync requires TCP 4353 (CMI) and network failover requires UDP 1026.
Fix: modify net self [HA-IP] allow-service default
Or minimal: modify net self [HA-IP] allow-service add { tcp:4353 udp:1026 }
Q3 ANSWER: Create two route domains. Assign each tenant's VLANs to a separate route domain.
- create net route-domain 1 vlans add { tenant-a-vlan }
- create net route-domain 2 vlans add { tenant-b-vlan }
Use %RD notation: 10.10.10.100%1 (Tenant A), 10.10.10.100%2 (Tenant B). The addresses are identical but isolated in separate routing tables.
Q4 ANSWER: TMM routes (Network > Routes) and management routes (System > Platform) are SEPARATE routing tables. The route you added only affects TMM traffic. Management SSH uses the host OS routing table. Add a management route under System > Platform for 10.1.20.0/24.
F5 DOCUMENTATION: K13250, K26588, K13284, K13946

## Slide 76
76 © 2026 F5
Exam checkpoints (continued)
Q5
U/A
What does 'strict' mode on a route domain do? When would you disable it?
Q6
U/A
What is the difference between a floating self IP and a non-floating self IP? Which one should servers use as their default gateway?
Networking quick reference
Port lockdown: None (default, ICMP only) → Allow Defaults (admin + HA) → Allow Custom → Allow All
Self IP: Floating (HA, moves with failover) vs non-floating (device-specific)
VLAN: Tagged (802.1Q, multiple per interface) vs untagged (one per interface)
Routes: TMM (Network > Routes) and management (System > Platform) are SEPARATE
Route domain: %RD notation for overlapping IPs. RD0 = default. Strict = no cross-domain traffic.
HA minimum ports: TCP 4353 (ConfigSync) + UDP 1026 (failover heartbeat)
Notes: WHAT THIS SLIDE TEACHES
Final checkpoints plus networking reference card.
Q5 ANSWER: Strict mode prevents traffic from crossing between route domains. When strict is enabled, packets cannot be forwarded from one RD to another — each RD is completely isolated.
Disable strict when: You have a shared services model — for example, a shared internet gateway in a parent route domain that child route domains need to reach. With strict disabled on the child, unmatched routes fall through to the parent's routing table.
Q6 ANSWER:
- Non-floating: Static, stays on one specific BIG-IP device. Used for device management (SSH to a specific unit).
- Floating: Shared between HA peers. Moves to the active device during failover. Part of a traffic group.
Servers should use the FLOATING self IP as their default gateway. This ensures that when failover occurs, the gateway address moves to the new active device, and server traffic continues to flow without reconfiguration. If servers used a non-floating self IP as their gateway, failover would break their connectivity.
F5 DOCUMENTATION: K26588 (route domains), K13284 (self IPs), K13946 (HA networking)

## Slide 77
77 © 2026 F5
Networking TMSH reference
Task | TMSH command
Create tagged VLAN | create net vlan vlan-30 tag 30 interfaces add { 1.3 { tagged } }
Create self IP | create net self HA-IP address 10.1.30.245/24 vlan vlan-30 allow-service default
Port lockdown: None | modify net self 10.1.10.245/24 allow-service none
Port lockdown: Defaults | modify net self 10.1.10.245/24 allow-service default
Port lockdown: Custom | modify net self 10.1.10.245/24 allow-service add { tcp:22 tcp:443 tcp:4353 udp:1026 }
Create route domain | create net route-domain 1 vlans add { tenant-a-vlan } strict enabled
Self IP in route domain | create net self rd1-self address 10.10.10.245%1/24 vlan tenant-a-vlan
Add static route | create net route my-route network 10.1.20.0/24 gw 10.1.10.1
Configure DNS | modify sys dns name-servers add { 8.8.8.8 }
Configure NTP | modify sys ntp servers add { pool.ntp.org }
Show interfaces | show net interface
List route domains | list net route-domain
allow-service values: none | default | all | add { tcp:22 tcp:443 udp:1026 tcp:4353 } | %RD notation: 10.10.10.1%1 = RD1, 10.10.10.1%2 = RD2
Notes: WHAT THIS SLIDE TEACHES
Complete TMSH reference for Lab 8 networking commands including route domain configuration and all port lockdown modes.
F5 DOCUMENTATION: K13250 (port lockdown), K26588 (route domains), K13284 (self IPs), K7595 (VLANs)

## Slide 78
F5CTSLTM4.03 | U/A | Explain the uses of user roles and administrative partitions
F5CTSLTM1.04 | U/A | Determine how to limit administrative access to LTM (GUI/CLI)
LAB 9
Roles and Partitions
User roles control what actions a user can perform. Partitions control
which objects a user can see and modify. Local and remote
authentication manage how users are validated.
50 min | 20 min slides + 30 min lab
Notes: WHAT THIS SLIDE TEACHES
Section opener for Lab 9. Maps to F5CTSLTM4.03 and F5CTSLTM1.04. 301a: 2.04–2.05.
F5 DOCUMENTATION: K14020 (roles), K13403 (partitions), K15811 (LDAP), K15596 (TACACS+), K15763 (RADIUS)

## Slide 79
79 © 2026 F5
Default user roles
Eight built-in roles assigned per user, per partition
Role | Read | Create / Modify | Users | Shell | Description
Administrator | ✔ | ✔ All partitions | ✔ | bash+tmsh | Full unrestricted access. Users, system, all LTM objects.
Resource Admin | ✔ | ✔ All LTM | ✘ | tmsh | All LTM config. No user management or system settings.
Manager | ✔ | ✔ Own partition | ✘ | tmsh | Full LTM in assigned partition. Read-only /Common.
Cert Manager | ✔ | Certs only | ✘ | tmsh | Manage SSL certificates/keys only.
iRule Manager | ✔ | iRules only | ✘ | tmsh | Create/modify/delete iRules only.
Operator | ✔ | Enable/disable | ✘ | tmsh | Enable/disable VS, members, nodes. NOC ops.
Guest | Read-only | ✘ | ✘ | None | View-only. Auditors, support.
No Access | ✘ | ✘ | ✘ | None | Block access to a specific partition.
Terminal access (independent of role, set per user)
Disabled: GUI only. No SSH. tmsh: SSH → TMSH. Cannot escape to bash. 'exit' logs out. Advanced shell: Full bash. Admin only.
Notes: WHAT THIS SLIDE TEACHES
All 8 default BIG-IP roles with capabilities. See Lab 9 v2 slide 2 notes for full documentation.
F5 DOCUMENTATION: K14020

## Slide 80
80 © 2026 F5
/Common vs created partitions
Every BIG-IP has /Common. Created partitions reference /Common but cannot modify it.
/Common partition
Always exists — cannot be deleted
Default partition for all objects
Objects without a partition go here.
Visible to ALL users (read-only)
Every user sees /Common. Greyed out in GUI.
Shared infrastructure lives here
VLANs, self IPs, routes, shared pools, profiles, iRules, monitors, certs.
User-created partition
Created by administrators
Isolated container
Invisible to other partition users.
Can REFERENCE /Common objects
create ltm virtual test_vs
pool /Common/www_pool
Live reference — /Common changes propagate.
Separate config file
/config/partitions/[name]/bigip.conf
How they relate
/Common ──┬──┬── referenced by all partitions (read-only)
│ │
/web_part /api_part (isolated from each other)
Admin modifies /Common → all partitions see the change immediately.
Notes: WHAT THIS SLIDE TEACHES
/Common is the shared foundation. See Lab 9 supplement notes for full documentation.
F5 DOCUMENTATION: K13403

## Slide 81
81 © 2026 F5
GUI configuration walkthrough
Creating partitions and local users in the BIG-IP Configuration Utility
Create Partition
create auth partition test_partition
Create Local User
create auth user testuser {
password testpass shell tmsh
partition-access add {
test_partition { role manager } } }
After creation: Partition appears in upper-right dropdown. User can log in immediately. Role + Partition are paired — select role first, then assign to partition. Can add multiple role/partition pairs per user.
Notes: WHAT THIS SLIDE TEACHES
GUI and TMSH for creating partitions and local users. See Lab 9 supplement notes for full documentation.
KEY: Create partition FIRST, then user. Role+Partition paired. Terminal access independent of role.
F5 DOCUMENTATION: K14020, K13403

## Slide 82
82 © 2026 F5
User access within a partition
What a partition user can see, use, create, and modify
Action | Own partition | /Common partition | Other partitions
View objects | ✔ Full visibility | ✔ Full visibility | ✘ Not visible
Create objects | ✔ Full create | ✘ Cannot create | ✘ Cannot create
Modify objects | ✔ Full modify | ✘ Greyed out (read-only) | ✘ Not accessible
Delete objects | ✔ Full delete | ✘ Cannot delete | ✘ Not accessible
Reference objects | ✔ Direct reference | ✔ Can use in own partition | ✘ Cannot reference
Example: Manager in test_partition
✔ Create test_vs referencing /Common pool:
create ltm virtual test_vs destination 10.1.10.120:80 pool /Common/www_pool
Works: VS in own partition, pool is a read-only REFERENCE (not copy). Pool changes propagate.
✘ Attempt to modify /Common pool:
modify ltm pool /Common/www_pool members add { 10.1.20.14:80 }
FAILS: No modify access to /Common. Only administrators can change Common objects.
Notes: WHAT THIS SLIDE TEACHES
Partition access matrix. See Lab 9 v2 slide 4 notes for full documentation.
F5 DOCUMENTATION: K13403

## Slide 83
83 © 2026 F5
Remote user authentication
Offload user management to external directories. Configure under System > Users > Authentication.
LDAP (TCP 389 / 636 (SSL))
Host: 10.1.20.252
Port: 389
Remote Directory Tree:
dc=f5demo,dc=com
Bind DN:
cn=Directory Manager
Bind Password: default
SSL: Disabled
Default Role: Administrator
modify auth source type ldap
modify auth ldap system-auth {
servers add { 10.1.20.252 }
search-base-dn
dc=f5demo,dc=com
bind-dn
cn=Directory Manager
bind-pw default
}
RADIUS (UDP 1812)
Server: 10.1.20.253
Port: 1812
Secret: shared_secret
Default Role: Operator
Role assignment via
F5 VSA attributes
in RADIUS response
modify auth source type radius
modify auth radius
system-auth {
servers add {
10.1.20.253 {
secret shared_secret
} } }
TACACS+ (TCP 49)
Server: 10.1.20.254
Port: 49
Secret: shared_secret
Service: ppp
Protocol: ip
Default Role: Operator
Per-command authorization
supported (audit every cmd)
modify auth source type tacacs
modify auth tacacs
system-auth {
servers add {
10.1.20.254 }
secret shared_secret
service ppp
protocol ip
}
Auth fallback: Remote REJECTS user → denied (no fallback). Remote UNREACHABLE → falls back to local auth. Always keep a local admin account as backup.
Revert to local: modify auth source type local | GUI: System > Users > Authentication > Change > Local
Notes: WHAT THIS SLIDE TEACHES
This slide covers remote user authentication and authorization, showing GUI configuration fields and TMSH commands for all three methods (LDAP, RADIUS, TACACS+). Directly addresses 301a objective 2.04: "Explain how to configure remote authentication."
FULL TECHNICAL EXPLANATION
LDAP (Lightweight Directory Access Protocol):
Most common in enterprise. Used with Active Directory and OpenLDAP.
- GUI: System > Users > Authentication > Change > LDAP
- Key fields: Host (LDAP server IP), Port (389 or 636 for LDAPS), Remote Directory Tree (base DN for user search), Bind DN (account used to search the directory), Bind Password, SSL (enable for LDAPS)
- Role assignment: Default role for all LDAP users, OR map LDAP groups to BIG-IP roles using "Remote Role Groups" configuration
- The lab uses: Host 10.1.20.252, Port 389, Tree dc=f5demo,dc=com, Bind DN cn=Directory Manager
RADIUS (Remote Authentication Dial-In User Service):
Centralized AAA. Common in ISP/telecom.
- GUI: System > Users > Authentication > Change > RADIUS
- Key fields: Server IP, Port (1812), Secret (shared key), Default Role
- Role assignment: Via F5 Vendor-Specific Attributes (VSA) in the RADIUS response. The RADIUS server includes F5-LTM-User-Info-1 attribute with the role name. If no VSA, the default role is used.
- F5 VSA: Vendor ID 3375, Attribute F5-LTM-User-Info-1 = "adm" (admin), "mgr" (manager), "op" (operator), etc.
TACACS+ (Terminal Access Controller Access-Control System Plus):
Cisco's AAA protocol. Provides per-command authorization.
- GUI: System > Users > Authentication > Change > TACACS+
- Key fields: Server IP, Port (49), Secret, Service (ppp), Protocol (ip)
- Role assignment: Via TACACS+ attributes. Can map to BIG-IP roles.
- UNIQUE CAPABILITY: Per-command authorization. The TACACS+ server can control which TMSH commands a user can execute. Every command the user types is sent to the TACACS+ server for authorization before execution. This provides the most granular access control.
- Service/Protocol: Set to "ppp" and "ip" for standard BIG-IP integration.
AUTH FALLBACK BEHAVIOR (CRITICAL EXAM CONCEPT):
When remote auth is configured, the BIG-IP handles authentication in this order:
1. User submits credentials (GUI or SSH)
2. BIG-IP forwards credentials to remote server
3. IF remote server AUTHENTICATES → access granted with remote-assigned role
4. IF remote server REJECTS → access DENIED. NO fallback to local.
5. IF remote server is UNREACHABLE → BIG-IP falls back to LOCAL auth
This means:
- LDAP user with wrong password → denied (LDAP server is reachable and rejected)
- LDAP server is down → local admin can still log in (fallback to local)
- Local user with LDAP configured and LDAP server up → denied (LDAP doesn't know this user, LDAP rejects, no fallback)
SECURITY BEST PRACTICE: Always maintain a local admin account. If the remote auth server goes down, you need a local account to log in and fix the issue.
REMOTE ROLE GROUPS (LDAP Advanced):
For more granular role mapping, configure Remote Role Groups:
- System > Users > Remote Role Groups
- Map LDAP group membership to specific BIG-IP roles
- Example: LDAP group "network-admins" → Administrator role, "noc-team" → Operator role
COMMON STUDENT MISTAKES
- Deleting the local admin after configuring remote auth → locked out if remote server fails
- Thinking local users still work when remote auth is active and remote server is UP → they don't (unless remote server doesn't know the user AND is configured to allow fallback)
- Not testing fallback before production deployment
- Confusing "rejected" (server says no) with "unreachable" (server is down) — only unreachable triggers fallback
PIVOT QUESTION
"LDAP is configured. An LDAP user enters the wrong password. The LDAP server is up. Does the BIG-IP try local auth?"
ANSWER: No. The LDAP server is reachable and explicitly rejected the credentials. The BIG-IP trusts this rejection and denies access. Fallback to local ONLY happens when the remote server is unreachable (network error, server down). This is by design — if fallback happened on rejection, it would create a security hole.
F5 DOCUMENTATION
- LDAP auth: https://my.f5.com/manage/s/article/K15811
- RADIUS auth: https://my.f5.com/manage/s/article/K15763
- TACACS+ auth: https://my.f5.com/manage/s/article/K15596
- Remote role groups: https://my.f5.com/manage/s/article/K3472
EXAM QUESTION PATTERNS
- "Remote server rejects user. Fallback to local?" → No
- "Remote server unreachable. Fallback to local?" → Yes
- "Which auth method supports per-command authorization?" → TACACS+
- "How are roles assigned with RADIUS?" → F5 Vendor-Specific Attributes (VSA)

## Slide 84
84 © 2026 F5
Lab 9 — Hands-on exercises
30 minutes | Lab guide: Module 9
# | Activity | Key tasks | Time
1 | Roles + Partitions | Create test_partition. Create testuser (Manager, tmsh). Log in — view Common (greyed), create test_vs. SSH test. Check /config/partitions/ file. | 20m
2 | Remote Auth | Configure LDAP (10.1.20.252, dc=f5demo,dc=com). Test adminuser/password. Verify local testuser still works. Revert to local. | 10m
Activity 1 discovery: testuser sees /Common objects (greyed out), creates test_vs in test_partition using /Common/www_pool. Config in /config/partitions/test_partition/bigip.conf.
Activity 2 key test: With LDAP active: LDAP user adminuser works. Local testuser works ONLY because LDAP server is UP but doesn't know testuser (falls through). If LDAP rejects → denied.
Notes: WHAT THIS SLIDE TEACHES
Lab launch. Two activities: partition/role testing and LDAP authentication.
F5 DOCUMENTATION: K14020, K13403, K15811

## Slide 85
85 © 2026 F5
Exam checkpoints
Q1
U/A
A Manager in test_partition sees /Common/www_pool but settings are greyed out. They create test_vs using www_pool. Expected?
Q2
U/A
Which role can manage SSL certificates but cannot create or modify virtual servers?
Q3
U/A
LDAP is configured. Server is UP. An LDAP user enters the wrong password. Does the BIG-IP fall back to local authentication?
Q4
U/A
Which remote auth method supports per-command authorization, controlling which TMSH commands a user can execute?
Key facts to memorize
8 roles: Administrator > Resource Admin > Manager > Cert Manager > iRule Manager > Operator > Guest > No Access
Auth fallback: Rejected = denied. Unreachable = fallback to local. TACACS+ = per-command auth.
/Common: visible to all (read-only). Partitions: isolated. References to /Common are live.
Notes: WHAT THIS SLIDE TEACHES
Q1: Yes. Manager can VIEW Common (read-only), CREATE in own partition, REFERENCE Common objects.
Q2: Certificate Manager.
Q3: No. Server is reachable and rejected. Fallback only on unreachable.
Q4: TACACS+. It sends each TMSH command to the server for authorization.
F5 DOCUMENTATION: K14020, K13403, K15811, K15596

## Slide 86
86 © 2026 F5
TMSH reference
Task | Command
Create partition | create auth partition test_partition
Create local user | create auth user testuser password testpass partition-access add { test_partition { role manager } } shell tmsh
Assign multi-partition roles | modify auth user testuser partition-access add { prod_partition { role guest } }
Switch partition (TMSH) | cd /test_partition
Configure LDAP | modify auth source type ldap; modify auth ldap system-auth servers add { 10.1.20.252 } search-base-dn dc=f5demo,dc=com
Configure RADIUS | modify auth source type radius; modify auth radius system-auth servers add { 10.1.20.253 { secret s3cret } }
Configure TACACS+ | modify auth source type tacacs; modify auth tacacs system-auth servers add { 10.1.20.254 } secret s3cret service ppp protocol ip
Revert to local auth | modify auth source type local
List users | list auth user
View partition config | cat /config/partitions/test_partition/bigip.conf
Decision tree
Full access + users → Administrator | Full LTM only → Resource Admin | One partition → Manager
Certs only → Cert Manager | iRules only → iRule Manager | Enable/disable → Operator | View-only → Guest
Remote users → LDAP (AD/OpenLDAP) or RADIUS (ISP) or TACACS+ (per-command auth, Cisco)
Notes: WHAT THIS SLIDE TEACHES
Complete TMSH reference for roles, partitions, and all three remote auth methods.
F5 DOCUMENTATION: K14020, K13403, K15811, K15763, K15596

## Slide 87
F5CTSLTM4.02 | U/A | Configure HA — traffic groups vs HA groups, failover prevention, network failover components
F5CTSLTM4.11 | U/A | Determine failover cause — network failover settings, unicast vs multicast, logs
F5CTSLTM4.12 | U/A | Determine loss of HA / sync failure — trust, groups, traffic groups, log interpretation
LAB 10
Device Service Clusters
and High Availability
Build device trust, sync-failover groups, traffic groups, and HA groups.
Configure failover (unicast/multicast), mirroring, and active/active.
Troubleshoot sync failures and failover using logs.
60 min | 15 min slides + 45 min lab
Notes: WHAT THIS SLIDE TEACHES
Opener for Lab 10. 301a: 2.05–2.07. Three Beta objectives with expanded sub-bullet detail in the opener text.
F5 DOCUMENTATION: K13946, K14592, K13639, K16427 (HA groups)

## Slide 88
88 © 2026 F5
DSC building blocks
Device Service Clusters require these components configured in order
1
Device trust
Certificate-based trust between BIG-IPs. Foundation for all HA. Built using peer's mgmt IP + admin creds. Creates hidden device-trust-group for cert sync.
2
Device group
Trusted devices that sync and/or fail over. Sync-Only: config only. Sync-Failover: config + failover. Up to 8 devices. Network Failover checkbox required.
3
Traffic group
Container for floating objects (virtual addresses, floating self IPs, SNAT translations). Determines which BIG-IP is active for a set of traffic.
4
Config sync
Pushes config via CMI (TCP 4353). Initial sync: push or pull. After: changes trigger 'Changes Pending'. Full overwrite or incremental.
5
Network failover
Heartbeat (UDP 1026). Lost heartbeat → standby promotes. Unicast (standard) or multicast (Viprion). Multiple unicast: ANY failure triggers failover.
6
Mirroring
Replicates connections + persistence to standby (TCP 1028). Without it, failover drops all state. Only mirrors records created AFTER enablement.
Prerequisites: Matching provisioning (LTM+AVR on both). NTP synced. HA VLAN with Allow Defaults (TCP 4353, UDP 1026). Device certs renewed (3650 days).
Notes: WHAT THIS SLIDE TEACHES
Six DSC building blocks. See Lab 10 v1 slide 2 notes for full documentation.
F5 DOCUMENTATION: K13946, K14592, K13639

## Slide 89
89 © 2026 F5
Building a DSC step-by-step
Complete workflow from standalone to synchronized HA pair
1
Prepare both devices
Matching provisioning. HA VLAN + self IP (Allow Defaults). NTP synced. Renew device cert (3650 days). Reset device trust cert.
2
Configure device settings
On EACH: Device Mgmt > Devices > (Self). ConfigSync = HA IP. Failover Unicast = HA IP:1026. Mirror primary = HA IP.
3
Build device trust
On ONE: Device Mgmt > Device Trust > Add. Peer mgmt IP + admin creds. Retrieve Info > Finished. Verify Peer Authorities.
4
Create device group
On ONE: Device Mgmt > Device Groups > Create. Type: Sync-Failover. Add both devices. Check Network Failover.
5
Initial sync
Device with good config: Overview > select device > Sync Device to Group. Wait 30s. WARNING: either device can sync during initial phase.
6
Verify HA
Both: In Sync, Active/Standby. Test: browse VIP. Force failover: Devices > (Self) > Force to Standby. Browse again.
Notes: WHAT THIS SLIDE TEACHES
DSC build workflow. See Lab 10 v1 slide 3 notes.
F5 DOCUMENTATION: K13946, K14592, K13639

## Slide 90
90 © 2026 F5
Traffic groups vs HA groups
Two different mechanisms: traffic groups control WHERE traffic goes, HA groups control WHICH device is preferred
Traffic groups
Purpose: Container for floating objects. Determines which BIG-IP is ACTIVE for a set of traffic.
Contains:
• Virtual addresses (NOT virtual servers)
• Floating self IPs (server gateway)
• SNAT translation addresses
Active/Standby: one TG, one active device.
Active/Active: multiple TGs on different devices.
Rule: All objects for one app in SAME TG.
HA groups
Purpose: Scoring system that determines which device SHOULD be active based on health.
Health score based on:
• Pools (weight per pool based on available members)
• Trunks (weight per trunk based on active links)
• VLANs (weight per VLAN based on link status)
How it works: Each device calculates a score. If active device's score drops below standby's score → failover.
Use case: Ensure the healthier device is always active.
Head-to-head comparison
 | Traffic group | HA group
Controls | Which device is active for specific traffic | Which device SHOULD be active based on health
Contains | Floating objects (VIPs, self IPs, SNATs) | Health scores (pools, trunks, VLANs with weights)
Triggers failover? | No — moved by failover, doesn't cause it | Yes — score drop below peer triggers failover
Notes: WHAT THIS SLIDE TEACHES
This slide directly addresses F5CTSLTM4.02: "Compare and contrast traffic groups vs HA groups." Students must understand that these are two DIFFERENT mechanisms that work together.
FULL TECHNICAL EXPLANATION
TRAFFIC GROUPS — WHERE TRAFFIC GOES:
A traffic group is a collection of floating objects that move together during failover. The default traffic-group-1 contains all floating objects unless you create additional groups.
Objects assigned to traffic groups:
- Virtual ADDRESSES (not virtual servers — the ADDRESS object): LT > Virtual Servers > Virtual Address List > select > Traffic Group
- Floating self IPs: Network > Self IPs > select > Traffic Group
- SNAT translation addresses: LT > Address Translation > SNAT Translation List > Traffic Group
Active/Standby: One traffic group → one device active for all traffic. Simple but wastes standby capacity.
Active/Active: Multiple traffic groups → each active on a different device. Both devices process traffic.
CRITICAL RULE: All objects supporting one application must be in the SAME traffic group. If www_vs VIP is in tg-2 but its SNAT pool is in tg-1, failover of tg-2 breaks the application because the SNAT address is still on the other device.
HA GROUPS — WHICH DEVICE IS PREFERRED:
An HA group is a health scoring mechanism. Each device calculates a score based on the health of its resources:
- Pools: Weight assigned per pool. Score based on available members / total members.
- Trunks: Weight assigned per trunk. Score based on active links / total links.
- VLANs: Weight assigned per VLAN. Score based on link status.
The device with the HIGHER score should be active. If the active device's score drops below the standby's score, failover is triggered.
Example:
Active device: www_pool = 100 pts (3/3 members up), trunk1 = 50 pts (2/2 links). Score = 150.
Active device loses a pool member: www_pool = 67 pts (2/3 members). Score = 117.
Standby device: www_pool = 100 pts (3/3 members), trunk1 = 50 pts. Score = 150.
150 > 117 → failover occurs because standby is healthier.
Configuration: Device Management > Traffic Groups > select traffic group > HA Group section > Enable > Add pools, trunks, VLANs with weights.
HOW THEY WORK TOGETHER:
1. HA groups determine WHEN to fail over (based on health scores)
2. Traffic groups determine WHAT moves during failover (floating objects)
3. Network failover determines HOW failover is detected (heartbeat)
Without HA groups: Failover only happens on total device failure or manual action.
With HA groups: Failover can happen when the device is still UP but degraded (lost pool members, lost trunk links).
COMMON STUDENT MISTAKES
- Confusing traffic groups (object containers) with HA groups (health scores)
- Thinking traffic groups cause failover (they don't — they're moved BY failover)
- Not understanding HA group scoring — it's proportional (available/total × weight), not binary
F5 DOCUMENTATION: K14592 (traffic groups), K16427 (HA groups), K13946 (failover)
EXAM QUESTION PATTERNS
- "What triggers failover when a pool loses members?" → HA group (if configured)
- "Traffic group vs HA group?" → TG = what moves. HA group = when to move.
- "All pool members down but no failover. Why?" → HA group not configured, or weight is 0

## Slide 91
91 © 2026 F5
HA groups and failsafe
Two mechanisms that trigger failover based on device health — not just heartbeat loss
HA group scoring
Each device calculates a health score:
Score = Σ (available/total × weight) per object
Scored objects and weights:
• Pools: available members / total members × weight
• Trunks: active links / total links × weight
• VLANs: link up/down × weight
Example:
www_pool weight=100: 3/3 up = 100 pts
trunk1 weight=50: 2/2 links = 50 pts
Total score = 150
Pool member fails → 2/3 = 67 pts
New score = 117. Peer score = 150.
150 > 117 → failover to healthier device
Failsafe mechanisms
VLAN failsafe
Monitors traffic on a VLAN. If no traffic is received for the timeout period, failsafe triggers. Catches: upstream switch failure, cable pull, silent VLAN death.
Config: Network > VLANs > [vlan] > Failsafe
Timeout: 90 sec (default). Action: failover.
Gateway failsafe
Pings the default gateway. If the gateway becomes unreachable, the BIG-IP cannot route traffic → failsafe triggers. Catches: router failure.
Config: System > HA > Gateway Failsafe
Interval + Timeout settings.
Hardware watchdog
TMM heartbeat monitored by host OS. If TMM stops responding (crash/hang), hardware watchdog triggers failover automatically.
When to use each
Mechanism | Triggers on | Use case | Configuration
HA group | Pool member loss, trunk link loss, VLAN failure | Fail over to healthier device when resources degrade | Traffic group > HA Group > Enable > Add pools/trunks/VLANs
VLAN failsafe | No traffic on VLAN for timeout period | Detect silent VLAN failure (switch crash, cable pull) | Network > VLANs > [vlan] > Failsafe > Enable
Gateway failsafe | Default gateway unreachable | Detect upstream router failure | System > HA > Gateway Failsafe
Hardware watchdog | TMM stops responding | TMM crash or hang recovery | Automatic (always enabled)
Notes: WHAT THIS SLIDE TEACHES
This slide provides deep coverage of HA groups (the scoring mechanism) and failsafe mechanisms, directly addressing F5CTSLTM4.02: "Compare and contrast traffic groups vs HA groups" and "Determine what prevented an expected failover."
FULL TECHNICAL EXPLANATION
HA GROUPS — HEALTH-BASED FAILOVER:
HA groups provide intelligent failover based on resource health rather than total device failure. Without HA groups, failover only happens when the active device is completely unreachable (heartbeat lost) or manually triggered. With HA groups, failover can happen when the device is still UP but degraded.
Configuration:
Device Management > Traffic Groups > select traffic group > HA Group section > Enable
Then add scored objects:
- Pools: Select pools to monitor. Assign a weight (importance) to each pool. The score for each pool = (available members / total members) × weight.
- Trunks: Select trunks. Weight per trunk. Score = (active links / total links) × weight.
- VLANs: Select VLANs. Weight per VLAN. Score = link status (1 or 0) × weight.
The total HA group score = sum of all individual object scores.
SCORING EXAMPLE (detailed):
Device A (active):
www_pool: 3/3 members up, weight 100 → score = (3/3) × 100 = 100
api_pool: 2/2 members up, weight 50 → score = (2/2) × 50 = 50
trunk1: 2/2 links up, weight 30 → score = (2/2) × 30 = 30
Total: 180
Device B (standby):
www_pool: 3/3, weight 100 → 100
api_pool: 2/2, weight 50 → 50
trunk1: 2/2, weight 30 → 30
Total: 180
Now www_pool on Device A loses 2 members:
www_pool: 1/3, weight 100 → score = (1/3) × 100 = 33
Total: 33 + 50 + 30 = 113
Device B still at 180. Since 180 > 113, Device A's traffic group fails over to Device B.
IMPORTANT: HA groups are configured PER TRAFFIC GROUP, not per device. Different traffic groups can have different HA group configurations.
FAILSAFE MECHANISMS:
VLAN FAILSAFE:
Purpose: Detect when a VLAN goes silent — no traffic at all. This catches "silent failures" where the physical link is still up but the upstream switch or connected network has failed.
Configuration: Network > VLANs > select VLAN > Configuration > Failsafe
Settings:
- Failsafe: Enabled/Disabled
- Failsafe Timeout: Number of seconds with no traffic before triggering (default 90 seconds)
- Failsafe Action: Failover (trigger HA failover) or Reboot (restart the BIG-IP)
How it works: The BIG-IP monitors incoming traffic on the VLAN. If NO traffic is received for the timeout period, failsafe triggers. Important: this includes ALL traffic, not just specific types. A completely idle VLAN will trigger failsafe even if nothing is wrong — so only enable on VLANs that should always have traffic.
TMSH: modify net vlan client_vlan failsafe enabled failsafe-timeout 90 failsafe-action failover
GATEWAY FAILSAFE:
Purpose: Detect when the default gateway (upstream router) becomes unreachable. If the BIG-IP can't reach its gateway, it can't route traffic — even though the device itself is healthy.
Configuration: System > High Availability > Gateway Failsafe
Settings: Gateway pool (ping the gateway), interval, timeout.
HARDWARE WATCHDOG:
Purpose: Detect TMM process failure. The host OS monitors TMM's heartbeat. If TMM stops responding (crash, hang, resource exhaustion), the hardware watchdog triggers failover automatically.
This is always enabled — no configuration needed. It's a last-resort mechanism for catastrophic TMM failure.
FAILSAFE vs HA GROUPS:
- HA groups: Proportional health monitoring. Score changes gradually as resources degrade. Good for "the device is working but degraded" scenarios.
- Failsafe: Binary detection. Either traffic is flowing or it's not. Either the gateway responds or it doesn't. Good for "something is completely dead" scenarios.
COMMON STUDENT MISTAKES
- Enabling VLAN failsafe on a VLAN that's normally quiet → false positive failover
- Not understanding that HA group scores are proportional, not binary (1/3 pool members = 33% score, not 0%)
- Confusing HA groups with device groups (device groups are for sync/failover membership; HA groups are for health scoring)
- Not configuring any health-based failover (HA groups or failsafe) → device only fails over on total failure or manual action
PIVOT QUESTION
"A pool has 4 members with weight 100 in the HA group. Two members fail. The peer device has all 4 members healthy. Does failover occur?"
ANSWER: Active device score for this pool = (2/4) × 100 = 50. Peer score = (4/4) × 100 = 100. If this is the only scored object, peer (100) > active (50) → YES, failover occurs. If there are other scored objects, you must calculate the total score for both devices and compare.
F5 DOCUMENTATION
- HA groups: https://my.f5.com/manage/s/article/K16427
- VLAN failsafe: https://my.f5.com/manage/s/article/K13297
- Gateway failsafe: https://my.f5.com/manage/s/article/K13297
- Failover overview: https://my.f5.com/manage/s/article/K13946
EXAM QUESTION PATTERNS
- "Pool members down but no failover. Why?" → HA group not configured (no health scoring)
- "VLAN failsafe timeout is 90. No traffic for 60 seconds. Failover?" → No (below timeout)
- "HA group score calculation?" → (available / total) × weight per object, sum all objects

## Slide 92
92 © 2026 F5
Network failover and mirroring
How devices detect failure, how state is preserved, and unicast vs multicast
Unicast vs multicast failover
 | Unicast (standard) | Multicast (Viprion only)
Transport | UDP 1026 — direct IP-to-IP between peers | UDP 1026 — multicast group 224.0.0.245
Platform | All BIG-IP platforms (appliance, VE, Viprion) | Viprion chassis ONLY (inter-blade failover)
Configuration | Per device: add HA self IP + port 1026 | Enabled globally on Viprion cluster
Multiple addresses | Can add multiple — ANY failure triggers failover | Single multicast group — all blades participate
Use case | Standard HA pairs and clusters | Viprion chassis redundancy
Failover triggers
• Network failover heartbeat lost (UDP 1026)
• Manual: Force to Standby
• HA group score drops below peer
• Failsafe: VLAN/interface failure
• System failure (TMM crash, power loss)
Mirroring
• Persistence: profile > Mirror Persistence ✔
• Connections: VS > Connection Mirroring ✔
• SNAT: SNAT > Connection Mirroring ✔
Only mirrors records created AFTER enablement.
Mirror address = HA self IP. Uses TCP 1028.
Without mirroring: failover drops ALL connections and persistence. With mirroring: connections continue seamlessly on the new active device.
Notes: WHAT THIS SLIDE TEACHES
This slide patches two gaps: the unicast vs multicast comparison (F5CTSLTM4.11: "Differentiate between unicast and multicast network failover modes") and detailed failover trigger list.
FULL TECHNICAL EXPLANATION
UNICAST FAILOVER:
- Standard method for all BIG-IP platforms (appliance, VE, Viprion)
- Each device sends UDP 1026 heartbeat packets directly to the peer's HA self IP
- Configured per device: Device Management > Devices > (Self) > Network Failover > Failover Unicast Configuration > Add > HA self IP, Port 1026
- MULTIPLE UNICAST ADDRESSES: You can configure more than one unicast address per device. If ANY address becomes unreachable, failover is triggered. This is aggressive — it's designed for fast failure detection. Use case: configure both HA VLAN IP and management IP for redundancy.
MULTICAST FAILOVER:
- Viprion chassis ONLY — used for inter-blade failover within a chassis
- Uses multicast group address 224.0.0.245 on UDP 1026
- All blades in the chassis participate in the multicast group
- Not applicable to standard BIG-IP appliances or VE
- Enabled under: Device Management > Devices > (Self) > Network Failover > Failover Multicast Configuration
WHEN DOES FAILOVER HAPPEN:
1. Network failover: Heartbeat lost → standby waits for the failover timeout → promotes to active
2. Manual: Admin clicks Force to Standby → immediate failover
3. HA group: Active device's health score drops below standby → automatic failover
4. Failsafe: Interface or VLAN goes down → triggers failover if failsafe is configured
5. System failure: TMM crash, kernel panic, power loss → standby detects loss of heartbeat
WHAT HAPPENS DURING FAILOVER:
1. Standby detects active failure
2. Standby promotes to Active status
3. Floating objects (VIPs, self IPs in traffic groups) move to new active
4. Gratuitous ARPs sent for all floating IPs (updates switch MAC tables)
5. New active device starts processing traffic
F5 DOCUMENTATION: K13946, K14592, K75975904 (failover troubleshooting), K54622241 (mirroring)
EXAM QUESTION PATTERNS
- "Unicast vs multicast?" → Unicast = IP-based, all platforms. Multicast = Viprion only, 224.0.0.245.
- "Multiple unicast addresses. One fails. Failover?" → YES (ANY failure triggers)
- "Without mirroring, what happens on failover?" → All connections and persistence lost

## Slide 93
93 © 2026 F5
HA logs and troubleshooting
Identify failover causes and sync failures from logs and TMSH commands
Common /var/log/ltm messages
Log message pattern | Cause | Fix
01071681:5: ... ACTIVE for traffic group | Device became active for a traffic group (normal failover) | Verify: intended failover or investigate trigger
01140029:5: HA daemon ... no longer hearing | Network failover heartbeat lost from peer | Check: HA VLAN, port lockdown, cables, peer status
01071431:4: ... is not in sync | Config sync out of sync (Changes Pending) | Run config sync from correct device
01070712:4: ... config sync failed | Sync failed — dependency error, cert issue, or port blocked | Check TCP 4353, resolve dependencies, try full overwrite
01071406:1: ... device trust certificate expired | Device trust cert expired → all HA communication fails | Renew cert (3650 days), reset device trust
TMSH troubleshooting commands
# Check sync status (In Sync / Changes Pending / Awaiting Initial Sync)
show cm sync-status
# Check failover status (active / standby / offline)
show sys failover
# Check device group status and members
show cm device-group
# Check traffic group status (which device owns which TG)
show cm traffic-group
# View failover and HA log messages
tail -f /var/log/ltm | grep -iE 'failover|sync|trust|HA'
Notes: WHAT THIS SLIDE TEACHES
This slide patches the log interpretation gap for both F5CTSLTM4.11 ("Identify the cause of failover using logs and statistics") and F5CTSLTM4.12 ("Interpret log messages to determine the cause of high availability issues").
FULL TECHNICAL EXPLANATION
LOG FILE: /var/log/ltm
All HA-related events are logged here. Key message patterns:
FAILOVER EVENTS:
- "ACTIVE for traffic group traffic-group-1" → Device just became active for that TG. Check: was this intentional (manual failover) or unexpected (heartbeat loss, HA group score)?
- "STANDBY for traffic group traffic-group-1" → Device went to standby. Normal after Force to Standby.
- "no longer hearing from device" → Network failover heartbeat lost. The device stopped receiving UDP 1026 from its peer. Causes: HA VLAN down, port lockdown blocking 1026, cable failure, peer device crashed.
- "Failover condition" → Generic failover trigger. Check preceding log entries for the specific cause.
CONFIG SYNC EVENTS:
- "is not in sync" → Configuration has changed on one device and hasn't been synced. The GUI shows "Changes Pending" in yellow.
- "config sync failed" → Sync attempted but failed. Common causes:
1. TCP 4353 blocked (port lockdown)
2. Object dependency error (object A references object B which doesn't exist on the peer)
3. Certificate trust issue (expired cert, trust not established)
4. Provisioning mismatch (one device has AVR, the other doesn't)
- "config sync completed successfully" → Sync worked. Both devices in sync.
TRUST EVENTS:
- "device trust certificate expired" → CRITICAL. The device certificate used for trust has expired. ALL HA communication fails — no sync, no failover, no mirroring. Fix: renew certificate with a long lifetime, reset device trust.
- "peer certificate verification failed" → Trust certificate validation failed. May occur after certificate renewal on one device but not the other.
TMSH STATUS COMMANDS:
show cm sync-status → Shows current sync state:
- "In Sync" (green) → Both devices have identical config
- "Changes Pending" (yellow) → Config changed, needs sync
- "Awaiting Initial Sync" (yellow) → Group created but never synced
- "Disconnected" (red) → Cannot reach peer for sync
- "Not All Devices Synced" (red) → Sync failed on one or more devices
show sys failover → Shows:
- "active" → Device is processing traffic
- "standby" → Device is waiting (traffic groups on peer)
- "offline" → Device is forced offline or in error state
show cm device-group → Shows device group members, sync status, and failover status per group.
show cm traffic-group → Shows which device is active for each traffic group. Critical for active/active troubleshooting.
TROUBLESHOOTING WORKFLOW:
1. Check sync status: show cm sync-status → identify the state
2. Check failover: show sys failover → active/standby/offline
3. Check logs: tail -f /var/log/ltm | grep -iE 'failover|sync|trust' → find the cause
4. Check ports: verify TCP 4353 and UDP 1026 are open (port lockdown)
5. Check NTP: ntpq -p → verify time is synchronized (clock skew breaks trust)
6. Check certs: show sys device-certificate → verify expiration date
COMMON STUDENT MISTAKES
- Not checking logs when sync fails — the error message usually tells you exactly what's wrong
- Forgetting that certificate expiration breaks ALL HA communication (not just trust)
- Not understanding "Changes Pending" — it requires manual sync action, it doesn't auto-sync
- Assuming "Disconnected" means the peer is down — it might be a port lockdown or VLAN issue
F5 DOCUMENTATION: K13946, K75975904 (failover troubleshooting), K95002127 (failover events), K13295 (sync troubleshooting)
EXAM QUESTION PATTERNS
- "Config sync status shows 'Disconnected'. What do you check?" → TCP 4353, HA VLAN, port lockdown, device trust
- "Log shows 'no longer hearing from device'. Cause?" → Network failover heartbeat lost (UDP 1026)
- "Device trust cert expired. Impact?" → All HA fails — no sync, no failover, no mirroring

## Slide 94
94 © 2026 F5
Lab 10 — Hands-on exercises
45 minutes | Lab guide: Module 10
# | Activity | Key tasks | Time
1 | Building a DSC | Prep both devices. Configure ConfigSync/Failover/Mirror addresses. Build trust. Create Sync-Failover group. Resolve avr dependency. Initial sync. | 20m
2 | Failover + Mirroring | Make server gateway (10.1.20.240) floating. Test failover. Enable persistence mirroring. Verify records replicate. Failover → confirm persistence survives. | 15m
3 | Traffic Groups | Create tg-2. Move www_vs virtual address to tg-2. Force to standby → active/active. Fix broken FTP by moving SNAT to tg-2. | 10m
Activity 1: Initial sync fails on avr_virtual2 dependency. Remove iRule from avr_virtual1, sync, re-add. Teaches: config sync validates object dependencies.
Activity 2: Server gateway 10.1.20.240 must float (traffic-group-1). Without it, server responses go to wrong BIG-IP after failover.
Activity 3: All objects for one app SAME traffic group. Moving VIP to tg-2 without SNAT breaks FTP. Move SNAT translation to tg-2 to fix.
Notes: WHAT THIS SLIDE TEACHES
Lab launch. Three activities.
F5 DOCUMENTATION: K13946, K14592, K13639

## Slide 95
95 © 2026 F5
Exam checkpoints
Q1
What is the difference between a traffic group and an HA group? Which one TRIGGERS failover?
Q2
You configure two unicast failover addresses. One becomes unreachable but the peer is still alive. Does failover occur? Why?
Q3
show cm sync-status reports 'Disconnected'. /var/log/ltm shows 'config sync failed'. What do you check first?
Q4
The log shows 'device trust certificate expired'. What is the impact, and how do you fix it?
Q5
You move www_vs virtual address to tg-2 and force tg-2 to standby. FTP through the same VIP breaks. Why?
TG = what moves during failover. HA group = when to fail over (health score). Unicast: ANY failure = failover. Logs: /var/log/ltm. Commands: show cm sync-status, show sys failover, show cm traffic-group.
Notes: WHAT THIS SLIDE TEACHES
Five checkpoints targeting all three objectives with the patched gaps.
Q1 (4.02): Traffic group = container for floating objects (VIPs, self IPs, SNATs). Determines WHICH device is active for specific traffic. HA group = health scoring mechanism. Calculates a score from pool/trunk/VLAN health. If active device's score drops below standby → failover. The HA GROUP triggers failover. Traffic groups are MOVED by failover but don't cause it.
Q2 (4.11): YES, failover occurs. Multiple unicast addresses: ANY failure triggers failover. This is intentional — aggressive detection. If one of two addresses becomes unreachable, the device assumes the peer is degraded even if the other address still works. This prevents split-brain scenarios where partial connectivity causes both devices to think they should be active.
Q3 (4.12): "Disconnected" + "config sync failed" = the devices cannot communicate for sync. Check in order:
1. TCP 4353 (ConfigSync port) — is it open? Check port lockdown on HA self IP.
2. HA VLAN — is the link up? Check interface status.
3. Device trust — is it established? Check Device Trust > Peer Authorities.
4. NTP — are clocks synced? Clock skew can cause certificate validation failures.
Q4 (4.12): Impact: ALL HA communication fails. No config sync, no failover detection, no mirroring. The devices operate independently — they cannot synchronize or fail over. Fix: On EACH device: System > Device Certificates > Renew (set lifetime 3650 days). Then reset device trust: Device Trust > Local Domain > Reset Device Trust > Generate New Self-Signed Authority. Rebuild trust.
Q5 (4.02): FTP SNAT translation address is still in tg-1 (active on bigip01). www_vs VIP moved to tg-2 (active on bigip02). Client connects to VIP on bigip02, but FTP needs the SNAT address which is on bigip01 → asymmetric routing breaks FTP. Fix: move SNAT translation to tg-2.
F5 DOCUMENTATION: K14592, K16427, K13946, K13295, K75975904

## Slide 96
96 © 2026 F5
DSC TMSH reference
Task | Command
ConfigSync address | modify cm device bigip01 configsync-ip 10.1.30.245
Failover unicast | modify cm device bigip01 unicast-address { { ip 10.1.30.245 port 1026 } }
Mirror address | modify cm device bigip01 mirror-ip 10.1.30.245
Build trust | modify cm trust-domain Root add-device { device-ip 10.1.1.246 device-name bigip02 username admin password [pw] }
Create device group | create cm device-group my_dg type sync-failover devices add { bigip01 bigip02 } network-failover enabled
Sync to group | run cm config-sync to-group my_device_group
Force failover | run sys failover standby
Check sync status | show cm sync-status
Check failover status | show sys failover
Check traffic groups | show cm traffic-group
Check device groups | show cm device-group
Move VIP to TG | modify ltm virtual-address 10.1.10.100 traffic-group traffic-group-2
View HA logs | tail -f /var/log/ltm ¦ grep -iE 'failover¦sync¦trust¦HA'
HA ports: TCP 4353 (ConfigSync) + UDP 1026 (failover) + TCP 1028 (mirroring) + TCP 6699 (MCP). All opened by Allow Defaults.
Notes: WHAT THIS SLIDE TEACHES
Complete TMSH reference with added troubleshooting commands (show cm sync-status, show cm traffic-group, show cm device-group, log grep).
F5 DOCUMENTATION: K13946, K14592, K13639, K16427

## Slide 97
F5CTSLTM4.07 | U/A | Describe benefits of custom alerting (OIDs, log levels, triggers)
F5CTSLTM4.08 | R | Set up custom alerting: SNMP, email, Remote Syslog, config files, log levels
F5CTSLTM4.09 | U/A | Identify appropriate command for LTM device problem (logs, stats, files)
F5CTSLTM1.06 | U/A | Interpret log file messages to identify LTM device issues
LAB 11
Security and Logging
Audit logging, SSH access control, High Speed Logging (HSL)
to remote syslog, custom SNMP alerting, log file analysis,
and troubleshooting commands.
45 min | 15 min slides + 30 min lab
Notes: WHAT THIS SLIDE TEACHES
Opener for Lab 11. Four Beta objectives covering logging, alerting, and troubleshooting. 301a: 2.12.
F5 DOCUMENTATION: K16197 (logging), K13080 (HSL), K3667 (custom alerts), K15106 (log files)

## Slide 98
98 © 2026 F5
BIG-IP log files and severity levels
Know which log file to check for each type of problem
Log file | Path | Contains | Check when
ltm | /var/log/ltm | LTM-specific: VS, pool, monitor, SSL, HA, failover events | Traffic issues, pool member down, SSL errors, failover
audit | /var/log/audit | Admin actions: config changes, logins, GUI/TMSH commands | Who changed what, unauthorized access attempts
daemon | /var/log/daemon.log | System daemons: mcpd, tmm, named, ntpd, snmpd | TMM crashes, daemon failures, NTP/DNS issues
boot | /var/log/boot.log | Boot sequence, provisioning, license loading | Boot failures, license problems, provisioning errors
kern | /var/log/kern.log | Kernel messages: hardware, drivers, interfaces | Interface failures, hardware errors, memory issues
Syslog severity levels (0–7)
Level | Name | Meaning | Action
0 | Emergency | System unusable | Immediate action required
1 | Alert | Immediate action needed | Fix immediately
2 | Critical | Critical conditions | Investigate now
3 | Error | Error conditions | Investigate soon
4 | Warning | Warning conditions | Review and monitor
5 | Notice | Normal but significant | Normal operations
6 | Informational | Informational messages | Verbose logging
7 | Debug | Debug-level messages | NEVER in production — fills disk, drops messages
Notes: WHAT THIS SLIDE TEACHES
Log files and severity levels. F5CTSLTM4.09: "Determine the appropriate log file to examine" and F5CTSLTM4.08: "Identify the available levels for local traffic logging."
KEY EXAM POINTS: /var/log/ltm is the primary log for LTM issues. Audit log tracks admin changes. Debug level (7) should NEVER be used in production — it generates enormous volumes that can fill disk and cause the BIG-IP to drop log messages.
F5 DOCUMENTATION: K15106 (log files), K16197 (logging overview)

## Slide 99
99 © 2026 F5
Audit logging and SSH access control
Track administrative changes and restrict CLI access to trusted networks
Audit logging
Purpose: Log all config changes by all users.
Enable: System > Logs > Configuration >
Audit Logging: Enable
View: System > Logs > Audit
Or: /var/log/audit
Logged events:
• User logins / logouts
• Config changes (VS, pool, profile, etc.)
• TMSH commands executed
• Who made the change + timestamp
SSH IP Allow
Purpose: Restrict which IPs can SSH to the BIG-IP management interface.
Configure: System > Platform > SSH IP Allow
Options:
• All Addresses (default — insecure)
• Specify Range: 10.1.1.0/24
• None (disables SSH entirely)
TMSH:
modify sys sshd
allow replace-all-with
{ 10.1.1.0/24 }
Also restrict GUI access: System > Platform > HTTPD Access: Specify Range (same concept as SSH IP Allow). TMSH: modify sys httpd allow replace-all-with { 10.1.1.0/24 }
Security hardening checklist
✔ Enable audit logging ✔ Restrict SSH to management subnet ✔ Restrict HTTPD to management subnet ✔ Port lockdown None on data VLANs ✔ Disable unused services ✔ Change default passwords ✔ Renew device certificates ✔ Configure NTP
Notes: WHAT THIS SLIDE TEACHES
Audit logging and SSH/HTTPD access control. Addresses 301a 2.12: "Determine appropriate LTM device security configuration."
KEY EXAM POINTS: Audit logging disabled by default. SSH IP Allow on System > Platform. Existing SSH sessions survive restriction changes. Both SSH and HTTPD access can be restricted independently.
F5 DOCUMENTATION: K16197, K13092 (SSH access), K15283 (HTTPD access)

## Slide 100
100 © 2026 F5
High Speed Logging (HSL) architecture
Three-step pipeline: Log Destination → Log Publisher → Log Filter/Profile
1 Log destination(s)
WHERE logs go. Create TWO destinations:
HSL destination: Pool of syslog servers + protocol (TCP/UDP).
Type: Remote High-Speed Log
Pool: logging_pool (10.1.20.252:514)
Formatted destination: Wraps HSL with format.
Type: Remote Syslog
Format: Syslog
Forward to: hsl_logging_dest
2 Log publisher
HOW logs are routed. Associates one or more destinations.
Name: logging_pub
Destinations:
• formatted_dest (remote syslog)
• local-syslog (keep local copy)
A publisher can send to multiple destinations simultaneously.
3 Log filter / profile
WHAT gets logged and at what level.
System filter (system events):
Source: mcpd
Severity: Informational
Publisher: logging_pub
LTM log profile (traffic events):
Attach to VS for request logging.
WARNING: Never log at Debug level to remote servers. It generates massive traffic, can overwhelm the syslog server, and causes the BIG-IP to drop log messages. Use Informational or Warning level in production.
Notes: WHAT THIS SLIDE TEACHES
HSL remote logging architecture. Addresses F5CTSLTM4.08: "List and describe custom alerts: SNMP, email and Remote Syslog" and "Identify the location of custom alert configuration files."
FULL TECHNICAL EXPLANATION
The HSL pipeline has three layers:
1. DESTINATIONS — where logs go:
a. HSL destination: Associates a POOL of syslog servers with a protocol. You create a pool with syslog server members (IP:port), then create an HSL destination that references the pool. The reason for the pool is to allow load balancing across multiple syslog servers and to use monitors for health checking.
b. Formatted destination: Wraps the HSL destination with a message format (Syslog, Splunk, ArcSight, etc.). This ensures messages arrive in the correct format for the receiving system.
2. PUBLISHER — how logs are routed:
A publisher groups one or more destinations. A single publisher can send logs to both remote syslog AND local files simultaneously. This is the component you attach to filters and profiles.
3. FILTER/PROFILE — what gets logged:
a. System Log Filter: Controls system-level events (mcpd, tmm, etc.). Configured under System > Logs > Configuration > Log Filters.
b. LTM Log Profile: Controls traffic-level events (requests, responses). Attached to individual virtual servers.
LAB EXERCISE:
1. Create pool: logging_pool with member 10.1.20.252:514 and syslog_inband + syslog_active monitors
2. Create HSL destination: hsl_logging_dest → type Remote High-Speed Log → pool logging_pool
3. Create formatted destination: formatted_dest → type Remote Syslog → format Syslog → forward to hsl_logging_dest
4. Create publisher: logging_pub → destinations: formatted_dest + local-syslog
5. Create filter: my-mcpd-filter → source mcpd → severity Informational → publisher logging_pub
6. Test: disable a pool member → check syslog server for the event
F5 DOCUMENTATION: K13080 (HSL), K16197 (logging overview)

## Slide 101
101 © 2026 F5
Custom alerting configuration
Three alert types with full configuration examples. Custom alerts go in /config/user_alert.conf (survives upgrades).
SNMP trap alert
Setup SNMP destination:
System > SNMP > Traps > Destination
Add NMS server IP + community string.
# /config/user_alert.conf
alert BIGIP_CUSTOM_POOL_DOWN {
snmptrap OID="\
.1.3.6.1.4.1.3375.2.4.0.99"
match "Pool .* now has\
no available members"
}
Email alert
Setup SMTP first:
System > Configuration > Device > SMTP
SMTP server, from address, auth.
# /config/user_alert.conf
alert BIGIP_CUSTOM_SSL_EXPIRE {
email toaddress="ops@co.com"
fromaddress="bigip@co.com"
body="SSL cert expiring"
match "certificate.*expir"
}
SNMP + syslog combined
One alert can trigger multiple actions
Send trap to NMS AND log to syslog simultaneously.
# /config/user_alert.conf
alert BIGIP_CUSTOM_FAILOVER {
snmptrap OID="\
.1.3.6.1.4.1.3375.2.4.0.100"
match "ACTIVE for\
traffic group"
}
Alert configuration files
File | Purpose | Edit? | Survives upgrade?
/config/user_alert.conf | YOUR custom alerts. SNMP traps, email, or both. | ✔ Edit this file | ✔ Yes (in UCS)
/etc/alertd/alert.conf | Default system alerts. Contains built-in alert definitions. | ✘ DO NOT edit | ✘ Overwritten
Testing custom alerts
1. Add alert definition to /config/user_alert.conf
2. Restart alertd: bigstart restart alertd
3. Generate a matching log message: logger -p local0.notice "Pool my_pool now has no available members"
4. Verify: SNMP trap received at NMS, email sent, or syslog entry created.
Notes: WHAT THIS SLIDE TEACHES
Full custom alerting configuration with three working examples. F5CTSLTM4.07 and 4.08.
FULL TECHNICAL EXPLANATION
ALERT DEFINITION FORMAT:
alert ALERT_NAME {
snmptrap OID=".1.3.6.1.4.1.3375.2.4.0.XX" (SNMP trap action)
email toaddress="ops@company.com" fromaddress="bigip@company.com" body="message" (email action)
match "regex pattern to match in log messages"
}
The alert daemon (alertd) monitors /var/log/ltm and other logs. When a log message matches the "match" pattern, the alert fires. Multiple actions can be defined in one alert.
OID FORMAT:
.1.3.6.1.4.1.3375 = F5 enterprise OID space
.2.4.0 = alert subtree
.XX = your custom alert number (use 99+ to avoid conflicts with defaults)
EMAIL SETUP PREREQUISITE:
Before email alerts work, you must configure SMTP:
System > Configuration > Device > SMTP
Or TMSH: modify sys smtp server smtp.company.com from-address bigip@company.com
SNMP TRAP DESTINATION:
System > SNMP > Traps > Destination
Add the NMS server IP, port 162, community string.
TMSH: modify sys snmp traps add { my_trap { host 10.1.1.100 community public } }
TESTING WORKFLOW:
1. Edit /config/user_alert.conf and add your alert definition
2. Restart alertd so it reads the new config: bigstart restart alertd
3. Generate a test log message that matches your pattern: logger -p local0.notice "Pool my_pool now has no available members"
4. Verify the alert fired by checking your NMS (SNMP trap), email inbox, or syslog server
COMMON STUDENT MISTAKES
- Editing /etc/alertd/alert.conf instead of /config/user_alert.conf → changes lost on upgrade
- Forgetting to restart alertd after editing user_alert.conf
- Using OIDs that conflict with built-in F5 alerts
- Not configuring SMTP before trying email alerts
F5 DOCUMENTATION: K3667, K6305, K13383

## Slide 102
102 © 2026 F5
Sample log analysis
Practice identifying LTM device issues from real /var/log/ltm messages
Jan 15 09:23:41 bigip01 mcpd[6543]: 01070638:5: Pool /Common/www_pool member /Common/10.1.20.11:80 monitor status down.
Issue: Pool member marked DOWN by health monitor
Fix: Check member health. Verify monitor settings (interval, timeout). Test connectivity: curl http://10.1.20.11:80
Jan 15 09:24:02 bigip01 tmm[11235]: 01260009:3: Connection error: ssl_hs_rxhello:6281: unsupported version (0301)
Issue: SSL handshake failed: client offered TLS 1.0 (0x0301) which is disabled
Fix: Client needs TLS 1.2+, or enable TLS 1.0 on Client-SSL (not recommended). Check cipher string.
Jan 15 09:25:17 bigip01 tmm[11235]: 01010251:7: 01010251:7: Virtual /Common/www_vs has no usable listeners
Issue: Virtual server has no available pool members or the VS itself is misconfigured
Fix: Check pool member status. Verify VS destination IP and port. Check if pool is assigned to VS.
Jan 15 09:30:44 bigip01 sod[4521]: 01140029:5: HA daemon_heartbeat for device /Common/bigip02 no longer hearing heartbeat.
Issue: Network failover heartbeat lost from peer device
Fix: Check HA VLAN link status. Verify port lockdown (UDP 1026). Check peer device status. Check cables.
Jan 15 09:31:02 bigip01 mcpd[6543]: 01071431:4: Config sync: device-group /Common/my_device_group: connected device bigip02 is not in sync.
Issue: Configuration out of sync between HA peers (Changes Pending)
Fix: Run config sync: Device Mgmt > Overview > Sync Device to Group. Check for dependency errors.
Log format: timestamp hostname daemon[pid]: errorcode:severity: message. Severity 5=notice, 4=warning, 3=error, 7=debug
Notes: WHAT THIS SLIDE TEACHES
Practice slide for F5CTSLTM1.06: "Interpret log file messages to identify LTM device issues" and F5CTSLTM4.09: "Identify platform problems based on log file messages and statistics."
FULL TECHNICAL EXPLANATION
LOG FORMAT BREAKDOWN:
Jan 15 09:23:41 bigip01 mcpd[6543]: 01070638:5: Pool /Common/www_pool member...
| timestamp | hostname | daemon[pid] | error_code:severity | message
- timestamp: When the event occurred
- hostname: Which BIG-IP generated the message
- daemon: Which process logged it (mcpd, tmm, sod, etc.)
- error_code: F5-specific error identifier (searchable on my.f5.com)
- severity: Syslog level (0-7). :5: = Notice, :4: = Warning, :3: = Error
- message: Human-readable description
SAMPLE 1: POOL MEMBER DOWN (01070638:5)
- mcpd detected that the health monitor for 10.1.20.11:80 failed
- The member is marked DOWN and removed from LB rotation
- Error code 01070638 is searchable: https://my.f5.com/manage/s/article/K01070638
- Action: Check if the server is actually down, check monitor settings, test manually
SAMPLE 2: SSL HANDSHAKE FAILURE (01260009:3)
- TMM received a ClientHello with TLS version 0x0301 (TLS 1.0)
- The Client-SSL profile has TLS 1.0 disabled (security hardening)
- Severity :3: = Error
- Action: Update client to TLS 1.2+, or (not recommended) enable TLS 1.0
SAMPLE 3: VIRTUAL SERVER NO LISTENERS (01010251:7)
- The VS has no usable pool members — could be all members down, no pool assigned, or VS misconfigured
- Severity :7: = Debug (this is an informational debug message)
- Action: Check pool health, verify VS configuration
SAMPLE 4: HA HEARTBEAT LOST (01140029:5)
- The SOD (Service Oversight Daemon) has lost the network failover heartbeat from bigip02
- This will trigger failover if the heartbeat isn't restored
- Action: Check HA VLAN, port lockdown, cables, peer status
SAMPLE 5: CONFIG OUT OF SYNC (01071431:4)
- Configuration has been changed on one device but not synced to the group
- Severity :4: = Warning
- Action: Initiate config sync from the correct device
TEACHING APPROACH:
Show these log messages one at a time and ask students:
1. Which daemon generated this? (mcpd, tmm, sod)
2. What is the severity level? (notice, warning, error, debug)
3. What is the issue?
4. What is the fix?
F5 DOCUMENTATION: K15106 (log files), K16197 (logging overview)

## Slide 103
103 © 2026 F5
Lab 11 — Hands-on exercises
30 minutes | Lab guide: Module 11
# | Activity | Key tasks | Time
1 | Security Features | Enable audit logging. Make change as adminuser. Review audit log. Restrict SSH to 10.1.10.0/24, then 10.1.1.0/24. Test SSH access from both networks. | 10m
2 | Remote Logging | Create logging_pool (10.1.20.252:514, inband+active monitors). Create HSL dest → formatted dest → publisher → mcpd filter. Disable pool member → verify on syslog server. | 20m
Activity 2 monitor trick: Inband monitor uses actual traffic to check syslog health (no extra probe traffic). Active monitor polls every 180s as backup. Together they reduce noise while ensuring fast recovery.
Notes: WHAT THIS SLIDE TEACHES
Lab launch for security and logging exercises.
F5 DOCUMENTATION: K16197, K13080, K13092

## Slide 104
104 © 2026 F5
Exam checkpoints
Q1
A pool member is marked down. Which log file do you check first, and what grep pattern do you use?
Q2
You need custom alerts to survive a BIG-IP software upgrade. Which config file do you edit, and which file must you NOT modify?
Q3
You want to send an SNMP trap when a specific pool has no available members. How do you configure this?
Q4
How many log destinations are needed for HSL remote syslog? Name them and explain why two are required.
Key facts
/var/log/ltm = LTM events. /var/log/audit = admin changes. Severity 0–7 (emerg→debug). Never debug in prod.
/config/user_alert.conf = custom alerts (survives upgrade). /etc/alertd/alert.conf = defaults (DO NOT EDIT).
HSL = 2 destinations (HSL + Formatted) → 1 publisher → filter/profile.
Notes: WHAT THIS SLIDE TEACHES
Q1: /var/log/ltm. Command: grep -i "pool_name" /var/log/ltm or tail -f /var/log/ltm | grep pool. This log contains all LTM events including monitor failures, member status changes, and SSL errors.
Q2: Edit /config/user_alert.conf — this file is included in UCS archives and survives upgrades. DO NOT edit /etc/alertd/alert.conf — it's overwritten during upgrades. If you need to customize a default alert, copy the definition to user_alert.conf and modify it there.
Q3: Add a custom alert to /config/user_alert.conf that matches the "no available members" log pattern and triggers an SNMP trap with a custom OID. Example in slide 5.
Q4: Two destinations are required: (1) HSL destination — specifies the pool of syslog servers and the transport protocol (TCP/UDP). (2) Formatted destination — wraps the HSL destination with a message format (Syslog, Splunk, etc.). The reason for two is separation of concerns: the pool/protocol definition is separate from the formatting definition. Both feed into a publisher.
F5 DOCUMENTATION: K15106, K3667, K13080

## Slide 105
105 © 2026 F5
Logging and security reference
Task | Command / Path
View LTM log | tail -f /var/log/ltm ¦ grep -i 'pattern'
View audit log | tail -f /var/log/audit ¦ grep 'username'
Enable audit logging | modify sys db audit.forward.destination value enable
Restrict SSH access | modify sys sshd allow replace-all-with { 10.1.1.0/24 }
Restrict GUI access | modify sys httpd allow replace-all-with { 10.1.1.0/24 }; save sys config
Create HSL destination | create sys log-config destination remote-high-speed-log hsl_dest pool-name logging_pool
Create formatted dest | create sys log-config destination remote-syslog fmt_dest format rfc5424 remote-high-speed-log hsl_dest
Create publisher | create sys log-config publisher logging_pub destinations add { fmt_dest local-syslog }
Create log filter | create sys log-config filter my_filter source mcpd level informational publisher logging_pub
Test custom alert | logger -p local0.notice 'Pool my_pool now has no available members'
Generate qkview | qkview (generates /var/tmp/hostname.qkview for F5 Support)
Troubleshooting order: 1) Check /var/log/ltm (LTM events) 2) Check /var/log/daemon.log (system daemons) 3) show sys performance 4) show sys tmm-info 5) qkview for F5 Support
Notes: WHAT THIS SLIDE TEACHES
Complete reference for logging, alerting, and security commands.
F5 DOCUMENTATION: K15106, K16197, K13080, K3667, K13092

## Slide 106
F5CTSLTM1.02 | U/A | Deployment topologies (one arm, two arm, nPath/DSR, auto last-hop)
F5CTSLTM5.01–5.04 | U/A, A/E | HTTP packet capture analysis (response codes, headers, tcpdump)
F5CTSLTM4.01, 4.06 | U/A | Software upgrades (HA rolling upgrade, boot locations)
F5CTSLTM4.04, 4.05 | U/A | Backup/restore (UCS vs SCF, GUI archives)
F5CTSLTM4.10 | A/E | Performance analysis (CPU/memory, host OS vs TMOS)
F5CTSLTM2.11 | A/E | Simplify LTM config (iRules → policies, consolidate VS)
F5CTSLTM2.12 | U/A | Device statistics, config cleanup, remove unused objects
F5CTSLTM3.02 | R | Application templates (iApp and FAST)
GAP-FILL SLIDE BLOCK
Objectives Not Covered
by Labs 1–11
These 9 objectives span 4 of the 6 Beta exams. They are covered here
as instructor-led slides with full speaker notes — no lab exercises.
All technical claims sourced from F5 documentation.
Notes: WHAT THIS SLIDE TEACHES Opener for the gap-fill slide block. Lists all 9 objectives not covered by Labs 1–11. These objectives were identified by a full gap analysis against the Beta blueprint. They span Exams 1-B (topologies), 2-B (simplify config, statistics), 3-B (templates), 4-B (upgrades, backup, performance), and 5-B (HTTP analysis). DELIVERY NOTE: This section is slides-only (no lab exercises). Instructor should present each slide and use the speaker notes for discussion. Exam checkpoint questions are embedded in the speaker notes.

## Slide 107
107 © 2026 F5
Deployment topologies
F5CTSLTM1.02 (U/A) — One arm, two arm, nPath/DSR, and auto last-hop
Topology | How traffic flows | SNAT required? | L7 features? | Use case
Two-arm (routed) | Client → BIG-IP (ext VLAN) → server (int VLAN). Server default gw = BIG-IP floating self IP. | No — if servers gw through BIG-IP. Yes — if servers use another gw. | ✔ Full proxy | Standard DC. Most common.
One-arm | Client and servers on SAME VLAN/subnet. BIG-IP has one interface. | YES — always. Without SNAT, server responds directly to client bypassing BIG-IP. | ✔ Full proxy | Simple. No network redesign.
nPath / DSR | Client → BIG-IP → server. Server responds DIRECTLY to client (bypasses BIG-IP). Loopback VIP on server. | No — server sees real client IP. BIG-IP inbound only. | ✘ No L7 Packet-based | Max throughput. Asymmetric. Video.
Auto last-hop
What it does: BIG-IP remembers the MAC of the device that sent each inbound connection. Responses return through the SAME device regardless of the routing table. Why it matters: Asymmetric routing (multiple routers/paths) — without auto last-hop, responses take different routes and stateful firewalls drop them. Default: enabled. TMSH: modify ltm global-settings traffic-control auto-lasthop enabled
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM1.02: Deployment topologies. nPath/DSR: server loopback VIP, no L7, max throughput. One-arm: SNAT always required. Auto last-hop: MAC-based return path. Default enabled. F5 DOCUMENTATION: K4707, K7820, K13167

## Slide 108
108 © 2026 F5
HTTP response codes
F5CTSLTM5.01 (U/A) — Interpret response codes to determine the root cause of an application problem
Code | Name | What it means | BIG-IP investigation
200 | OK | Request succeeded. Normal response. | No issue. Baseline for comparison.
301 | Moved Permanently | Resource permanently at new URL. | Check iRules (HTTP::redirect). Server vs BIG-IP redirect?
302 | Found (Temp Redirect) | Temporary redirect to different URL. | Common in HTTP → HTTPS redirects. Check redirect iRule/policy.
400 | Bad Request | Malformed request from client. | Check HTTP profile max header size. Oversized cookies?
403 | Forbidden | Server understood but refuses. | Server ACLs, iRule deny, ASM block? Check both sides.
404 | Not Found | Requested URI doesn't exist on server. | Wrong pool? Content switching sending to wrong pool/member?
500 | Internal Server Error | Server-side application crash. | Not BIG-IP. Check server logs. Capture server-side response.
502 | Bad Gateway | BIG-IP got invalid response from server. | Server sent malformed HTTP. Capture server-side pcap. Check health.
503 | Service Unavailable | Service temporarily unavailable. | All pool members down? Check pool status. Sorry page configured?
Troubleshooting tip: Capture BOTH client-side and server-side tcpdump simultaneously. Compare response codes — if client sees 502 but server sent 200, BIG-IP may be mangling the response (HTTP profile, compression, iRule). If both show 500, the problem is the server.
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM5.01: HTTP response codes. Students must map codes to BIG-IP investigation steps. KEY PATTERNS: - 4xx = client-side problem (bad request, auth, not found) - 5xx = server-side problem (500/502/503) - 502 = BIG-IP acting as gateway got bad response FROM server - 503 = often means all pool members down on BIG-IP F5 DOCUMENTATION: K57474155

## Slide 109
109 © 2026 F5
Key HTTP headers for BIG-IP
F5CTSLTM5.01 (U/A) — Headers that affect BIG-IP traffic processing and troubleshooting
Header | Direction | What it does on the BIG-IP | Exam relevance
Host | Request | Content switching via LTM policy or iRule. Route to different pools based on hostname. | Policy condition: HTTP Host header matches
Cookie | Both | Cookie persistence. BIG-IP inserts persistence cookie (BIGipServer...) on response. Client sends it back on next request. | Persistence troubleshooting. Cookie name = BIGipServer<pool>
X-Forwarded-For | Request | BIG-IP inserts original client IP when SNAT is used. Server sees real client. Enabled in HTTP profile: Insert XFF. | Without XFF + SNAT, server only sees BIG-IP self IP
Content-Type | Response | Determines HTTP compression eligibility. text/html = compressed. image/jpeg = not compressed. Controlled by content list. | Compression profile: Content Type Include/Exclude
Cache-Control | Response | Controls BIG-IP RAM cache behavior. no-cache / no-store / max-age directives determine what gets cached. | Web acceleration profile cache settings
Vary | Response | Cache key variation. Vary: Accept-Encoding = separate cache entries for gzip vs identity. Prevents serving wrong encoding. | RAM cache stores per Vary value
Connection | Both | Keep-Alive vs Close. Affects OneConnect reuse. OneConnect allows server-side connection pooling across clients. | OneConnect + Keep-Alive = connection multiplexing
tcpdump for HTTP analysis
# Client-side: see original request headers from client
tcpdump -nni client_vlan -s0 -A host 10.1.10.100 and port 80
# Server-side: see what BIG-IP sends to pool member (XFF inserted, cookies modified)
tcpdump -nni server_vlan -s0 -A host 10.1.20.11 and port 80
# Both sides with SNAT/OneConnect: server-side source IP = BIG-IP self IP, not client
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM5.01-5.04: HTTP headers and their role on BIG-IP, plus tcpdump for HTTP analysis. KEY EXAM POINTS: - SNAT + OneConnect in pcap: server-side source = BIG-IP self IP. Multiple client requests may share one server connection. - XFF: only inserted if HTTP profile has Insert XFF enabled. Without it, server sees BIG-IP IP. - Cookie persistence cookie name: BIGipServer<pool_name>. Encoded with member IP and port. F5 DOCUMENTATION: K4707, K411

## Slide 110
110 © 2026 F5
Software upgrades
F5CTSLTM4.01, 4.06 (U/A) — Upgrade while maintaining application availability
HA rolling upgrade (zero downtime)
1
Pre-checks
Verify HA In Sync. UCS on BOTH devices. Verify disk space. Read release notes.
2
Upgrade standby
Upload ISO to standby. Install to unused boot location. Reboot standby into new version. Verify rejoins cluster.
3
Force failover
Force active to standby. Traffic moves to upgraded device. Verify apps on new version.
4
Upgrade former active
Install ISO on original active (now standby). Reboot into new version. Verify rejoins.
5
Verify and sync
Both on new version. Sync config. Test failover both ways. Verify all applications.
# Show boot locations (HD1.1, HD1.2, HD1.3)
show sys software status
# Install ISO to inactive boot location
install sys software image BIGIP-16.1.4-0.0.3.iso volume HD1.2
# Reboot into new boot location (rollback: reboot volume HD1.1)
reboot volume HD1.2
# GUI: System > Software Management > Image List > Install / Boot Locations > Activate
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM4.01/4.06: Software upgrades. HA rolling upgrade = zero downtime. Boot locations for rollback. F5 DOCUMENTATION: K13845, K34745165

## Slide 111
111 © 2026 F5
Backup and restore
F5CTSLTM4.04, 4.05 (U/A) — UCS vs SCF, and the GUI archive interface
 | UCS (User Configuration Set) | SCF (Single Configuration File)
Contains | FULL: config, SSL certs/keys, license, users, custom alerts | TEXT only: bigip.conf, bigip_base.conf. No certs/license.
Format | .ucs (compressed tar). Passphrase encryption optional. | .scf (human-readable text). No encryption.
Restore to | Same platform/version only. NOT cross-platform. | Any platform. Config migration across hardware.
Use case | Pre-upgrade backup, disaster recovery, same-model replacement | Config migration, audit/review, partial restore
GUI: System > Archives
Create archive: System > Archives > Create > enter name + optional passphrase > Finished Restore archive: System > Archives > select archive > Restore WARNING: Overwrites entire configuration Download / Upload: Select archive > Download: .ucs file
Upload: restore from off-box backup
# Create UCS
save sys ucs /var/local/ucs/backup.ucs
# Create encrypted UCS
save sys ucs backup.ucs passphrase s3cret
# Restore UCS (OVERWRITES all config)
load sys ucs /var/local/ucs/backup.ucs
# Create / restore SCF
save sys config file my-config.scf
load sys config file my-config.scf
Always create a UCS BEFORE any upgrade or major change. UCS restore OVERWRITES the entire config. Store copies off-box for disaster recovery.
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM4.04/4.05: UCS vs SCF, GUI archive interface. GUI: System > Archives shows existing UCS files. Create: enter name, optional passphrase, click Finished. Download: select archive, click Download. Upload: allows restoring from downloaded file. Restore: select archive, click Restore. KEY: UCS stored at /var/local/ucs/. Passphrase encrypts SSL keys in the archive. Always store a copy off-box. F5 DOCUMENTATION: K13132, K13408

## Slide 112
112 © 2026 F5
Performance analysis
F5CTSLTM4.10 (A/E) — CPU, memory, throughput from GUI and TMSH
 | Host OS (Linux) | TMM (Traffic Microkernel)
Handles | Management: mcpd, httpd, sshd, named, ntpd, alertd | Traffic: SSL, compression, iRules, LB, monitors
Memory | Separate pool. Check: free -m or show sys host-info | Separate pool. Check: show sys tmm-info
CPU | Shared cores. Check: top, show sys cpu | Dedicated cores. Check: show sys tmm-info
High = | Config changes slow, GUI unresponsive, mcpd busy | Traffic overload, SSL bulk, complex iRules
GUI: Statistics > Performance Reports
GUI location | What it shows | Use when
Statistics > Performance Reports | Time-series graphs: CPU, memory, throughput, connections, SSL TPS | Trending, capacity planning, correlating spikes with events
System > Resource Provisioning | Module allocation: LTM, AVR, etc. Shows host-level resource usage. | Check if modules are competing for resources
Statistics > Module Stats > LT | VS/pool/member connection counts, bits in/out, current sessions | Identify unused VS, overloaded members, traffic distribution
System > Logs > Dashboard | Recent log messages, alerts, severity breakdown | Quick health check, recent errors at a glance
show sys performance all-stats # Single best overview: CPU, mem, throughput, connections
show sys tmm-info # Per-TMM CPU, memory, connection counts
show sys host-info # Host OS CPU and memory utilization
show sys connection count # Total active connections (spike = DDoS or leak)
grep -i 'memory\|exhausted' /var/log/ltm # Resource exhaustion warnings
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM4.10: Performance analysis. Host OS vs TMM separation. GUI performance reports. GUI LOCATIONS: - Statistics > Performance Reports: graphical CPU, memory, throughput over time - System > Resource Provisioning: shows allocated vs used resources per module - Statistics > Module Statistics > Local Traffic: VS/pool/member stats KEY EXAM POINTS: - TMM CPU 100% = traffic overload. Host CPU 100% = management overload. Different pools. - Connection count spike + high TMM CPU = possible DDoS - show sys performance all-stats is the single best starting command F5 DOCUMENTATION: K15468, K16419, K14813

## Slide 113
113 © 2026 F5
Simplify LTM configuration
F5CTSLTM2.11 (A/E) — Replace iRules with policies, consolidate virtual servers
Replace iRules with LTM policies
When to replace: • HTTP → HTTPS redirect • URI-based pool selection • Host header routing • Response code actions Why policies are better: • No TCL coding — GUI point-and-click
• Easier to audit and troubleshoot
• Lower CPU than complex iRules
• Version-controlled via GUI
Consolidate virtual servers
When to consolidate: • Multiple host-specific VS on same IP → one VS + LTM policy for routing • HTTP + HTTPS VS → one HTTPS VS with HTTP redirect policy • VS with identical profiles/settings Benefits: • Fewer objects to manage and sync
• Simpler troubleshooting
• Reduced config sync time
• Easier compliance audit
Example: Three iRules (HTTP redirect, Host routing, URI switching) replaced by ONE LTM policy with conditions (Host matches, URI starts with) and actions (forward to pool, redirect). Assign under VS Resources > Policies.
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM2.11: Simplify config. A/E level. F5 DOCUMENTATION: K14912, K14163

## Slide 114
114 © 2026 F5
Device statistics and config cleanup
F5CTSLTM2.12 (U/A) — Identify and remove redundant objects using statistics and tools
Find this | Where to look | What to check | Action
Unused VS | Statistics > Module Stats > LT show ltm virtual detail | 0 current connections over weeks. Bits In/Out flat at 0. | Confirm with app team. Disable → monitor → delete.
Orphaned pools | Local Traffic > Network Map shows pool-VS relationships | Pool not linked to any VS. No iRule references to it. | Verify no iRule uses pool. Delete if truly orphaned.
Excessive monitors | list ltm pool [name] monitor show ltm pool [name] members | Multiple monitors per pool. 5-second intervals on stable servers. | Reduce to one monitor. Increase interval (30-60s).
Unused profiles | list ltm virtual ¦ grep profile Compare against profile list. | Custom profiles not assigned to any virtual server. | Delete unused custom profiles. Keep defaults.
Duplicate iRules | list ltm rule ¦ diff Review iRule logic manually. | Two iRules doing same thing. Overlapping match conditions. | Consolidate into one. Or replace with LTM policy.
Stale nodes | show ltm node Compare against server inventory. | Nodes with no pool membership. Servers decommissioned months ago. | Remove from pools first. Then delete orphaned nodes.
# VS with zero traffic (show connection counts)
show ltm virtual | grep -A3 'Availability\|Cur Sessions\|Bits'
# Find orphaned pools not used by any VS
tmsh -q -c 'list ltm pool one-line' | while read p; do
name=$(echo $p | awk '{print $3}'); grep -q $name <<< "$(list ltm virtual)"; done
# Network Map (GUI): Local Traffic > Network Map > shows all VS-pool-member links
# Objects not linked are candidates for cleanup
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM2.12: Config cleanup with statistics. Network Map is the primary GUI tool for identifying orphaned objects. CLEANUP WORKFLOW: 1) Network Map identifies orphans. 2) Statistics identify unused. 3) Confirm with app team. 4) Disable first, monitor for complaints. 5) Delete after confirmation period. Removing functions: understand the impact. Removing a profile from a VS changes traffic behavior. Removing a pool member changes LB distribution. Always disable first. F5 DOCUMENTATION: K14163, K98133564

## Slide 115
115 © 2026 F5
iApp templates (legacy)
F5CTSLTM3.02 (R) — Deploy, modify, and identify objects created by iApp
What is an iApp? A wizard-driven template that deploys a complete application service: virtual server, pool, profiles, monitors, iRules — all created and grouped together. How it works: 1. Select a template (HTTP, HTTPS, Exchange, SharePoint, etc.) 2. Answer questions (IP, port, pool members, SSL cert, etc.) 3. iApp creates all LTM objects automatically 4. Objects grouped under: /Common/app_name.app/ Modifying iApp-deployed objects: • Default: Strict Updates = enabled. Objects are LOCKED.
• Must reconfigure through iApp wizard to make changes.
• Direct edits to objects are OVERWRITTEN on reconfigure.
• To allow direct edits: Properties > uncheck Strict Updates.
• WARNING: reconfigure reverts manual changes.
GUI and TMSH reference
Deploy: iApps > Application Services > Create View deployed: iApps > Application Services > Applications Templates: iApps > Templates (built-in + imported)
# List deployed iApps
list sys application service
# List objects in an iApp
list ltm virtual /Common/myapp.app/*
# Disable Strict Updates
modify sys application service
/Common/myapp.app/myapp
strict-updates disabled
Identifying iApp objects: All objects use the naming pattern /Common/app_name.app/object_name. In the GUI, they appear grouped under iApps > Application Services. In TMSH: list ltm virtual /Common/myapp.app/* shows all objects belonging to the iApp.
Strict Updates exam question: "You try to modify a pool created by an iApp but the settings are greyed out. Why?" Answer: Strict Updates is enabled (default). The iApp locks its objects. Reconfigure through the iApp wizard, or disable Strict Updates under Properties.
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM3.02: iApp templates. R (Remember) level. GUI LOCATION: iApps > Application Services > Applications (list of deployed apps) iApps > Templates (list of available templates) KEY EXAM POINTS: - iApp = wizard creates all objects. Grouped under .app container. - Strict Updates = default ON. Objects locked. Must edit through wizard. - Disable Strict Updates to allow direct object edits. - Object naming: /Common/app_name.app/vs_name F5 DOCUMENTATION: K15645

## Slide 116
116 © 2026 F5
FAST templates (modern)
F5CTSLTM3.02 (R) — The modern replacement for iApp using AS3 declarations
What is FAST? F5 Application Services Templates. A modern template engine that uses AS3 (Application Services 3) declarations to deploy LTM objects. Available on BIG-IP 14.1+. How it differs from iApp: • JSON schema templates (not TCL) • API-driven (REST API + GUI) • Uses AS3 declarations under the hood • Templates are versioned and shareable • No Strict Updates lock issue Modifying FAST-deployed objects: • Edit FAST template parameters in the GUI
• Or modify the AS3 declaration directly (API)
• Changes outside FAST/AS3 may be reverted
on next deployment
• Best practice: always modify through FAST
GUI and API reference
Deploy: iApps > Application Services > FAST > Deploy Select template > fill parameters > Deploy View deployed: iApps > Application Services > FAST > Applications API (REST): POST /mgmt/shared/fast/applications
# FAST uses AS3 declarations
# Example AS3 declaration (JSON):
{
"class": "AS3",
"declaration": {
"class": "ADC",
"myApp": {
"class": "Application",
"template": "http"
}
}
}
iApp vs FAST quick comparison
 | iApp (legacy) | FAST (modern)
Template language | TCL-based templates | JSON schema + AS3 declarations
Object locking | Strict Updates (locked by default) | Declaration-managed (no lock)
Status | Legacy — still supported, widely deployed | Current recommended approach
Notes: WHAT THIS SLIDE TEACHES F5CTSLTM3.02: FAST templates. R (Remember) level. GUI LOCATION: iApps > Application Services > FAST FAST vs iApp: - FAST = JSON + AS3. Modern. API-driven. No Strict Updates issue. - iApp = TCL. Legacy. Wizard-driven. Strict Updates locks objects. - Both create the same LTM objects (VS, pools, profiles, monitors). - FAST is the recommended approach for new deployments. F5 DOCUMENTATION: FAST on GitHub, AS3 documentation

## Slide 117
FINAL REVIEW
Exam Prep and
Course Summary
Six exams. 44 objectives. One certification.
This section maps every exam to the course content, reviews
the hardest topics, and gives you a strategy for exam day.
F5 Certified Technology Specialist, BIG-IP LTM (F5-CTS, LTM)
Notes: WHAT THIS SLIDE TEACHES
Final review section opener. Sets the stage for comprehensive exam prep across all six Beta exams.

## Slide 118
118 © 2026 F5
Exam coverage map
Every Beta exam mapped to course labs and gap-fill slides
Exam | Topic | # Obj | Covered by | Hardest objectives
F5CTSLTM1-B | Base Config + Networking | 6 | Labs 1, 8, 9, 11 + GF1 | 1.02 nPath/DSR, 1.06 log interpretation
F5CTSLTM2-B | VS + Local Traffic Objects | 14 | Labs 1, 2, 4, 6, 7 + GF2-3, 7-8 | 2.07 VS matching, 2.11 simplify config (A/E)
F5CTSLTM3-B | iRules, Analytics, Templates | 7 | Labs 2, 3 + GF9-10 | 3.05 iRule traffic result (A/E), 3.06 AVR
F5CTSLTM4-B | Upgrades, HA, Monitoring | 12 | Labs 9, 10, 11 + GF4-6 | 4.02 TG vs HA groups, 4.10 perf analysis (A/E)
F5CTSLTM5-B | Packet Capture — TCP/HTTP | 4 | GF2-3 + Labs throughout | 5.03/5.04 pcap root cause + solution (A/E)
F5CTSLTM6-B | Packet Capture — TLS/SSL | 4 | Lab 5 | 6.02/6.03 SSL pcap + config data (A/E)
TOTAL |  | 44 | All covered | 
Cognitive complexity breakdown
R (Remember) | U/A (Understand/Apply) | A/E (Analyze/Evaluate)
Recall facts, definitions, locations. • 3.02 iApp/FAST templates • 2.06 SNAT types • 4.08 Alert config files | Apply knowledge to scenarios. • Most objectives (30+) • "Given a scenario, determine..." • "Explain how to configure..." | Hardest — analyze data, evaluate options. • 2.10/2.11 Profile + config optimization • 4.10 Performance analysis • 5.03/5.04/6.02/6.03 Packet capture
Notes: WHAT THIS SLIDE TEACHES
Full course-to-exam mapping. Students can see exactly where each exam's content is covered.
GF = Gap-Fill slide block. GF1 = slide 1, GF2 = slide 2, etc.
A/E objectives are the hardest and require practice with real scenarios and packet captures. These are where most students fail.

## Slide 119
119 © 2026 F5
Exam strategy
Tips from F5 instructors for the Beta certification series
1
Read the scenario completely
Beta exam questions are scenario-based. The scenario contains clues. Read every word before looking at answers. The scenario setup is often more important than the question itself.
2
Eliminate wrong answers first
Most questions have one obviously wrong answer. Remove it. Then evaluate remaining options. If two answers seem correct, re-read the scenario for the distinguishing detail.
3
Know your TMSH
Many questions test TMSH command syntax. Know: show vs list (show = runtime stats, list = config). Know the key commands: show cm sync-status, show ltm virtual, show sys performance.
4
Packet captures: follow the flow
For tcpdump questions, trace the packet path: client → client VLAN → BIG-IP → server VLAN → server. Know what changes at each hop (source IP with SNAT, headers with profiles, encryption with SSL).
5
Log messages: read the error code
Error codes tell you the source: 01=TMM, 07=MCP, 0c=SOD, 26=SSL. The severity after the second colon: :3:=Error, :4:=Warning, :5:=Notice. This narrows the problem immediately.
6
HA questions: know the order
DSC build order: Prepare → Device settings → Trust → Group → Sync. Traffic groups hold floating objects. HA groups score health. Failsafe monitors VLANs/gateways. These are distinct mechanisms.
Time management: 6 exams, each ~60 min. Flag hard questions and come back. Don't spend 5 minutes on one question.
Notes: WHAT THIS SLIDE TEACHES
Exam strategy for the Beta series. Six practical tips covering reading comprehension, elimination, TMSH, packet captures, log analysis, and HA.
KEY POINT: show = runtime statistics/state. list = configuration. Students confuse these constantly.

## Slide 120
120 © 2026 F5
Comprehensive review — Exams 1–3
1
1-B
One-arm deployment. SNAT is not configured. Client connects to VIP. Server responds. What happens and why?
Server responds directly to client via L2 (same subnet), bypassing BIG-IP. Client rejects response — different source MAC. Fix: enable SNAT.
2
2-B
Two VS: 10.1.10.100:80 (Standard) and 10.1.10.100:* (Performance L4). Client sends to 10.1.10.100:80. Which VS processes?
10.1.10.100:80 (more specific destination port wins over wildcard). Specificity: addr:port > addr:* > net:port > net:*
3
2-B
Pool has Round Robin, cookie persistence, and a member is Force Offline. New client with no cookie arrives. What happens?
Force Offline: no new connections. Member skipped by LB. Existing persisted clients CAN still reach it. New client gets next available member via RR.
4
3-B
iRule has 'when HTTP_REQUEST' event but VS has no HTTP profile. What happens?
iRule never fires. HTTP_REQUEST requires the HTTP profile to parse Layer 7. Without it, BIG-IP treats traffic as L4 only. The event is ignored.
5
3-B
AVR shows server latency at 800ms but client latency at 200ms. Where is the bottleneck?
Server tier. Server latency (server response time) is 4x client latency. The server is slow to respond. Investigate server-side: database, application code, disk I/O.
Notes: WHAT THIS SLIDE TEACHES
Five review questions covering Exams 1-3 (networking, VS/LB, iRules/AVR). Each question includes the answer below for instructor-led discussion.
TEACHING APPROACH: Show the question, give students 30 seconds to think, then reveal the answer.

## Slide 121
121 © 2026 F5
Comprehensive review — Exams 4–6
6
4-B
You upgrade the standby device and reboot it. It comes up but does not rejoin the cluster. show cm sync-status shows 'Disconnected'. What do you check?
Device trust certificate may have been invalidated by the upgrade. Check: device trust (Peer Authorities), TCP 4353 open, NTP synced, matching provisioning. May need to reset trust.
7
4-B
HA group is configured. www_pool has 4 members (weight 100). Two members fail. Peer has all 4 up. Does failover occur?
Active score: (2/4)×100 = 50. Peer score: (4/4)×100 = 100. Peer higher → YES, failover. HA group triggers failover when active score drops below peer.
8
4-B
/config/user_alert.conf vs /etc/alertd/alert.conf — which survives upgrade? Which do you edit?
Edit /config/user_alert.conf (survives upgrade, in UCS). NEVER edit /etc/alertd/alert.conf (overwritten on upgrade). Restart alertd after editing.
9
5-B
Client-side tcpdump shows HTTP 200 OK. Server-side shows HTTP 503. Where is the disconnect?
BIG-IP is serving a cached response or sorry page to the client (200) while the actual server is returning 503 (unavailable). Check: RAM cache, sorry page iRule, fallback host.
10
6-B
SSL handshake fails. Client sends ClientHello with TLS 1.0. BIG-IP Client-SSL profile has Options: No TLSv1. What happens?
BIG-IP rejects the handshake — TLS 1.0 is disabled in the profile. Log shows 01260009:4 'unsupported version'. Fix: client must use TLS 1.2+, or enable TLSv1 in profile (not recommended).
Notes: WHAT THIS SLIDE TEACHES
Five review questions covering Exams 4-6 (HA/upgrades, TCP/HTTP pcap, SSL pcap).

## Slide 122
122 © 2026 F5
TMSH command cheat sheet
show = runtime state/stats. list = saved configuration. Know the difference.
Category | show (runtime) | list (config) | action
Virtual servers | show ltm virtual | list ltm virtual | create/modify/delete ltm virtual
Pools | show ltm pool [name] members | list ltm pool | modify ltm pool [name] members add/delete
Nodes | show ltm node | list ltm node | modify ltm node [ip] state user-down
Connections | show sys connection | — | delete sys connection all
Persistence | show ltm persistence persist-records | list ltm persistence | delete ltm persistence persist-records
HA sync | show cm sync-status | list cm device-group | run cm config-sync to-group [name]
Failover | show sys failover | list cm traffic-group | run sys failover standby
Performance | show sys performance all-stats | — | show sys tmm-info / show sys host-info
Software | show sys software status | — | install sys software image [iso] volume HD1.2
Archives | — | — | save sys ucs [name] / load sys ucs [name]
Users | — | list auth user | create/modify auth user [name]
Key patterns: save sys config (write to disk) | save sys ucs (full backup) | show sys (runtime) | list (config) | modify (change) | create/delete (add/remove). TMSH: cd /partition to switch context. 'exit' from tmsh = logoff for non-admin users.
Notes: WHAT THIS SLIDE TEACHES
TMSH command reference organized by category with show/list/action columns. Students must know show vs list.
show = live runtime data (connections, stats, status)
list = saved configuration (what's in bigip.conf)
This distinction appears on every exam.

## Slide 123
123 © 2026 F5
Key facts to memorize
Networking and Virtual Servers
• Port lockdown None = block all. Allow Defaults opens HA ports.
• HA ports: TCP 4353 (sync), UDP 1026 (failover), TCP 1028 (mirror), TCP 6699 (MCP)
• VS matching: addr:port > addr:* > net:port > net:* > *:port > *:*. Source tiebreaker.
• VS types: Standard (full proxy), Perf L4 (fast, limited), Forwarding IP (route), L2 (bridge)
• One-arm = SNAT always. nPath/DSR = no SNAT, no L7, server loopback VIP.
• Auto last-hop: returns via same device that sent the request. Default: enabled.
• SNAT automap: uses self IP. SNAT pool: dedicated IPs. 65535 ports per IP.
HA and Administration
• 8 roles: Admin > Res Admin > Manager > Cert Mgr > iRule Mgr > Operator > Guest > No Access
• Auth fallback: Rejected = denied. Unreachable = local fallback.
• Traffic groups: hold floating objects. HA groups: health scoring.
• Multiple unicast failover: ANY failure triggers failover.
• Mirroring only mirrors records created AFTER enablement.
• UCS = full backup (certs, license). SCF = text config only.
• Custom alerts: /config/user_alert.conf (survives upgrade).
• Device cert expires → ALL HA fails. Renew 3650 days.
Profiles and iRules
• HTTP profile required for: cookies, XFF, compression, caching, iRule HTTP events.
• Client-SSL = decrypt from client. Server-SSL = re-encrypt to server.
• OneConnect: server-side connection reuse. Requires HTTP profile.
• Force Offline: no new connections, existing persist clients allowed.
• Disable: no new connections at all. Active connections gracefully drain.
• LTM policy replaces simple iRules (redirects, routing). Lower CPU.
Logging and Troubleshooting
• /var/log/ltm = primary LTM log. /var/log/audit = admin changes.
• Severity :3:=Error :4:=Warning :5:=Notice :7:=Debug (never in prod).
• Error prefix: 01=TMM, 07=MCP, 0c=SOD, 26=SSL.
• HSL pipeline: destination → publisher → filter/profile.
• tcpdump --f5 ssl provider for modern TLS decryption (not ssldump).
• show sys performance all-stats = best single troubleshooting command.
Notes: WHAT THIS SLIDE TEACHES
Key facts organized into four categories. Every item on this slide has appeared in exam questions. Students should review this slide the night before each exam.

## Slide 124
Good luck on your exams.
F5-CTS BIG-IP LTM Beta Certification Series
F5CTSLTM1-B through F5CTSLTM6-B
Resources:
• my.f5.com — F5 Knowledge Base (K articles)
• techdocs.f5.com — Official documentation
• devcentral.f5.com — Community, iRules, code samples
• clouddocs.f5.com — AS3, FAST, automation
• AskF5 (my.f5.com) — Search for K article numbers cited throughout this course
Notes: WHAT THIS SLIDE TEACHES
Course closing. Resource links for continued study.